## Slide 1: General Accelerator Development B&R KA-15-02-011 A LABORATORY-UNIVERSITY COLLABORATION TO UNDERSTAND PERFORMANCE LIMITS OF SRF CAVITIES (DE-PS02-09ER09-05) and EQUIPMENT (INTEGRATED CAVITY PROCESSING APPARATUS AND CAVITY TUNING MACHINE)
Lance Cooley
Technical Division
SRF Materials Group Head

## Slide 2: Laboratory – University Collaboration
Coordinated program to understand what limits performance in SRF cavities
  First area of focus: weld pits
$0.5 M / year x 3 years
FNAL, Florida State, IIT, UChicago, Northwestern
  Leveraged ILC support for UIC
FY10 money arrived 9/1/09, FY11 money arrived Jan 2010, $200k arrived 7/1/2010 (1.2 M total of 1.5 M already here)
MOUs with universities completed Jan. 2010, funds transmitted to universities Feb. 2010 per SOWs
FY11 SOWs in preparation now

## Slide 3: SRF University Collaboration meeting 13 August 2010
Fermilab
Lance Cooley* (PI)
Alex Romanenko* (Peoples Fellow)
John Zweibohmer* (budget)
Allan Rowe*
Dmitri Sergatskov*
Donna Hicks*
Denise Ford (NWU Ph.D student)
Genfa Wu*
Mingqi Ge*
Charlie Cooper*
UIC
Robert Klie (PI)
Runzhe Tao
* Supported at FNAL by this B&R
IIT
John Zasadzinski (PI)
Sandra Bishnoi (Chem. Faculty)
Brian Albee
Chaoyue Cao
Northwestern
David Seidman (PI)
Yoon Jun Kim
U Chicago
Steve Sibener (PI)
Jim Becker
Miki Nakayama (absent)
Florida State
David Larbalestier (PI)
Peter Lee (PI)
Zu-Hawn Sung
Tolya Polyanskii
Bill Starch

## Slide 4: Milestones FY2010
Organized SRF Materials Workshop – Feb 2010 Tallahassee
Coupon work investigated how and why of pitting
  Invited presentation at ASC2010
  New recommendations for cavities:
    Anneal prior to EP and perhaps prior to welding
    Keep improving temperature control in EP

## Slide 5: Milestones FY10
Point-contact tunneling combined with Raman spectroscopy showed dramatic role of defective Nb-oxide at hot-spots
  Proslier and Ciovati, submitted to PR-STAB 2010
FSU – Zu-Hawn Sung Ph.D.: Grain boundaries in Nb admit flux and permit dissipation
Clear Raman signature for oxidized spot

## Slide 6: Anticipated Milestones FY2011
Accumulated surface science of pits will connect dots
  Cavity cut-outs added to coupons
  Cold work and/or excessive oxidation during EP Þ pits with defected oxide Þ cavity hot spots
  FSU explore, dual FIB to cut out, IIT to probe
Oxidation vs. surface orientation
  UChicago high quality Nb crystals
  UIC detailed electron microscopy – what are the defects?
Cottrell atmospheres (binding of H to Nb-vac)
  Hydrogen affects mobility of vacancies, dislocations
    Dislocations = oxygen elevators?
    Peoples Fellow Romanenko + Northwestern

## Slide 7: Equipment – Integrated Cavity Proc. Apparatus
Scope: 1-cell processing R&D (acid, rinse, assemble)
Scale infrastructure for 9-cell
System | FY 2008 |  |  |  |  | FY2009 |  |  |  |  |  | FY2010 |  |  |  |  | FY2011 |  |  |  |  | 
 | Q1 | Q2 | Q3 |  | Q4 | Q1 | Q2 |  | Q3 | Q4 |  | Q1 | Q2 |  | Q3 | Q4 | Q1 |  | Q2 | Q3 |  | Q4
Clean Room |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
UP Water |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
HPR tool |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Acid work infra |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
EP tool |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
EP controls |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Design
Permit
Procure
Constr.
/ Assy.
ORC
Operation
Doc &
Review
Draft /
Specify

## Slide 8: Equipment – ICPA – HPR and Clean Room
1-cell initial R&D, 9-cell infrastructure capacity
Successful completion of Class 10 clean room, dessicator, ultrapure water plant, high-pressure pump, HPR tool, controls.
Now in ORC trials
FNAL designed and specified entire layout, and built all systems except clean room, dessicator, and UPW plant
Clean rinse and assembly capability improves on FNAL/ANL and JLab features
HPR control
Clean room
HPR pump
HPR
Tool
UPW Plant

## Slide 9: Equipment – ICPA – Chemistry Area
1-cell initial R&D, 9-cell infrastructure capacity
Successful completion of all acid handling, storage, vapor scrubbing, and safety equipment
Permitting complete
FNAL designed and specified entire layout, and served as lead contractor
EP tool, acid transport, and control system designed and custom built by FNAL, in assembly stage now.
EP Cabinet and
Tool frame
Scrubber
Neutralizer
EP Control

## Slide 10: ICPA – What’s next
ORC
  Engineering triggers, Procedures
  Formal review by oversight committee
Operations
  Staffing
  Support of clean room: gowning, hardware, tools, vacuum pump cart, wash down
  Support of lab space: chemical PPE, furniture, access controls
  Support of cavity work: cavities, carts, fixtures
  Consumables: acids, filters, buffers
  Maintenance: UPW service, scrubber service
Upgrades
  9-cell ultrasonic cleaner, BCP / VEP cabinet

## Slide 11: Equipment - Automatic Cavity Tuning Machines
Successful international collaboration effort by FNAL, DESY, and KEK
Four machines designed, fabricated, commissioned, and delivered to their respective institutions:
  Two for DESY, one for FNAL, one for KEK
Critical equipment for SCRF cavity industrialization and high volume production
  Allows a non RF-expert operator to tune and align a 9-cell 1.3 GHz cavity in less than 4 hours
  Both DESY machines to be used by European industry for XFEL cavity fabrication
Some members of the FNAL, DESY, and KEK collaboration during machine commissioning at FNAL
One of the two DESY machines after commissioning at DESY

## Slide 12: Tuning Machines – FNAL Deliverables
Control Software: Combination of Labview, Matlab, and Phytron scripts. Designed for automation, includes embedded electrical and mechanical models

## Slide 13: Tuning Machines – FNAL Deliverables
Control Electronics: one control rack per machine with several custom-made electronic boxes and printed circuit boards

## Slide 14: Tuning Machines - Next
Design and Fabricate a tuning machine for 650 MHz cavities?
  Mostly mechanical changes for the tuning jaws, tuning frame, and eccentricity measurement device
Tuning Jaws (x3)
Eccentricity Measurement Sensors (x11)