## Slide 1: Welcome/Opening Remarks
Andy Hocker
FNAL
US Hydroforming Workshop
1-SEP-2010

## Slide 2: Why hydroforming?
Cavities almost always fail near the equator welds
  Magnetic field is highest at the equator
  Equator is subject to the abuse of electron beam welding
    Pits, spatter, degraded RRR in HAZ…
EBW is expensive and tricky
For weld-free cavities, hydroforming holds good deal of promise
  Proof of principle established by Singer et al. at DESY
  First(!) hydroformed 9-cell (3x3) cavity reached ~30 MV/m
    Reminder: ILC goal = 35 MV/m (31.5 MV/m operating point)
  Everyone wants to see this evolve beyond R&D
Based on this, ILC ART has agreed to fund hydroforming efforts in FY11

## Slide 3: What remains to be done?
No one has ever hydroformed a full 9-cell Nb cavity
  DESY does 3 x 3-cells, limited by the size of their equipment
    Should be scalable
No one has attempted a “production run”
  Accumulate performance statistics (what’s the yield?)
  Realistic assessment of fabrication cost
No one has optimized the recipe
  Cost, reproducibility, simplicity, etc.
  What is the best line of attack in these areas?

## Slide 4: Our Task
Primary goal: Hydroform a 9-cell Nb cavity, then several
  Make use of previous efforts!
    DESY has developed a procedure that works
    Black Labs/ATI-WC has developed a tube of appropriate dimensions/characteristics
  Critical path: set up a pilot facility for hydroforming cavities
    Establish a production workflow
  Establish a baseline for improvements
  This should be a 1-2 year project
Secondary goal: Refine/optimize process
  Example: better/simpler/cheaper tubes
    Understanding of microstructural issues
  Longer-term projects… leverage SBIR program

## Slide 5: Outcome(s) of this workshop
Everyone becomes aware of the interested parties and their capabilities
  Especially identify areas of possible collaboration or coordination
We identify possible paths to achieving the primary and secondary goals
Perhaps even reach a consensus about the best path forward

## Slide 6: How today should work
We have two “sessions:” one on Nb tube and one on the creation of hydroforming facilities
First we hear presentations on what’s currently happening in these areas
Then we have an informed discussion, keeping in mind our primary goal
  What do we need to push the hardest?
  Are there important issues left uncovered? Who can tackle them?
  Where do we need to put resources?
After the workshop
  Results of our discussions get written up
  FNAL starts requesting formal proposals