## Slide 1: Considerations for FET-based Broadband Chopper Modulator
Craig Burkhart & Tao Tang April 13, 2011

## Slide 2: Modulator Parameters
162.5 RFQ frequency
  6.15 ns bunch spacing
  Maximum kicker pulse: ~12 ns
  Maximum kicker PRF: ~80 MHz?
5 mrad deflection
  Four, 0.5 m lattice locations at 180o separation
  Kicker length: 30 cm?
  Kicker aperture?
  Kicker efficiency (effective electric field on beam): 0.7 to 1
Allowable perturbation to transported beam
  Transverse energy
  Transverse energy jitter
Better definition in Functional Specifications Requirements

## Slide 3: Hybrid Switch Module (HSM)
Hybrid FET/driver
Developed for ILC DR
Ultra-fast switching
  Turn on ~1 ns
  Turn off α RCOSS
Select FET for load
  1.2 kV max
  35 A max
Limitations
  Stability, pseudo linear regime
  Average power

## Slide 4: Ultra-fast Adder
Inductively combines HSMs in series
HSMs ground referenced, simplifies
  Isolation
  Charging
  Triggering
Minimal degradation of HSM waveforms

## Slide 5: HSM Stability
MOSFET junction is not fully saturated with carriers for several ns
Switching is in semi-linear mode
Variations in Gm will effect switching behavior
Many factors influence gain
  Die temperature, and hence kick pattern
  Manufacturing variations
Stability ~10% for broadband application

## Slide 6: HSM Dissipation
Dominated by switching losses at high PRF
Switching loss is primarily dissipation of energy stored in device output capacitance
  P = 0.5 COSS V2
Power hybrids are typically capable of dissipating 0.1 to 1 kW, but 2nd generation HSM must be fabricated and tested to determine capability

## Slide 7: MOSFET Output Capacitance
Output capacitance is voltage dependent
Output capacitance is device dependent
  Increases with FET ampacity (for a given VDSS )
  Increases with FET voltage (for a given IDS )
  Examples
    APT1201R4
      1200 V, 36 A, 310 pF (~150 pF effective)
      P = (0.5) (150 pF) (1 kV)2 (80 MHz) = 6 kW
    IRF630N
      200 V, 37 A, 89 pF (~47 pF effective)
      P = (0.5) (47 pF) (0.18 kV)2 (80 MHz) = 61 W

## Slide 8: Output Capacitance Dependencies

## Slide 9: Broadband Kicker Modulator Topologies
Traveling wave structures are resistive load
  HSM turn on is fine
  HSM turn off
    RC ≈ (0.1 nF) (50 Ω) = 5 ns, too long
    Consider line-type modulator, switch is only closing
Distributed electrode structures are capacitive
  Need totem pole driver to discharge
  Switches charge COSS of other

## Slide 10: “Classic” Line-type Modulator
Pulse length: 2X propagation time of T1
Rise/fall time
  Characteristic of M1, ~1 ns
Chopper voltage: HV/2

## Slide 11: Possible Traveling Wave Alternative
Kicker normally “on”, HSM shunts voltage
Chopper voltage: HV
Increased kicker load power
HSM sets fall time, HV impedance sets RC

## Slide 12: Totem Pole for Distributed Electrodes
Upper switch charges
Lower switch discharges
Switch load: Cload + COSS

## Slide 13: Benefit of Series Totem Pole
Switch load: Cload + COSS /2
Series can be achieved using adder topology

## Slide 14: Conclusions
Requirements require better definition
Hybrid MOSFET/driver has sufficient switching speed for broadband application
Thermal capacity of 2nd generation HSM must be evaluated
Switching losses must be minimized
  Investigate approaches to reduce effective FET output capacitance
  Alternative topologies