## Slide 1: Revival of the cern ps neutrino beam
Rende Steerenberg,
CERN Switzerland
Short-Baseline Neutrino Workshop
12 - 14 May 2011, Fermilab – Batavia, IL - USA

## Slide 2: Acknowledgements:
Thanks to:
Jan Borburgh, Marco Calviani, Tobias Dobers, Ilias Efthymiopoulos, Alfredo Ferrari, Massimo Giovannozzi, Edda Gschwendtner, Alberto Guglielmi, Dominique Missiaen, David Nisbet, Ans Pardons, Francesco Pietropaolo, Youri Robert, Paola Sala, Bernard Vandorpe, Heinz Vincke, Samuel Zeler,
for fruitful discussions and work done so far.
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 3: Contents
Why Another Neutrino Facility
PS Proton Beam Production Scheme
The Infrastructure
Target System and Decay Tube
Present status
Concluding Remarks
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 4: Contents
Why Another Neutrino Facility
PS Proton Beam Production Scheme
The Infrastructure
Target System and Decay Tube
Present status
Concluding Remarks
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 5: Why a New Neutrino Facility ?
The idea for reviving the CERN PS neutrino beam line was triggered by a letter of intent from an experimental collaboration led by C. Rubbia for the search of sterile neutrinos
A more concrete experimental proposal is being considered
  See talk of F. Pietropaolo Saturday morning 8:00
However, the facility can also be used for other experiments/studies:
  Neutrino cross section measurements at very low energies (on and/or off-axis)
  Target R&D
  Detector studies, etc......
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 6: The Proposed Lay-out
Re-use the old TT7 tunnel and cavern to house primary beam line and target station
Proton beam to be provide by CERN PS
150t liquid argon TPC near detector in building 181
600t liquid argon TPC far detector in building 191
Near detector
Far detector
T600
ICARUS
detectors
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 7: Experimental Requirements
Request: 2.5x1020 protons over 2 years
  Based on neutrino production yield of 1980’s
Proton beam momentum ~ 20 GeV/c
  Secondary νμ and νμ beam with Eν ≤ 2 GeV
The challenge lies in:
  producing this extra amount of protons from the CERN PS
  designing the optimum and reliable target and focussing system
  Respect radiation limits for this surface facility
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 8: Contents
Why Another Neutrino Facility
PS Proton Beam Production Scheme
The Infrastructure
Target System and Decay Tube
Present status
Concluding Remarks
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 9: The actual CERN Accelerator Complex
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 10: The Accelerator Complex with PSNF
PSNF
REVIVAL OF THE CERN PS NEUTRINO BEAM
Beam delivery by partial time sharing

## Slide 11: Beam Scheduling
Super Cycle outside LHC filling periods (39.6 sec):
  SPS provides beam to Fixed target physics, CNGS and LHC
  PS provides beam to the SPS, East Area, AD, nTOF
  PSB provides beam to PS and ISOLDE
PS
SPS
Leaving 12 pulses out of 33 possible (36% duty cycle) for the ISOLDE experiment behind the PS booster. They request actually~ 50%
Fixed target
physics
CNGS
CNGS
CNGS
CNGS
No place for more cycles in the super cycle left to produce the required extra protons
DIRAC
EA
DIRAC
DIRAC
DIRAC
DIRAC
EA
EA
EA
nTOF
nTOF
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 12: How to Produce the Extra Protons
PS produces beam for other users while SPS is accelerating and extracting
  No direct competition for protons from PS and SPS
The DIRAC experiment in the East Experimental Area has mentioned plans to move to the SPS, freeing 5 cycles
However, the nTOF facility requests extra cycles, leaving again little possibilities
Only possibility left :
    Make even more efficient use of the PS
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 13: Beam Sharing
On the nTOF cycle only 1 bunch is produced, while 8 can be produced.
The nTOF cycle can routinely produce 3x1013 protons in 8 bunches:
  7 bunches for the PSNF (2.6x1013)
  1 bunch for the nTOF facility (3.8x1012)
Putting in total 7 of these cycles in the super cycle:
  PS can produce ~ 6.7x1019 protons per typical run of 180 days
  PS would need 3 to 4 runs (years) to accumulate 2.5x1020 protons, instead of the requested 2 years.
  Run time can be shortened by extending the years PS run with dedicated PSNF running
More efficient use of the CERN PS and no loss of integrated protons for nTOF (slight increase)
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 14: PS to TT7 Transfer Line
About 150 m of transfer line to be build
No real design made yet
Magnet needs for beam transfer line:
  ~ 16 Main Dipoles
  ~ 14 Quadrupoles
  ~ 6 Corrector Dipoles
  Fast switching magnet (~ 200 ms) for sharing
Beam instrumentation:
  Beam current transformer
  Beam positioning monitors
  Beam profile measurement
  Beam loss monitors
Primary beam collimator
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 15: Contents
Why Another Neutrino Facility
PS Proton Beam Production Scheme
The Infrastructure
Target System and Decay Tube
Present status
Concluding Remarks
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 16: Re-use existing infrastructure
In the 80’s the PS also provided protons beam to a target for neutrino physics:
  CDHS
  CHARM
  BEBC experiment
The infra-structure is presently not use and could after thorough consolidation be re-used to house:
  Primary proton transfer line
  Target and focusing
  Decay channel
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 17: The TT7 Tunnel
The TT7 tunnel:
Jura
Geneva
Geneva
Jura
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 18: The TT7 tunnel towards the target
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 19: The TT7 Target Cavern
TT7 cavern shaft
TT7 cavern
TT7 cavern
TT7 emergency exit
TT7 cable & ventilation
shaft
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 20: Beam Dump / Hadron Absorber
4 meter thick beam dump (none sealed iron blocks)
~ 65 meter of earth
No cooling
To be reviewed !
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 21: Contents
Why Another Neutrino Facility
PS Proton Beam Production Scheme
The Infrastructure
Target System and Decay Tube/Tunnel
Present status
Concluding Remarks
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 22: Preliminary Target & Focusing Ideas
The design has not started, but some ideas are being discussed.
  Target (partly) inside single horn (Eν ≤ 2 GeV)
  Beam synchronous pulsed horn
  Type of target material to be used
Graphite target rod of <6 mm radius is being considered
Interaction length is ~ 40 cm therefore an ~80 cm long target would be needed
For a 20 GeV/c beam with 4x1013 ppp at a 1.2 second repetition rate ~ 1.3 kW is deposited in target
Simulations have started
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 23: Primary Beam Parameters
REVIVAL OF THE CERN PS NEUTRINO BEAM
 | Old neutrino facility |  | New neutrino facility |  | 
 | PS dedicated Feb-Mar 1983 | PS parallel 1983 - 1984 | PS dedicated | PS parasitic | PS ultimate[1]
Proton Momentum | 19.2 GeV/c | 19.2 GeV/c | 20 GeV/c | 20 GeV/c | 26 GeV/c
Protons/pulse | 1.25x1013 | 1.2x1013 | 3x1013 | 2.6x1013 | 4x1013
Max. rep. rate | 1.2 s | 14.4 s | 1.2 s | 1.2 s | 1.2 s
Beam energy | 38 kJ | 38 kJ | 96 kJ | 84 kJ | 166 kJ
Average beam power | 32 kW | 2.5 kW | 80 kW | 70 kW | 140 kW
[1] The PS ultimate beam is presently not possible, but could perhaps be in reach after the completions of the LHC Injector Upgrade (LIU) project.
Running with 7 cycles in the previously mentioned super cycle with PS parasitic beam
  Corresponds to 21% duty cycle and 15 kW beam power
To complete experiment dedicated running during short periods at 80% - 100% duty cycle (80 kW) is needed

## Slide 24: Decay Tunnel
The available decay tunnel is 50 meters long
Cross section:
  3.5 x 2.8 m2 for the 1st 25 m
  5.0 x 2.8 m2 for the remainder
No vacuum or helium filled decay tube available to be considered
Consider also muon detectors for beam steering and target/horn alignment
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 25: Contents
Why Another Neutrino Facility
PS Proton Beam Production Scheme
The Infrastructure
Target System and Decay Tube/Tunnel
Present status
Concluding Remarks
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 26: Present Status
A partial feasibility study, addressing the most critical issues, was made and result have been reported to the CERN management
A memorandum with the experimental proposal, prepared by C. Rubbia et al, was discussed in the CERN SPSC in April
CERN is now considering some form of a conceptual design study
  The existing very rough cost estimate is not representative and should not be used
  A realistic cost estimate and project planning should be made instead
A decision is expected after the Research Board of June 8th
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 27: Contents
Why Another Neutrino Facility
PS Proton Beam Production Scheme
The Infrastructure
Target System and Decay Tube/Tunnel
Present status
Concluding Remarks
REVIVAL OF THE CERN PS NEUTRINO BEAM

## Slide 28: Concluding Remarks
A very exciting physics experiment is proposed for the more than 50 years old CERN PS
  More news awaited after the CERN Research Board meeting of 8 June
TT7 and nTOF beam sharing makes efficient use of the CERN PS:
  The proposed experiment could be completed in 3 to 4 runs without forming any competition for protons with other experiments
  Shortening possible by dedicated running
  nTOF would gain also on the number of integrated protons
No direct competition for protons between PS and SPS neutrino facilities
Large part of the required infrastructure is available, but needs to be consolidated
Everything else needs to be designed and constructed
The facility can also be (re-)used for other low energy neutrino physics, target R&D, Detector R&D, etc...
REVIVAL OF THE CERN PS NEUTRINO BEAM