## Slide 1: Kicker R&D for a Broadband Chopper
Greg Saewert
Manfred Wendt

## Slide 2: 2.5 MeV, 162.5 MHz Beam Structure
σz = 3.5 mm, σt = 160 psec ??!!
vbeam = 21.84 mm/nsec
tbunch-to-bunch = 6.15 nsec
zbunch-to-bunch = 134.3 mm

## Slide 3: Broadband Chopper
Broadband chopper:
  Travelling wave structure vE-field = vbeam
  High Etr-field, ideal: 3.0 nsec rectangular pulse
  Kick angle = ≈
  Basically only the E-field is used for the beam kick
Etr ℓki
E0 γ β2
Etr ℓki
5 MV
vbeam = 21.84 mm/nsec
vE-field = 21.84 mm/nsec
134.3 mm
25…100 mm

## Slide 4: Chopper Technologies
Travelling wave chopper
Lumped element chopper
Pulse Delay Network
Requires only one, but high-power pulser
Meander, helical or similar transmission-line
Pulse shape degradation
  Long transmission-line with dispersion effects
  Reflection effects for some structures, e.g. meander
Only a small part of the travelling field energy is used to kick the beam
Requires many low-power pulsers
  Low cost homebrew (SLAC)
  Driver output-stage physically close to high-impedance electrode
Digital delay driver network
Short lumped, capacitive electrodes
  dimensions << wavelength
  control of parasitic elements

## Slide 5: Helical R&D, prototype #3
characteristic impedance | 200 Ω
brass conductors dimensions | 0.09 x 0.02 inches (w x t)
pitch | 0.336 inches
outer diameter | 1.46 inches
ground tube diameter | 0.875 inches
ceramic spacer rods diameter | 3/16 inches
total length | 6 inches
Low signal degradation suggests a bandwidth of ~1.8 GHz(!)
Courtesy G. Saewert

## Slide 6: Lumped Element R&D
Copper electrodes
  ~11 x 12 mm
  ~3.5 pF
15 mm pitch
Ceramtec feedtrough
~15 mm aperture
+/- 500 V differential supply
Very preliminary!!!

## Slide 7: Electrostatic Results
E-field >45 kV/m (@ +/- 500 V)
  for ~20 mm range
  varies 45…58 kV/m
kicker parameters
  effective length: 500 mm
  kick angle: 4.5 mrad

## Slide 8: Dynamics Results
simulation bandwidth: 15 GHz
simulation bandwidth: 5 GHz

## Slide 9: Next Steps
Modify lumped element structure
  Electrodes can be made longer, ~25…35 mm
  Expect 6…8 pF capacitance
Extract lumped element equivalent LC network (S11)
  Driver output load, for SPICE network simulation
More dynamics simulations
  Realistic drive signal
  Realistic frequency limit (a few GHz) for the simulation