## Slide 1
IOTA run 2 NIO implementation and first results
Nikita Kuklev and IOTA NL team
IOTA collaboration meeting
June 15, 2020

## Slide 2: Outline
Previous results and run 2 goals
Run 2 configuration
Run 2 commissioning
Data collection
Simulations
Analysis

## Slide 3: Run 1 – partial success
Reminder: QI =
In run 1, measured significant tune spread, ~0.6x of simulated performance
Did not get invariants to sufficient accuracy
Limitations:
  Insufficient BPM resolution
  Bent pipe aperture restriction
  Only V-kicker control
Run 1 FMA

## Slide 4: Run 2 plans
Improve and fix HW/SW
3 experimental phases
  Stage 1
    Commission, measure nominal configuration
    Demonstrate predicted performance
  Stage 2
    Perturbed systems (tune/dispersion/field errors/etc.)
    Demonstrate resiliency to errors
  Stage 3
    Different working points, close to resonances, etc.
    Explore exotic conditions
Uses same base, nominal lattice
Needs new lattice design/tuning

## Slide 5: Outline
Previous results and run 2 goals
Run 2 configuration
Run 2 commissioning
Data collection
Simulations
Analysis

## Slide 6: Main upgrades
Added flux compensators to change dipole edge field
  Improved path length discrepancy
Added 4 sextupoles (2 families)
Added tunable H-kicker
BPM hardware improvements
SW/timing improvements

## Slide 7: Remaining issues
Significant optics breathing
Operational issues – drifts, trips, etc. (minor)

## Slide 8: Remaining issues
Significant optics breathing
Operational issues – drifts, trips, etc. (minor)

## Slide 9: Outline
Previous results and run 2 goals
Run 2 configuration
Run 2 commissioning
Data collection
Simulations
Analysis

## Slide 10: Commissioning
4 main categories:
  Lattice
  Knobs/kickers/etc.
  BPMs
  Insert
Lattice: LOCO provided best precision
  β within a few %, but drift + hysteresis problematic
  Verified with TBT data from each sequence
Kickers: analyzed repeated triggers
  Jitter - <5% rms
  Linearity within 5-8%

## Slide 11: Commissioning
Lattice: Unknown reduction in x chromaticity
  Suspect due to dipole effects
  Means sextupole strength required for (x,y)=(0,0) < model
Too low
Good

## Slide 12: Commissioning – BPMs
Orbit linearity and noise:
  <1% linear within 4 mm of center
  ~1um @ 0.3mA
TBT noise:
  100um @ 0.8mA
  Meets specs!
Overall, improved significantly from run 1
A few issues remained:
  Dynamic saturation
  Timing/ADC desync
  Errors/timeouts
Position rms vs current (and RF=bunch length)
Kick amplitude vs current

## Slide 13: Commissioning – QI
Insert was taken apart and each magnet tested at TD (rotating coil)
  Rebuilt with best ones in the middle
Alignment done with precision mechanical rod and laser
  Both indicated < 150um mechanical
Testing @ TD VTS
Final assembly
Precision soviet stick alignment

## Slide 14: Commissioning – QI
Laser tracker aligned into the ring
Manual edge checks
Measured tracker model

## Slide 15: Commissioning – QI
Alignment tested with close orbit responses
Found very large displacements in some magnets
  Some not physical (almost 1 mm)!
Closed orbit distortion model/measurement
Magnet offsets (A. Romanov)

## Slide 16: Commissioning – QI
Tried to slide around, demagnetize, test inductance
Realigned in place with laser and left as is
Root cause still unclear
Laser inserted using 3d-printed holder
Sanity checking/moving with indicators

## Slide 17: Commissioning summary
Goal for run 2: achieve beam parameters, machine tuning and system performance necessary for the NIO experiments
Octupoles: 10% beta-function accuracy, ~0.01 betatron phase accuracy, 100um orbit centering
NL magnet: 1% beta-function, 0.001-0.003 betatron phase, 50um orbit centering
Variable single-turn kick, H/V
Turn-by-turn BPM system, 100um resolution

## Slide 18: Outline
Previous results and run 2 goals
Run 2 configuration
Run 2 commissioning
Data collection
Simulations
Analysis

## Slide 19: Data channels
Nominally, 21 BPMs – 19 useful
  -1 special pickup, different size/calibration
  -1 for anti-damper
Data:
  8k turns, triggered at -172 from kick (‘pilot’ signal)
  Ring state afterwards saved
    284 channels – magnets, beam currents, etc.
  Other data available via ACNET

## Slide 20: Collection
Typical sequence:
  58 nonlinear kicks (2/point)
    In 3 lines, slightly nonlinear spacing
  ~5-10 calibration kicks (insert off)
    At start/end + after reinjection – used for optics recovery
  Automated collection/injection
    Current > 0.8mA
    With pyIOTA: github.com/nikitakuklev/pyIOTA “unified modelling/control environment”
This grid was repeated for many configurations
  Nominal
  Tune/dispersion/etc. errors
  QI/NL current errors
Kick
Inject
Bad inject (retry)
Low current dump
Kick to kick period ~50s, no operator input
Lattice switch

## Slide 21: Dataset breakdown
Two main collection periods
  ‘doomsday’: March 15/16 + ‘actual doomsday’: March 20/21
In total:
  QI: 2600 kicks / 37 configs
  NL: 1100 kicks / 36 configs
  ~1000 on blank lattice for various calibrations
  Around 1-2k other kicks for various studies (RDTs, …)
Stage 1+2 – data mostly collected
Stage 3 was not completed due to covid-19 lab shutdown

## Slide 22: Outlier rejection
Observed a variety of anomalies
  Example: timing/ADC desync
Solution – veto voting by filters + manual curation
  Absolute value threshold
  SNR/symmetry
  Mean/variance outliers

## Slide 23: Sample dataset
Example of data remaining after cleaning

## Slide 24: Sample dataset
Example of single kick data

## Slide 25: Outline
Previous results and run 2 goals
Run 2 configuration
Run 2 commissioning
Data collection
Simulations
Analysis

## Slide 26: Simulations
Heavy simulations with elegant, via pyIOTA wrapper
  Thick symplectic tracking - fringe fields + errors + SR
(Non)linear optics - OCELOT + MADX + custom code

## Slide 27: Simulation predictions
Updated simulations to latest v8.6 lattice run 2 config
Predicted strong impact of chromaticity
  Need to reduce chroma to get more turns (more data)
  But only have 2 families / 4 sextupoles (not properly π-phased) out of 12 possible
  Nonlinearities hurt dynamics
Sextupoles only
Sextupoles + octupoles
Color scale – diffusion (how chaotic)

## Slide 28: Simulation predictions
Of interest to measure in 3 lines, 1 per sector
Vertical
Horizontal
Observable limit
Diagonal

## Slide 29: Outline
Previous results and run 2 goals
Run 2 configuration
Run 2 commissioning
Data collection
Simulations
Analysis

## Slide 30: Analysis methods
Methods (briefly)
  Preprocessing
    SVD cleaning, ROI cut based on SNR
  Tunes
    Modified adaptive NAFF
  Linear optics
    Model-independent methods
  Phase space
    SVD/ICA decomposition
    Envelope function – chromatic + octupolar decoherence fit with annealing/bin hopping
    Parameter optimization for smallest invariant jitter

## Slide 31: Results – stage 1
Nominal config – 1.0A QI (central octupole)
  No time for aperture scans – estimate from BPM sum
  Good match with FMA simulations
  Similar results at 0.75A/1.25A
Note discrepancy
Ideal lattice FMA + QI data

## Slide 32: Results – stage 1
Nominal config – 1.0A QI (central octupole)
  Discrepancy in H/V due to different (sextupolar) detuning – result of mystery chromaticity
ξ=0 matches H branch
ξ=-2 matches V branch

## Slide 33: Results – stage 1
Comparison with 0.25A flat distribution (‘conventional octupole’)
  Has ~ same detuning strength
  But loses more beam at same amplitude
  Weird resonant excitations overwhelm signal
Signal spectrogram
Ideal lattice FMA + flat data

## Slide 34: Results – stage 1
Looking at invariants
  Analysis ongoing – signal zoo, a lot of manual tweaking, complicated coupling
  Preliminary data using SVD modes
  Can’t compare to simulations quantitatively yet (beam size matters, need good bunch estimate)
CS linear part
QI
Normalized phase space after decoherence compensation
Strength parameter
Diagonal kick data

## Slide 35: Results – stage 1
Looking at invariants
  Flat configuration H-invariant jitter worse while CS invariants ~ same
  Simulation work in progress to verify results and estimate sensitivity
1.0A nominal
0.25A flat
Signal too low
I1
I1
<
=
=

## Slide 36: Results – stage 2
Available perturbations - a mixed bag, sparse sampling
  Δν inside insert
  Δν ring (outside insert)
  β*
  Insert currents (i.e. ν=5.31 curve)
  Dx

## Slide 37: Results – stage 2
Example: tune inside insert
  Small shifts – little impact
  Large shifts – different behavior, DA reduction, signal anomalies – need stage 3
Qx+0.003 shift
Qx+0.01 shift

## Slide 38: Conclusion
Run 2 has produced significant improvements in data quality
We demonstrated performance consistent with simulations
  High tune spread
  Invariant conservation
  Superior performance vs flat arrangement
  Stage 2 perturbation analysis ongoing
Further required work
  Characterization of ring nonlinearities
  Resolving misalignment mysteries
  Hardware - optics fluctuations fix + full 12 sextupoles (major DA boost!)

## Slide 39: Thanks! Questions?