## Slide 1: 3D Magnet Simulations for SNS Bean Transport Lines
J. G. Wang
SNS/ORNL
In 4th Special Workshop on Magnet Simulations for Particle Accelerators
March 28-April 1, 2011, in PAC11,
New York, NY.

## Slide 2: Topics of Presentation
Effect of magnetic fringe fields and interference on beam matching in a Medium Energy Beam Transport (MEBT) line of SNS linear accelerator.
Tracking stripped proton particles in SNS ring injection momentum dump line.
(see poster WEP039)

## Slide 3: SNS MEBT line (Courtesy of LBNL design documents)
MEBT32: iron length: 4.5 cm, aperture: 3.2 cm;
MEBT42: 4.5 cm, 4.2 cm.

## Slide 4: SNS MEBT lattice
Effective length of MEBT quads: 6.1 and 6.6 cm for MEBT32 and MEBT42

## Slide 5: MEBT42 simulation models
A single MEBT42
for fringe field study
Two MEBT42s
for interference study
(10 cm apart)

## Slide 6: Field distributions of MEBT42 quads
A single MEBT42
Two MEBT42s
3D multipole expansion yields:
Linear quadrupole term;
Pseudo-octupole term;
Dodecapole term;
….
A single MEBT42

## Slide 7: Linear Particle Optics of MEBT42
 | Focus | Defocus
dM11 | 18.49% | 0.64%
dM21 | -1.71% | 1.63%
dM12 | 1.56% | 0.05%
dM22 | 18.49% | 0.64%
Transfer matrices of
a single MEBT42
(z from -0.2 to 0.2 m)
Transfer matrices of
two MEBT42s in interference
(z from -0.2 to 0.2 m)
Relative differences between linear optics and design hard edge models
 | Focus | Defocus
dM11 | 22.39% | 0.35%
dM21 | -2.18% | 0.64%
dM12 | 1.96% | -0.19%
dM22 | 29.62% | -0.01%

## Slide 8: Hard edge models for a single MEBT42 quad

## Slide 9: 3D simulation models of half MEBT line
Q1
Q2
Q3
Q4
Q5
Q6
Q7
MEBT32 Assembly
MEBT42 Assembly

## Slide 10: Hard edge models from design and linear optics

## Slide 11: Principle rays in first half MEBT lattice from linear particle optics and design hard-edge models
M12(z) and M22(z) for the x-motion from two different models
M21(z) and M22(z) for the y-motion from two different models
At z=1.64 m (MEBT lattice center): The relative difference in M12 is 41%, while M22 has opposite signs
At z=1.64 m (MEBT lattice center): The relative difference in M21and M22 is 84% and 704%, respectively.

## Slide 12: Beam envelope in first half MEBT lattice from linear particle optics and design hard-edge models
Beam envelope amplitude from two different models
Beam envelope slope from two different models
At z=1.64 m (MEBT lattice center): The envelope amplitudes are fairly close from two difference models
At z=1.64 m (MEBT lattice center): The relative difference in Xm’ is 50%, while Ym’ has opposite signs.

## Slide 13: The z-dependent transfer functions for matching
Definition:
The linear focusing function per unit current.
Generation:
- Through 3D magnet modeling and multipole expansion;
- The shape remains and the amplitude changes linearly with current;
- There are 11 independent functions for 14 MEBT quads.
Linear Superimposition:
Correction for magnet core saturation:
Can be made if the saturation properties are known from measurements or simulations

## Slide 14: Linear focusing function of first half MEBT lattice from 3D models and superposition

## Slide 15: A full 3D beam dynamic model with space charge (T. P. Wangler, RF Linear Accelerators)
K3=1.512*10-8 m is a 3D space-charge parameter for a 38 mA H- beam;
Where kx(z) = k(z)-kc(i) and ky(z) = k(z)+kc(i)
kc(i) is transverse defocusing constant of the 4 cavities (i=1,2,3,4);
kz(z)= kz(i) is longitudinal focusing constant of the cavities;
is an ellipsoid form factor.

## Slide 16: A 38 mA H beam envelopes matched with the superimposed transfer functions

## Slide 17: Conclusions:
Conventional hard-edge models for quads with large apertures and densely installed are incorrect.
Correct hard-edge models based on linear particle optics can be obtained through 3D magnet modeling and 3D multipole expansion.
For beam matching, smooth, overlapped, z-dependent transfer functions should be generated and employed.
3D magnet simulations are the only way to accomplish these tasks; Though magnet measurements are important for checking simulation accuracy, the existing techniques can not produce desired data for these applications.

## Slide 18: SNS ring injection momentum collimation (courtesy of P. He et al of BNL)

## Slide 19: 3D simulation model of momentum dump line
H- particle for injection;
DH14 bending angle: 11.25o
Dump window
Scraped proton particles

## Slide 20: Reference trajectory for stripped proton beams

## Slide 21: 3D multipole expansion about reference trajectory
Quadrupole field B2 at R = 4 cm
and its linear term 2*b2(z)*4,
leading to the linear focusing function along reference track
Dipole field B1 at R = 4 cm and its linear term b1(z), leading to the curvature of reference trajectory

## Slide 22: Linear Particle Optics – Transfer Matrices
Skew terms are small
and can be neglected

## Slide 23
Test particle approach :
About a reference trajectory;
In LCS of a moving frame;
3 test particles for x-motion;
2 test particles for y-motion;
Numerical results:
Approach by Equation of motion:
Where k(s)=2*b2(s)/Br
h(s)=b1(s)/Br
Transfer Matrix Calculations

## Slide 24: Particle distributions at scrapper and dump window
in the y-y’ phase space
in the x-x’ phase space

## Slide 25: Initial particle positions at the scrapper (blue) and final positions at dump window (red)

## Slide 26: Summary
3D modeling and 3D multipole expansion are performed for the SNS momentum dump line to obtain field distributions around a reference trajectory;
Linear particle optics – transfer matrices are obtained through test particle approach and the equation of motion;
Particle distributions on the dump window can be calculated with the transfer matrices.