## Slide 1
Overview of the Circular Electron Positron Collider (CEPC) design
Chenghui Yu
for the CEPC accelerator team
June 24, 2020

## Slide 2: Outline
Physics goals of CEPC
Overview of the facility
Machine introduction
Collider ring  Booster  Linac
Key beam physics challenges
Summary

## Slide 3: Physics goals of CEPC
Precision measurement
e+e- Higgs & Z factory
Ecm  240GeV, luminosity/IP  31034cm-2s-1, 2 IPs, >1M Higgs in 10 years
Ecm  91GeV, luminosity/IP > 11034cm-2s-1, 2 IPs, 1010 Z /year
Precision measurement of the Higgs boson and the Z boson
BEPCII has already operated for 12 years
CEPC – possible accelerator based particle physics program in China after BEPCII
Higgs precision 1% or better
Potential for beam energy upgrade
 enough magnet length space in ARC and long enough straight section in RF region

## Slide 4
Overview
of
the facility
Beam Energy | GeV | 120
Peak Luminosity (10^34)/IP | cm-2 s-1 | 3.0
Int. Luminosity | ab-1/year | 1.4
Beam dE/E at IP |  | 0.00134
Transv. Beam sizes at IP x/y | um | 20.9 / 0.06
Rms bunch length / betaY* | mm | 4.4 / 1.5
Crossing angle | mrad | 33
Rep./Rev. frequency | Hz | 3000
Bunch spacing | ns | 680
# of IPs |  | 2
# of bunches |  | 242
Length/Circumference | km | 100
Facility site power | MW | 300
Cost range | $B US | 5.0
Timescale till operations |  | 2030

## Slide 5: CEPC Timeline (preliminary and ideal)
R&D Engineering Design (2016-2022)
Construction (2022-2030)
Data taking (2030-2040)
Pre-studies (2013-2015)
1st Milestone: Pre-CDR (by the end of 2014) ; 2nd Milestone: R&D funding from MOST (in Mid 2016); 3rd Milestone: CEPC CDR progress Report (by the end of 2016); 4th Milestone: CEPC CDR Report (by the end of Aug 2018); 5th Milestone: CEPC TDR Report and Proto R&D (by the end of 2022); 6th Milestone: CEPC construction start (2022);
CEPC
Current time

## Slide 6
CEPC accelerator CDR completed in June 2018
  Introduction
  Machine Layout and Performance
  Operation Scenarios
  CEPC Collider
  CEPC Booster
  CEPC Linac
  Systems Common to the CEPC Linac, Booster and Collider
  8. Super Proton Proton Collider
  9. Conventional Facilities
  10. Environment, Health and Safety
  11. R&D Program
  12. Project Plan, Cost and Schedule
CDR International Review June 28-30, 2018. Final CDR (accelerator) released on Sept. 2, 2018
arXiv:1809.00285

## Slide 7
Candidate sites of CEPC

## Slide 8
Machine introduction
Double ring collider with 2 IPs
Compatible with the geometry of SPPC

## Slide 9
CEPC which aims at researching Higgs boson is a double ring scheme optimized at the beam energy of 120GeV.
Super proton-proton collider (SPPC) will be the next project after the operation of CEPC in the future.
The circumference of CEPC is 100km which is determined by the requirements of SPPC.
The arc regions of the SPPC collider ring, the CEPC collider ring and the CEPC booster ring are in the same tunnel.
The booster ring of CEPC is located above collider ring with the distance of 2.4m.
Machine introduction

## Slide 10
 | Higgs | W | Z
Number of IPs | 2 |  | 
Beam energy (GeV) | 120 | 80 | 45.5
Circumference (km) | 100 |  | 
Synchrotron radiation loss/turn (GeV) | 1.73 | 0.34 | 0.036
Crossing angle at IP (mrad) | 16.5×2 |  | 
Piwinski angle | 3.48 | 7.0 | 23.8
Number of particles/bunch Ne (1010) | 15.0 | 12.0 | 8.0
Bunch number (bunch spacing) | 242 (0.68s) | 1524 (0.21s) | 12000 (25ns+10%gap)
Beam current (mA) | 17.4 | 87.9 | 461.0
Synchrotron radiation power /beam (MW) | 30 | 30 | 16.5
Bending radius (km) | 10.7 |  | 
Momentum compact (10-5) | 1.11 |  | 
 function at IP x* / y* (m) | 0.36/0.0015 | 0.36/0.0015 | 0.2/0.001
Emittance ex/ey (nm) | 1.21/0.0024 | 0.54/0.0016 | 0.18/0.0016
Beam size at IP sx /sy (m) | 20.9/0.06 | 13.9/0.049 | 6.0/0.04
Beam-beam parameters x/y | 0.018/0.109 | 0.013/0.123 | 0.004/0.079
RF voltage VRF (GV) | 2.17 | 0.47 | 0.10
RF frequency f RF (MHz) (harmonic) | 650 (216816) |  | 
Natural bunch length z (mm) | 2.72 | 2.98 | 2.42
Bunch length z (mm) | 4.4 | 5.9 | 8.5
HOM power/cavity (2 cell) (kw) | 0.46 | 0.75 | 1.94
Energy spread (%) | 0.134 | 0.098 | 0.080
Energy acceptance requirement (%) | 1.35 | 0.90 | 0.49
Energy acceptance by RF (%) | 2.06 | 1.47 | 1.7
Photon number due to beamstrahlung | 0.082 | 0.050 | 0.023
Beamstruhlung lifetime /quantum lifetime* (min) | 80/80 | >400 | 
Lifetime (hour) | 0.43 | 1.4 | 2.5
F (hour glass) | 0.89 | 0.94 | 0.99
Luminosity/IP L (1034cm-2s-1) | 3 | 10 | 32
The machine parameters for the Z and w modes do not increase the budget which is based on operation as a Higgs factory.
Collider ring
Machine introduction

## Slide 11
During the operation of Higgs mode all the RF cavities are shared by both e+ and e- beams with the application of the kicker and pulser power supply nearby the RF cavities.
For the W and Z modes the surveys of e+ and e- rings in the RF region are designed independently by turning off the kickers so that all bunches can be filled along the whole rings.
  Common cavities for Higgs mode, bunches filled in half ring for e+ and e-.
  Independent cavities for W & Z mode, bunches filled in full ring.
  Two cell & 650MHz RF cavity.
Higgs, W and Z modes can be switched at any time
CW=6.06kHz, 50%
Machine introduction

## Slide 12
On-axis injection only for Higgs mode
Several circulating bunches from Collider are extracted to the Booster. The Booster circulating bunches are then merged with the injected bunches from Collider. Then, the merged bunches in the Booster are injected back into collider ring by vertical on-axis injection. The procedure will be repeated several times so that all the circulating bunches in the Booster can be accumulated into the Collider. The beamloading effect in the Booster RF system is weak. The maximum cavity voltage drop is 0.48% and the maximum phase shift is 0.63 degree. The peak HOM power per RF cavity is 62W.
Circumference is same
Trajectory difference is 0.011m
0.037ns in time
17 degree RF phase shift in the booster
Machine introduction

## Slide 13
Standard TME cells are chosen for lower booster emittance to relax the DA requirement of collider ring.
The magnetic field quality at the injection energy of 10GeV is still a challenge for both FODO and TME schemes. DA of Booster should be estimated carefully.
 Pre-Booster (10GeV to 45GeV) to deal with the low field problem
High precision requirement for the orbit control at the entrance of collider ring.
Booster ring
Machine introduction

## Slide 14
Parameter | Symbol | Unit | Designed
e- /e+ beam energy | Ee-/Ee+ | GeV | 10
Repetition rate | frep | Hz | 100
e- /e+ bunch population | Ne-/Ne+ |  | > 9.4×109 / >9.4×109
 |  | nC | > 1.5
Energy spread (e- /e+ ) | σe |  | < 2×10-3 / < 2×10-3
Emittance (e- /e+ ) | εr | nm rad | 40
Bunch length (e- /e+ ) | σl | mm | 1 / 1
e- beam energy on Target |  | GeV | 4
e- bunch charge on Target |  | nC | 10
The total beam transfer efficiency from transfer line to the injection point of collider ring is greater than 90%.
The transfer efficiency can be made much higher with a damping ring of energy 1.1GeV while the beam emittance of Linac can be controlled below 40 nm.
Linac
1.1GeV
1200m
Machine introduction

## Slide 15
Project is the integration of physics goals, beam performance, construction cost and operation cost.
Key beam physics challenges
For the CEPC beam physics,
Beam performance reduction caused by fluctuation and beamstruhlung effects
Enough dynamic aperture vs. Beam lifetime and injection
 FODO cell, 90/90, non-interleaved sextupole scheme in ARC
 Selection of BetaY*, IR design, On-axis injection, etc
 Powerful DA optimization logic
 Relax errors tolerance of the machine
 Flexibility and robust

## Slide 16
 L*=2.2m, c=33mrad, βx*=0.36m, βy*=1.5mm, Detector solenoid=3.0T
  Lower strength requirements of anti-solenoids (Bz~7.2T)
  Enough space for the SC quadrupole coils in two-in-one type (Peak field 3.8T & 136T/m) with room temperature vacuum chamber.
Design of interaction region
Key beam physics challenges
The length of cryostat is 4.9m

## Slide 17
  Support and connection (Preliminary)
  Alignment (No idea)
IP assembly
Key beam physics challenges
Connect the flanges using RVC

## Slide 18
SAD code for tracking
145 turns tracked
100 samples
IR sextupoles + 32 arc sextupoles
(Max. free various=254)
Damping at each element
RF ON
Radiation fluctuation ON
Sawtooth on with tapering
Crab waist=100%
Component | x (mm) | y (mm) | z (mm) | x (mrad) | y (mrad) | z (mrad) | Field error
Dipole | 0.10 | 0.10 | 0.10 | 0.1 | 0.1 | 0.1 | 0.01%
Arc Quadrupole | 0.10 | 0.10 | 0.10 | 0.1 | 0.1 | 0.1 | 0.02%
FF Quadrupole | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 
Sextupole | 0.10 | 0.10 | 0.10 | 0.1 | 0.1 | 0.1 | 
RMS close orbit distortions are smaller than 40 µm in both horizontal and vertical plane. Beta beatings < 1.5% , Coupling < 0.2%
Dynamic aperture optimization with errors @ Higgs
Dipole | Quadrupole | Sextupole
B2/B0≤4×10-4 B3/B0≤0.8×10-4 B4/B0≤0.2×10-4 Bn(n>4)/B0≤0.8×10-4 | B2/B1≤4×10-4 B3/B1≤4×10-4 B4/B1≤2×10-4 Bn(n>4)/B1≤1×10-4 | B3/B2≤20×10-4 B4/B2≤3×10-4 B5/B2≤20×10-4 Bn(n>5)/B2≤10×10-4
RMS
R=12mm
> 90% of 1000 seeds
Key beam physics challenges

## Slide 19
~50% of 1000 seeds
Dynamic aperture optimization with errors @ Higgs
Key beam physics challenges
~10% of 1000 seeds
The optics correction is very challenging for the relaxed tolerance of the imperfections.
More finer correction of orbit and optics
More harsh alignment restrictions

## Slide 20
  We still have no effective online measurement and alignment.
Under gravity, deformation=190m
1C variation, deformation=48m
Under magnetic field force the deformation> 0.5mm
  Short FF system  larger betaY*  Decreasing the luminosity
Key beam physics challenges
In fact

## Slide 21: Summary
CEPC which aims at researching Higgs boson is a double ring scheme optimized at the beam energy of 120GeV.
The machine parameters for the Z and w modes do not increase the budget which is based on operation as a Higgs factory.
The key beam physics issues are DA and dominant factors which can reduce the DA.
IR design is the most important for the whole machine.