## Slide 1
Plasma – Laser Wakefield Accelerators
1 TeV and beyond
Carl Schroeder
BELLA Center
Lawrence Berkeley National Laboratory
July 1, 2020, Joint AF-EF Meeting of Future Colliders: Day 2
WarpX
Work supported by the U.S. DOE, Office of Science, Office of High Energy Physics, under Contract No. DE-AC02-05CH11231

## Slide 2
Novel accelerator technologies / advanced accelerator concepts based on wakefields producing gradients >1 GV/m
Goal: to develop accelerator technology to build an e-/e+/gamma linear collider at the TeV energy scale (and beyond), with much reduced footprint (and cost)
Dielectric (~1 GV/m)
Laser
Beam
Dielectric Laser Accelerator (DLA)
Laser wakefield accelerator (LWFA)
Plasma (~10 GV/m)
Structure-based wakefield accelerator (SWFA)
Plasma wakefield accelerator (PWFA)
Common features: ultra-high gradient; small structures; short bunches
Technical maturity and time frame: Longer-term collider options
driver
medium
2
Novel accelerator technology based on wakefields

## Slide 3
Laser-driven plasma wakefield accelerators (LWFA)
Main advantage of laser-plasma accelerator technology: compact linac footprint (both accelerating plasma cell and drive laser beam)
Wakefield (plasma wave) driven by the ponderomotive force of a resonant laser pulse in plasma
Focusing and acceleration provided by plasma wave
Characteristic size of accelerating field:
    Plasma density n0=1017 cm-3 yields E=30 GV/m
Uses short duration, high intensity drivers [laser drivers rely on Chirped Pulse Amplification (CPA) – Nobel prize 2018]
Compact coupling (< 1 m) of laser drivers using plasma mirrors
3
electron plasma density
laser driver
particle beam
plasma wavelength
Esarey, Schroeder, Leemans, Rev. Mod. Phys. (2009)

## Slide 4
Basic configuration of a laser-plasma-based linear collider
Preliminary/Strawperson designs have been produced to guide R&D
R&D focus has been on developing accelerator technology
No complete conceptual design is ready
Linac: staged laser wakefield accelerators (LWFAs):
Design (optimizing operational plasma density) yields 5 GeV/stage (100 stages/linac for 1 TeV):
    Geometric/average gradient = 2.3 GV/m
Time structure at IP:
    single bunches, separated by 20 μs
Short (8.5 μm rms), shaped (trapezoidal current dist.):
    beamstrahlung reduction:
    𝞂z< β*
Flat or round beams may be accelerated
Key characteristics of a LWFA-based collider:
4
Leemans & Esarey Phys. Today (2009)

## Slide 5
Potential Facility Table
Laser-plasma collider - e-/e+ |  | 1 TeV cme | 3 TeV cme | 30 TeV cme
Beam Energy | TeV | 0.5 | 1.5 | 15
Luminosity (10^34) | cm-2 s-1 | 1 | 10 | 1000
Int. Luminosity | ab-1/yr | 0.18 (5000hrs) | 1.8 (5000hrs) | 18 (5000hrs)
Beam dE/E at IP |  |  |  | (Y>>1 regime)
Transv. Beam sizes at IP x/y | nm | 50 / 1 | 10 / 0.5 | 0.2 / 0.2
Rms bunch length / beta* | mm | 0.0085 / 0.1 | 0.0085 / 0.1 | 0.0085 / 0.2
Crossing angle | urad |  |  | 
Rep. frequency | kHz | 47 | 47 | 47
Bunch spacing | us | 21 | 21 | 21
# of IPs |  | 1 | 1 | 1
# of bunches |  | 1 | 1 | 1
Length (2x main linac tunnel) | km | 0.44 | 1.3 | 13
Facility site power (2 linacs) | MW | 105 | 315 | 3151
Cost range | $B US |  |  | 
Timescale till operations |  | >30 years | >30+ years | >30++ years
requires laser tech maturity before estimate
5
1 um laser wavelength
1017 cm-3 plasma density
Schroeder et al. NIMA (2016)
TBD: similar to conventional collider designs
Laser rep. rate not available with present laser technology
Upgrade potential: Same laser system for 1, 3, 30 TeV
ALL PARAMETERS NEED SYSTEM-INTEGRATED DESIGN STUDY

## Slide 6
Status of LWFA experimental R&D
  Single LWFA stage achieved multi-GeV acceleration: 8 GeV in 20 cm (40 GV/m)
  Proof-of-principle staging of LWFAs
Compact driver coupling using plasma mirrors
  Proof-of-principle experiment demonstrate 100 MeV energy gain
  Multi-GeV staging experiments are planned / being commissioned
divergence:
150 mrad
Plasma lens focusing of beam
  1 Hz rep. rate
  Reproducibility limited by laser fluctuations (at ~100 Hz)
discharge-capillary plasma waveguide
6
2019 (LBNL)
2014 (LBNL)
2006 (LBNL)
Energy gain (GeV) in LWFA stage
Operational plasma density (x1018 cm-3)
Gonsalves et al. PRL (2019)
Steinke et al. Nature (2016)
2013 (TPW)
2013 (GIST)

## Slide 7
Laser technology requirements for collider applications
Laser energy/pulse [J]
rep. rate [kHz]
Two promising laser architectures for collider applications:
  Coherent combination of fiber lasers (1 micron). R&D at Jena, Michigan, LBNL, LLNL, et al.
      ~40-60% wall-to-laser efficiency
  Tm:YLF (1.9 micron) – (4x as many LWFA stages). R&D at LLNL
100 kW
10 kW
1 kW
kBELLA
(Ti:Sa)
fiber
fiber
Tm:YLF
BELLA (LBNL)
HAPLS (ELI)
CoReLS (Korea)
7
existing laser system
technically feasible today
collider requirement
+

## Slide 8
Key accelerator R&D challenges
8
Laser technology development
  Coherent combining of fiber lasers
  Development of Tm:YLF
  kW average power systems feasible today
Robust e+ acceleration configuration
  Proposed configurations (hollow plasma channels, plasma columns) require experimental demonstrations
Beam matching/coupling between stages
  Strong focusing forces in plasma: β~ 0.01 - 0.1 m
Alignment
  Small structures (~10-100 um) place severe (~nm) alignment tolerances
Stability in main linac
  Transverse stability (BBU) is issue in strong wakefield regime
  Proposed mitigation methods (ion motion, plasma focusing chirp) require R&D
common challenges for advanced accelerator concepts

## Slide 9
R&D
Construction
5 10 15 20 25 30
LWFA R&D timeline towards a collider
DOE HEP AAC Roadmap (2016)
  US AAC community outlined R&D goals in 2016 roadmap
  Progress on all R&D goals
  Roadmap to be updated
  Technically limited timeline:
Critical Technologies:
  High average power laser development: TRL2
  Plasma cell development: TRL3
  Multi-GeV/cell acceleration: TRL4
  Staging of LWFAs: TRL3
  Positron acceleration methods: TRL2
  Stability: TRL3
  Alignment: TRL2
9
years

## Slide 10
LWFA R&D facilities world-wide
10
US LWFA R&D Laboratories:
LBNL – BELLA
LLNL – JLF
BNL – ATF
SLAC – MEC
U. Texas
U. Michigan
LLE (Rochester)
U. Nebraska
NRL
UCLA
U. Maryland
International LWFA R&D Laboratories:
ELI-Beamlines (Czech)
ELI-NP (Romania)
U. Lund (Sweden)
HZDR (Germany)
DESY (Germany)
LMU (Germany)
Jena (Germany)
RAL (UK)
SCAPA (UK)
U. Oxford (UK)
LOA (France)
Apollon (France)
LULI (France)
INFN (Italy)
CoReLS (Korea)
KPSI (Japan)
Tsinghua U. (China)
SIOM (China)
SJTU (China)
TIFR (India)
IAMS (Taiwan)
ALLS (Canada)
Weizmann Inst. (Israel)
Compactness of laser systems has led to proliferation of LWFA R&D in laboratories and universities world-wide

## Slide 11
International community working toward addressing collider R&D challenges
11
Advanced LinEar collider study GROup
Foster Advanced Linear Collider activities based on Advanced and Novel Acceleration (ANA) concepts
Framework to amplify international coordination, broaden the community, involving accelerator labs/institutes
Identify topics of ANAs requiring intensive R&D and facilities needed
Physics
Case
Theory
Modeling Simulations
Collider Machine Design
LWFA
SWFA
PWFA
DLA
Positron Acceleration
ALEGRO Steering Group
ALEGRO Working Groups
ICFA
ICFA ANA Panel
Euronnac
B Cros
C Schroeder
P Muggli
http://www.lpgp.u-psud.fr/icfaana/alegro
Worldwide
R&D for all aspects of collider design
Input document for the European Strategy
Global Scientific Roadmap
Development of an Advanced Linear Collider (ALIC) at the energy frontier
Contribution to the US strategy
arXiv:1901.08436
arXiv:1901.10370

## Slide 12
Overall Technical Maturity: 1-Significant R&D Required
Laser-driven plasma accelerators:
  Ultra-high gradient accelertor technology: ~10 GV/m
  Goal: e-/e+/gamma linear collider at the TeV energy scale (and beyond), with much reduced footprint (and cost)
  Longer-term collider option: >30 years
Experimental facilities to advance LWFA R&D in next 5-10 years planned: kBELLA, EuPRAXIA, etc.
Near- and mid-term applications (LWFA-driven X-FEL, compact gamma-ray source, ion acceleration for medical applications, etc.) are actively being pursued
  Near-term applications are important demonstrations of accelerator technology that will advance collider R&D
12
Summary

## Slide 13
Thank you.
13