## Slide 1: DUNE CDR – Cryostat Structural Analysis
Giorgio Vallone
DUNE CDR: Near Detector
07-09 July 2020

## Slide 2: Index
Introduction
Composite Window Design
Structural Analysis
Frame/Window Joint Design
Conclusion

## Slide 3: Index
Introduction
Composite Window Design
Structural Analysis
Frame/Window Joint Design
Conclusion

## Slide 4: Cryostat Description
Liquid Argon enclosed by stainless steel plates / Polyurethane sandwich
One side covered by a composite window (described later) to reduce the impact on the particle beam
Window size: L8156*W3810*T372 (max)
Steel Frame
Detector
Polyurethane
Steel Plate 1
Steel Plate 2
Liquid Ar
Composite Window
Box Beams

## Slide 5: Design Criteria – Applicable Guidelines
The design shall follow the applicable Fermilab Note (FESHM 5031.7: Guidelines for the Design, Fabrication, Installation and Testing of Metallic Membrane Cryostats)
  A couple of important points:
    If the structural support (…) is made of structural steel, then (…) ANSI/AISC 360 “Specification for Structural Steel Buildings” applies to the design and construction of the steel structure
    The following standards (…) are used for the design, fabrication, installation and testing of metallic membrane cryostats: JGA RP-107-02) (…); British Standard BS EN 14620
    Level of safety commensurate with ASME Boiler and Pressure Vessel Code, Section VIII as required by (…) 10 CFR 851 Worker Safety and Health Program
    The design (…) shall be independently verified and certified by a U.S. licensed Professional Engineer (…) and submitted for review by the Large Quantity Liquid Argon Cryogenic Panel
Following these guidelines we will proceed as follows:
  Design the steel structure according to one of the listed standards
  Design the composite window following the ASME Boiler and Pressure Vessel Code, Section X – Fiber-Reinforced Plastic Pressure Vessels
  Grade IV analysis (ASME BPVC Sec. VIII) + experimental tests to verify the joint between the two

## Slide 6: FEA Model Description – Geometry and Material Properties
Geometry:
    YZ symmetry
    Steel plates, frame: shell elements
    Composite plate, foam: solid elements
  Foam properties:
      Density = 90 kg/m3
      E = 10 MPa – Seems a reasonable order of magnitude
      𝜈 0.5 (incompressible)

## Slide 7: FEA Model Description – Boundary Conditions and Loads
Boundary conditions:
  Floor b.c. only on y, but probably friction will lock also the other directions
  Everything bonded
Loads:
    Liquid Argon Hydrostatic Load - Density = 1400 kg/m3 - Liquid Level Height = 4.5 m w.r.t. membrane floor
    Overpressure Load = 350 mbar
    Gravitational Acceleration

## Slide 8: Index
Introduction
Composite Window Design
Structural Analysis
Frame/Window Joint Design
Conclusion

## Slide 9: Window Design: Which are the Available Parameters?
Sandwich design
  Better than locally stiffened designs for distributed loads (e.g. pressure)
Available parameters:
    Skin thickness / Core thickness
    Skin material
    Core material
  Carbon and Aluminum outperform other materials, but they are much more expensive

## Slide 10: Window Design – Design Space as function of the Parameters
Parameter space:
  Skins in Glass/Carbon Fiber, 25 or 50 mm thick.
  Polyurethane core, density from 80 to 400 kg/m3
  Carbon fiber costs more but does not bring advantages considering the design requirements
    Total mass/attenuation is more important than radiation length
  Design point: G10 skin, 25 mm thickness, 250 kg/m3 polyurethane
    Trade off between surface density and displacement
Only solutions with u<10 mm

## Slide 11: Window Design: Surface Density Contribution of the Window
Surface density of each component
  Target (total) is ~ 50 g/cm2
Composite window contribution ~ 16% of the total
  Advantage on steel:
    factor ~2.5 on average
    1 order of magnitude on the beam locations
Layer | Material | thickness | rho | rho*t | Contrib.
/ | / | mm | kg/m3 | g/cm2 | %
Liquid | Argon | 300 | 1396 | 41.9 | 62.7%
Plate | Steel | 2 | 7000 | 1.4 | 2.1%
Insulation | Polyurethane | 808 | 90 | 7.3 | 10.9%
Window | Composite | 372 |  | 16.2 | 24.3%
Steel Avg. | Steel | 58.3 | 7000 | 40.8 | 
Steel Max. | Steel | 372 | 7000 | 260.4 | 
Total |  |  |  | 66.78 | 100%

## Slide 12: Index
Introduction
Composite Window Design
Structural Analysis
Frame/Window Joint Design
Conclusion

## Slide 13: Structural Analysis - Displacements
Total displacement is 7.9 mm
  It can still be easily improved, if necessary, but design target is 10 mm
Contributions (plate, z direction):
  Gravity: 0.1 mm
  Hydrostatic: 5 mm
  Pressure: 2.8 mm
All Loads
Hydrostatic
Gravity
Pressure

## Slide 14: Structural Analysis – Impact of the frame on the displacement
Plate stiffness – simply supported and fixed on the outer edge
  Displacement: 7.9 mm or 2.6 mm
  Most of the deformation is coming from the frame!
    Edge rotation ~ 3.3 mm
    Support motion ~ 2 mm
Fixed
Supported

## Slide 15: Structural Analysis – Stress Analysis
Negligible stress on the plate
Stress on the steel structure is low almost everywhere
  Few joints see local stress spikes (still lower than the yield limit)
  Max stress ~ 180 MPa on the square beam joint
    This can be easily be reduced adding local reinforcements (as in ProtoDUNE)

## Slide 16: Index
Introduction
Composite Window Design
Structural Analysis
Frame/Window Joint Design
Conclusion

## Slide 17: Joint Design
Joint selection:
  Box beam around the plate for torsional stiffness
  A tapered lap joint is not able to satisfy the strength requirements (with a reasonable length). A scarf joint can sustain much higher loads
  Production process is more complicated
Design process:
  2D analysis to quickly optimize the geometry
  Detailed analysis on a 3D model
  Submodel critical regions (grade IV analysis)
  Experimental verification

## Slide 18: Scarf Joint – Production Process
  Lay-up the bottom face sheet on the steel c-joint bottom half
  Glue the bottom joint steel ‘shoe’
  Glue the core
  Glue the top joint steel shoe
  Lay-up the top face sheet
  Weld the c-joint, then weld to the box beam
1
2
3
4
5
6

## Slide 19: Scarf Joint – 2D Model Results - Compliance
Joint compliance is almost all in the box beam constraint
  This is what we want, and a joint behaving like this will guarantee similar results to the one provided by the 3D analysis
Stress in the composite components is negligible
High local stresses in steel,
  May need some reinforcement / higher radius
  We might decide to accept a small amount of plastic deformation there
  Here we are considering an ‘exaggerated’ scenario where there is no longitudinal support

## Slide 20: Scarf Joint – 2D Model Results – Glue Strength
Stress allowed in the glue:
  5 MPa average on shear stress
  10 MPa average on tensile
We are ~1 order of magnitude below
  Also the maximum stress in the glue is lower than our average criteria

## Slide 21: Structural Analysis – Stress Analysis on the Joint
Grade IV analysis example: joint submodel
  displacements interpolated from the global model and applied on the cut boundary
Stress allowed in the glue:
  5 MPa average on shear stress, 10 MPa average on tensile
Max frictional stress ~ 6 MPa, Max. tension ~ 5 MPa
Criteria satisfied with significant margin

## Slide 22: Experimental Verification of the Joint Performances
Prototype plan aimed at the verification of the mechanical strength of the joint
Planned tests:
  Stiffness/strength measurements on sub-scale samples
    Results used along with numerical models
  Stiffness/strength measurement on a real-scale portion of the joint
  Thermal cycle the joint:
    Important to verify strength
      This can happen only in a catastrophic scenario where the Argon leaks
    We already have experience with glued joints at -40 °C (e.g. ATLAS)
Back-up plans:
  FEA suggests that we will not need them, but...
  Increase the glued surface size
  Joints of greater complexity can further increase the strength of the joint

## Slide 23: Index
Introduction
Composite Window Design
Structural Analysis
Frame/Window Joint Design
Conclusion

## Slide 24: Conclusion
The proposed design can meet the requirements:
  Displacement < 10 mm
  Surface density 16 g/cm2
  Strength is ok
An ‘acceptable’ design space was defined
  The final design can be decided based on trade-offs (cost, physics performances, mechanical performances)
An analysis procedure was proposed to verify the structure and the composite joint in particular
  Experimental tests will be performed in order to verify the strength of the joint and the effect of thermal cycles

## Slide 25
Back-up slides

## Slide 26: Window Design: Material Selection
Core material mechanical performances vs radiation length

## Slide 27: Plate Design - Summary
Considering only FR-3700 series polyurethane
  Density from 80 to 400 kg/m3
  Shear modulus ~ linear with the density
  G10 has higher radiation length than Polyurethane
Last plot: only solutions with disp. < 10 mm
/Update with density and remove rad. Length?

## Slide 28: Window Design: Material Selection
  G10 can provide sufficient performances but higher radiation length
    Carbon fiber significantly more expensive
  Joints are a fixed cost, and performance can be like the steel side
    Could we consider to extend the window on the whole side? Would this be better?

## Slide 29: Window Design: Surface Density Contribution of the Window
Surface density of each component
  Target (total) is ~ 50 g/cm2
Composite window contribution ~ 16% of the total
  Advantage on steel:
    factor ~2.5 on average
    1 order of magnitude on the beam locations
Layer | Material | thickness | x0_s | rho | L | x0 | X0 | Contrib. | rho*t | Contrib.
/ | / | mm | g/cm2 | kg/m3 | cm | cm/cm | % | % | g/cm2 | %
Liquid | Argon | 300 | 14 | 1396 | 10.029 | 2.99 | 299% | 67.4% | 41.9 | 62.7%
Plate | Steel | 2 | 1.7 | 7000 | 0.243 | 0.82 | 82% | 18.5% | 1.4 | 2.1%
Insulation | Polyurethane | 808 | 40.8 | 90 | 453.333 | 0.18 | 18% | 4.0% | 7.3 | 10.9%
Window | Composite | 372 |  |  |  | 0.45 | 45% | 10.1% | 16.2 | 24.3%
Steel Avg. | Steel | 58.3 | 1.7 | 7000 | 0.243 | 24.00 | 2400% |  | 40.8 | 
Steel Max. | Steel | 372 | 1.7 | 7000 | 0.243 | 153.18 | 15318% |  | 260.4 | 
Total |  |  |  |  |  | 4.44 | 444% | 100% | 66.78 | 100%

## Slide 30: Alternative Joint Design
  Test design 1:
    G10 links might be connected or not (single piece or core)

## Slide 31: Comparison to Fermilab Technical Report
Comparison with results from Technical Report (EDMS No: 2061797)
    We can use the displacement on the side with no window
      The roof is not comparable, geometry completely different
    Report displacement between 7 and 8 mm
    New model displacement is 6.6 mm
      Expected as there are more beams in this design

## Slide 32: Structural Analysis - Displacements
Total displacement is 7.8 mm
  It can still be easily improved, if necessary, but design target is 10 mm
  Rotate everything
Contributions (z direction):
  Gravity: 0.1 mm
  Hydrostatic: 2.8 mm
  Pressure: 5 mm
All Loads
Hydrostatic
Gravity
Pressure