## Slide 1: DUNE Near Detector PRISM Design
Robert Flight
DUNE CDR: 30% Near Detector Design Review
8 July 2020

## Slide 2
DUNE Near Detector PRISM Transport System
Review topics
PRISM Specifications
Detector weights
System components and specs - speeds/times/acceleration
Transport system - movement considerations for SAND
Existing Hilman examples
Prototype plans
PRISM movement safety
Energy chain application

## Slide 3: PRISM Specifications
Overall movement time for detectors
  8 hours to travel 30.5m
"Gentle" accelerations and low speed of motion
  Accelerate to 0.17cm/sec², top speed 10.2cm/min (1.7mm/sec [0.066”/sec])
"Minimal" vibrations to minimize sloshing & LAr module movements
  Verify FEA analysis with the prototype
  Smoothness of rollers/beams during movement
Precision of location
  +/-3cm, with a goal of +/-1cm
Monitoring of location, +/- 1cm, with a goal of +/-1mm
Hilman powered rollers satisfy the movement and location needs
  Can be controlled locally or remotely
  Commercially available product
Goals to be confirmed with prototype and testing

## Slide 4: Transport system movement detector weights Primary Design
Approximate loads:
LAr detector – 900 tonne
MPD – 800 tonne
SAND – 900 tonne
20 tonne of side reaction loads from magnets
20 tonne side load creates a 33 tonne unequal loading on the transport wheels. Not enough to unseat the rollers
KLOE
MPD
LAr Detector

## Slide 5: Transport system movement detector weights Fallback Design
Approximate loads:
LAr detector – 900 tonne
Muon Spectrometer – 600 tonne
SAND – 900 tonne
20 tonne of side reaction loads from magnets
SAND
MUON
SPECTROMETER
LAr Detector

## Slide 6: Transport system movement plans
Use Hilman Powered rollers to move detectors
This example shows (6) 100 ton electric motorized roller assemblies moving a 400 ton test load at 1 ft/min for a nuclear waste conversion plant.

## Slide 7: Transport system movement plans
Use Hilman Powered rollers to move detectors
Guide rollers at the 4 corners are sufficient to handle the side loads

## Slide 8: Transport system movement plans
This video shows it’s slow, smooth, and can bridge gaps

## Slide 9: Hilman Powered Skate
It’s the modern version of rolling stuff on logs
The recirculating rollers support the load at plate #11
Similar to a motor driven bulldozer track

## Slide 10: Hilman Powered Skate
Hilman 200 Tonne capacity unit
“rail”
“skate”
Leading & Trailing brushes sweep debris off rails (not shown)

## Slide 11: Transport system movement plans
Planned total travel is within 8 hours
1 hour preparation at the beginning and at the end
6 hrs remain for travel time
Average speed is 8.5cm/min [3.3in/min] over 30.5m
Multiple stops within the 30.5m are planned, actual locations to be flexible per run
Choosen stop locations within 3cm with a goal of 1cm, verify location using servo motor counts and laser distance measurement of 1cm, goal of 1mm
Location changes may be a 1 week apart
Complete movement is planned to be unmanned, controlled remotely

## Slide 12: Transport system movement speeds
Speed-time-distance charts for 30.5m travel within 6 hrs
Acceleration works out to be 0.17cm/sec²
Does this create sloshing? Or other issues?
Analysis performed at FNAL and Mockups to be tested at Stony Brook

## Slide 13: Transport system location monitoring
Position sensing, 2 redundant systems
Primary source is to use the Hilman servomotors as the position encoder
Secondary source, the Laser distance sensor removes errors of possible roller errors within the Hilmans
Both provide mm level accuracy

## Slide 14: Transport system SAND movement plan
SAND movement zigs & zags around detectors
Track rail spacing needs to be equal to allow zig-zag
Transport speed can be faster than other detectors, TBD
Controlled movement performed locally
Transport system design affects the design of all detectors

## Slide 15: Hilman Costs
One system would be used for each detector
Hilman units are a commercially available product, a plug ‘n’ play system
On site costs not included
Future plans
Visit Hilman in NJ
Better understand the details of their proposal
Refine specs, requote, etc
Order a 4 unit system for prototype, then reuse for a ND detector

## Slide 16: Prototype plans
600 tonne , (4) powered Hilmans
FEA analysis planned to simulate sloshing and module movements
Dry prototype shown
Wet prototype version to be based upon FEA analysis
Vibration sensors, various motion profiles, etc based upon analysis
Components reused for detectors
Test powered units combined with free rolling units

## Slide 17: Prototype Plans
Developing prototype location plans at Stony Brook

## Slide 18: PRISM movement safety
Hilmans will have brushes to sweep debris out of the way, off the rails
Auditable alarms and flashing lights precede movements to alert local personnel
Provisions for an emergency stop
Movement safety requirements will follow FNAL & OSHA safety requirements and procedures

## Slide 19: Perimeter Light Curtain for E-Stop
Create a perimeter laser beam curtain that moves with each detector
Break the curtain anywhere to stop movement
A common use of this device type is on elevator doors

## Slide 20: Energy Chain Application
Cryogenic Line Guides Require a Commercial Design Solution
Metal Guide Option
Plastic Guide Option
Vacuum Jacketed Lines
Commercially Available
Guide Designs Needs To Resist “Coil-Up” Under Vacuum Load

## Slide 21: Energy Chain Application
Commercially available product
We are working closely with the supplier to have a successful product application
Plastic chain parts to reduce vibrations
Similar design steps are being applied to the MPD and the MUON Spectrometer
Examples

## Slide 22: Energy Chain Application
IGUS E4-350-500
Internal Cross section: 350mmx500mm
Weight: 65.7 kg/m
Cryogenic layout provided to IGUS for a design proposal. The inclusion of electric and control cabling is in process.

## Slide 23: Energy Chain Application
Energy Chain Sizing
Length of energy chain: 26.25 meters
  16 m for necessary travel
  8.25 m in energy chain bend
  1 m relief at both ends
Weight of Energy Chain
Cryogenic Piping(filled): 572.1 kg
Igus Chain(65.7kg/m): 1,724.6 kg
Total Weight: 2,296.7 kg
Translating support

## Slide 24: Summary Costs
Support Frames are in individual detector BOEs
  ND-LAr support frame is in cryostat BOE (131.02.03.03.02)
  Spectrometer frame is in muon spectrometer BOE (131.02.03.04)
  SAND frame needs to be reconfigured -> SAND cost, not US scope
Floor Rails are in PRISM BOE
  Rails for all three detectors (LAr, Spectrometer, SAND) plus installation is in PRISM BOE (131.02.03.08.02)
Movement System (rollers, control interface, safety system, position sensor, hardware)
  ND-LAr movement system plus common tooling is in PRISM BOE (131.02.03.08.02)
  Spectrometer movement system is in I&I BOE (131.04.02.02)
  SAND Movement system -> SAND cost, not US scope
Energy Chains
  LAr and spectrometer chain procurements plus pre-assembly are in PRISM BOE (131.02.03.08.02)
  Energy chain cavern wall mounts, assembly, installation are in I&I BOE (131.04.02.02)
$ 1,071,882
$ 970,235
$ 921,915
$ 379,883
Total PRISM Cost:
$ 3,343,915
N/A
N/A
N/A

## Slide 25: Overall Summary
Goals are well defined
The major system components use commercial products to satisfy the goals
Prototype the system to verify analysis
For commonality of parts and systems
  Similar design approach has been applied to the MPD and MUON Spectrometer
  Commonality of parts helps reduce costs

## Slide 26: Supporting documents

## Slide 27: Transport system movement speeds
Charts for 30.5m travel within 6 hrs
Time vs distance
Acceleration is 0.17cm/sec²

## Slide 28: Transport system movement speeds
Speed-time-distance charts for 4m travel within 1.6 hrs
Acceleration is 0.17cm/sec²

## Slide 30
Preliminary Hilman hardware costs
Does not include any on site costs

## Slide 31: Who am I
Licensed Mechanical Engineer
30+ years of experience
17 years working on research projects
    Minerva, T2K, CMS
    CHICO, TIGRESS, JANUS
    FRIB
    Medical device R&D
Prior industrial experiences included factory assembly and automation equipment and project management