## Slide 1: Open-Midplane Dipole Magnet Field Homogeneity
Bob Weggel
5/19 & 5/20/2011

## Slide 2: Illustrative OMD. 1st-quadrant windings X-section & contours of field magnitude B ≡ (Bx2+By2)½; central field B0 ≡ B(x=0,y=0). Muon beam is at [0, 0]; keyhole accommodates energy absorber.

## Slide 3
Design Goals and Constraints
Vertical force on inboard coil must be away from midplane.
Central field B0 = 10 T @ 200 A/mm2 overall current density.
Midplane half-gap = 15 mm for OMD’s of this presentation.
Web between bars should be robust, to withstand stresses.
Design OMD magnets of better and better field homogeneity.

## Slide 4: OMD Ring-Magnet Questions
1) How good can the field homogeneity be?
2) How good does it need to be? 0.01%? Width? Height?
3) How big (high) does the midplane gap need to be?

## Slide 5: Dependence of Field Ratio Bmax/B0 & Megamp-meters of Superconductor on Half-Height of OMD Magnet Gap
An OMD magnet of 75-mm gap half-height uses ~2¼ times as much conductor as a magnet of 15 mm half-height. The field ratio may be ~120% instead of ~107%.

## Slide 6: Radii of Field-Homogeneity Contours
1.0 mm @ 10 ppm
3.0 mm @ 100 ppm
9.0 mm to 10.3 mm @ 1,000 ppm

## Slide 7: Equations for Magnetic Field
For a bar of infinite length, rectangular-cross section and carrying a uniform current density J, the vertical field By is:
where cB = −μ0 j/2𝜋; ui and vj are shorthand for ai−x and bj−y, the horizontal and vertical distances, respectively, from a corner [ai, bj] of a bar cross section to the field point [x, y]. Bx is of the same form, with ui and vj interchanged.

## Slide 8: Equations for Magnetic Force
The vertical component of force, Fy, between two parallel bars of conductor has 16 terms of the form:
where cF = μ0 j1 j2 / 12𝜋; u and v are shorthand for ui,m and vj,n, the horizontal and vertical distances between bar corners [ai, bj] and [am, bn]; i, j, m and n each run from 1 to 2. Fx is similar, with u and v interchanged.

## Slide 9: Inhomogeneity Coefficients for Bar

## Slide 10: Inhomogeneity Coefficients for Wire

## Slide 12: OMD magnet with ∂2B/dx2 = ∂2B/dy2 = 0; Bmax/B0 = 108%.

## Slide 13: Radii of Field-Homogeneity Contours
5.6 mm @ 10 ppm
9.8 mm to 10.0 mm @ 100 ppm
17.1 mm to 18.2 mm @ 1,000 ppm

## Slide 14: Comparison of 2nd & 4th-Order OMD’s 1,000 ppm: 9.0 mm 17.1 mm in x, 1.03 mm  18.2 mm in y 10 ppm: 1.0 mm  5.6 mm in both x & y

## Slide 15: OMD with field homogeneity of 6th order; both bars ∆x >> ∆y.

## Slide 16: Radii of Field-Homogeneity Contours
22 mm to 23 mm @ 10 ppm
32 mm to 34 mm @ 100 ppm
45 mm to 52 mm @ 1,000 ppm

## Slide 17: OMD of 6th order; outboard bar ∆x << ∆y; Bmax/B0 = 118%.

## Slide 18: Radii of Field-Homogeneity Contours
21 mm to 22 mm @ 10 ppm
30 mm to 34 mm @ 100 ppm
42 mm to 78 mm @ 1,000 ppm

## Slide 19: Field magnitude of open-midplane dipole magnet with field homogeneity of 8th order. Bmax/B0 = 119%.

## Slide 20: Radii of Field-Homogeneity Contours
30 mm to 32 mm @ 10 ppm
40 mm to 43 mm @ 100 ppm
52 mm to 60 mm @ 1,000 ppm

## Slide 21: Field magnitude of OMD magnet with homogeneity of 12th order. White contours are ±0.01%. Bmax/B0 = 119%.

## Slide 22: Radii of Field-Homogeneity Contours
77 mm @ 10 ppm
~100 mm @ 100 ppm
~120 mm @ 1,000 ppm