## Slide 1: Muon Collider
D. Schulte for the International Muon Collider Collaboration

## Slide 2: Overview
In the past, muon colliders have mainly be studied in the US (MAP collaboration)
  Muon beams produced from proton beam
  MICE in the UK to demonstrate required muon cooling, concluded its programme recently
Some activity on alternative muon source using positron beam mainly in Italy
For the European Strategy working group was formed to assess muon collider potential
  N. Pastrone et al.
  recommended to strategy process arXiv:1901.06150
  Strategy recently proposed international muon collider design study
Forming an international design study collaboration
  see meeting on Friday July 3rd, https://indico.cern.ch/event/930508/

## Slide 3: Proton-driven Muon Collider Concept (MAP)
Short, intense proton bunches to produce hadronic showers
Pions decay into muons that can be captured
Muon are captured, bunched and then cooled
Acceleration to collision energy
Collision
No CDR exists, no fully integrated baseline
No cost estimate
Need to extend to higher energies (10+ TeV)
But did not find something that does not work
From the MAP collaboration: Proton-driven source (M. Palmer et al.)

## Slide 4: The LEMMA Scheme
45 GeV positrons to produce muon pairs
Accumulate muons from several passages
Low emittance muon beam
no cooling required, much less radiation
But large positron current and production needed O(1017/s)
Target is challenging
Currently, do not reach luminosity goal
More work is needed to conclude
From the LEMMA team: Positron-driven source (M. Antonelli et al.)

## Slide 5: Proposed Tentative Timeline (2019)
1
3
5
7
9
11
13
15
17
2
4
6
8
10
12
14
16
Design
Construct
Test Facility
Design
Technologies
Ready to decide on test facility
Cost scale known
Ready to commit
to collider
Cost known
Ready to construct
Baseline design
Exploit
Design optimisation
Project preparation
Design / models
Prototypes / t. f. comp.
Approve
Exploit
Prototypes / pre-series
R&D detectors
Prototypes
CDRs
MDI & detector simulations
Large Proto/Slice test
TDRs
Technically limited
MACHINE
DETECTOR
To be reviwed

## Slide 6: Proposed Scope
“In the first period, in time for the next European Strategy for Particle Physics Update, the study aims to establish whether the investment into a full CDR and a demonstrator is justified. It will provide a baseline concept, well-supported performance expectations and assess the associated key risk as well as cost and power consumption drivers. It will also identify an R&D path to demonstrate the feasibility of the collider.”
Benchmark region around O(3 TeV), L = O(1034 cm-2s-1)
  Well above higgs factory energy
  Should focus on technologies ready in 10-20 years
  MAP did work on this range
Benchmark region 10+ TeV, L = O(1035 cm-2s-1)
  New territory, beyond what CLIC can do
  Need to fully understand physics needs
  Need to address a number of additional challenges
Exploration of synergies
  Neutrino factory
    potential useful application, would be large-scale demonstrator
  Higgs factory
    more mature options exist currently, but we can come back if no one is moving forward

## Slide 7: Tentative Target Parameters
Parameter | Unit | 3 TeV | 10 TeV | 14 TeV
L | 1034 cm-2s-1 | 1.8 | 20 | 40
N | 1012 | 2.2 | 1.8 | 1.8
fr | Hz | 5 | 5 | 5
Pbeam | MW | 5.3 | 14.4 | 20
C | km | 4.5 | 10 | 14
<B> | T | 7 | 10.5 | 10.5
εL | MeV m | 7.5 | 7.5 | 7.5
σE / E | % | 0.1 | 0.1 | 0.1
σz | mm | 5 | 1.5 | 1.07
β | mm | 5 | 1.5 | 1.07
ε | μm | 25 | 25 | 25
σx,y | μm | 3.0 | 0.9 | 0.63
Note: The study will have to verify that these parameters can be met
Note:
Based on extrapolation
CLIC @ 14 TeV would need
130 MW beam power
for L = 28 x 1034 cm-2s-1
of which 1/3 is within 1% around nominal energy
Additional benefits for muon collider less initial state radiation and smaller beam energy spread
2 IPs in each case
Single bunch
Luminosity decays exponentially

## Slide 8: Initial Key Issues
Neutrino radiation
  known to need mitigation for 10+ TeV
  explore mitigation methods
MDI and background conditions
Cost and power drivers
  fast ramping magnet systems
  collider ring magnets
  RF systems
Beam quality
  Muon source, two options, define baseline and alternative, improve performance
    Improvement of cooling channel for proton-driven scheme appears possible because hardware performance is better than initially assumed
  Preservation of beam quality
Define demonstration programme for implementation in second half of the decade
  test facility and components

## Slide 9: Conclusion
International muon collider design study collaboration is forming
Synergy with hadron colliders and facilities
neutron spallation sources
superconducting magnets for hadron colliders
shielding, collimation
Synergy with normal, superconducting and plasma-based linear colliders
Physics studies
Superconducting and normal-conducting RF technology
Lattice design
Synergy with electron-positron circular colliders and light sources
optics design challenges
RF technology