## Slide 1: Instrumentation for 21cm cosmology Paul O’Connor
20200730

## Slide 2: What?
PUMA
Packed Ultrawideband Mapping Array
arXiv:1907.12559v1, arXiv:2002.05072
https://puma.bnl.gov
A cosmological survey using the 21cm intensity mapping technique:
              An array of 32,000 6-m parabolic reflectors (900,000m^2 collecting area)
              Low noise 200-1100MHz front end electronics and on-antenna digitizers
              Real-time ~100 PFLOPS processor for interferometric correlation
              DAQ output 7PB/day, sky maps in 4,000 frequency bands
              Calibration hardware for gain, phase, angular acceptance per dish

## Slide 3: Why?
Cost-effective approach for investigating cosmic acceleration after current generation of survey experiments (Rubin Obs / DESI / CMB-S4).
Look where we haven't looked before : redshift range 6 < z < 1.2
Make a tomographic map of the dark matter distribution in the universe
Monitor the transient radio sky: fast radio bursts, pulsars, LIGO followup
Take advantage of emerging digital RF technologies
Rubin, DESI
PUMA
redshift z
NOW
1.2
2.5
6
 CMB-S4 (z = 1100)
Nearby galaxy M31 imaged in 21cm

## Slide 4: How?
Technological path
Team
See arXiv:2002.05072 for details of R&D plan
Jamali 2016 IEEE MTT-S

## Slide 5: Synergies?
picosecond timing and synchronization (FELS, TOF/LIDAR, under-ice neutrino detectors
digital RF beamforming (radar, 5G), digital RF FDM
machine learning for RFI rejection
high-throughput DSP architectures
exascale computing

## Slide 6: Conclusion
21cm intensity mapping is a new, cost-efficient observational technique that is complementary to optical and CMB surveys.
It opens the largely unexplored redshift range 2.5 < z < 6 where beyond-LCDM physics can be studied - dynamic DE, modified GR, inflationary relic signatures.
Leverages industry advances (wireless, AI) and requires no specialized detector environments (cryo, radiation).
Research needs center on DAQ architectures (with 2030-era electronics), and on calibration methods, including sub-picosecond phase synchronization.
The PUMA project is well-matched to HEP expertise and is synergistic with many emerging trends in EF and IF electronics.

## Slide 7: Backup slides

## Slide 8: PUMA: speed of LSST/Rubin, accuracy of DESI

## Slide 9: Obstacles to scaling optical surveys
Detector technology for IR
Atmospheric transparency in IR
Telescope cost scaling
Let’s consider another wavelength range…
z = 0
z = 3.5
Airglow

## Slide 10: The 21cm transition of neutral hydrogen provides precise redshift marker
Spin-flip transition of neutral atomic hydrogen
21cm line in Milky Way galaxy, observed by BMX pathfinder
Spectral line at 21cm rest-frame wavelength is sharp and isolated
 Once detected, provides precise redshift
f, MHz
Atmospheric transmission is favorable in radio window

## Slide 11: Polychromatic Interferometer

## Slide 12: Front end electronics for BMX pathfinder

## Slide 13: BMX pathfinder activities

## Slide 14: Full array network

## Slide 15: Data and computation rates: current estimates
 | PUMA-5K | PUMA-32K | 
Raw data rate | 240 | 1500 | Tbit/s
Real-time computation | 15 | 100 | PFLOP
Output data rate | 13 | 82 | GB/s
Data volume | 0.9 | 5.7 | PB/day
Power * | .23 | 1.5 | MW

## Slide 16: Notional schedule (from whitepaper)
Note: a smaller (5,000-dish) instrument configuration, with scaled-back science reach, is also described in the whitepaper and can be considered as a first stage to construction of the full array.

## Slide 17
CMS (HL-LHC upgrade) 4D tracking
Askaryan Radio Array
LCLS-II
sub-mm resolution LIDAR
arXiv:2005.08992v1
Smart RFI rejection with Machine Learning
2005 cellphone