## Slide 1
1
1
Synchrotron Design and Methodical Cell Optics Study
Aaron Fawley, mentor: Carol Johnstone, co-mentor: Jeff Eldred
CCI Poster Presentation
08/05/2020
Notes: 1
1
1
1
1
1

## Slide 2
Outline
Aaron Fawley | Synchrotron Design and Methodical Cell Optics Study
2
Motivation for new Rapid Cycling Synchrotron (RCS) design
Accelerator terminology and optics background
Description of Particle Undulation Form Factor (PUFF) cell phase advance study
Description of transitionless RCS lattice.
Apply PUFF study to RCS design
Summary of project and main parameters of RCS design
Notes: 2
2
2
2

## Slide 3
Motivation
Aaron Fawley | Synchrotron Design and Methodical Cell Optics Study
3
Future experiments requires greatly increased beam power.
  The Fermilab flagship neutrino experiment, DUNE, requires 2.4 MW of 120 GeV Main Injector (MI) protons on target delivered by the external beamline, LBNF.
A new, high-intensity, 800-MeV superconducting H- Linac (PIP II) is under construction to deliver increased beam power.
However, once PIP-II is commissioned, the now 0.8 – 8 GeV Fermilab Booster becomes the bottleneck for achieving the required beam intensity in the MI.
  At 20 Hz, the Booster is only capable of delivery ~20 x 1012 p/sec.
To achieve the 2.4 MW of beam power will require a new transitionless Rapid Cycling Synchrotron (RCS) with the following specifications
  2 GeV injection energy to mitigate space charge effects (planned upgrade for PIP II Linac)
  Higher extraction energy: 16 GeV
  Between 480 and 620 m circumference (5-6 Booster batches in the Main Injector)
  Fermilab Booster multiturn injection will be upgraded from 400 MeV to accept 800 MeV H- beam from the PIP II Linac
Notes: 3
3
3
3

## Slide 4
Background
Aaron Fawley | Synchrotron Design and Methodical Cell Optics Study
4
FODO Cell – F Quad, Drift, D Quad, Drift, repeat for a periodic lattice.
  Dipoles which bend the beam in an arc are inserted in the drift section for a separated-function circular accelerator
Betatron Functions – “amplitude” or beam envelope in a transverse plane.
  Nominally vertical and horizontal with the dipoles or bending in the horizontal plane
Dispersion – offset of the reference trajectory for off-momentum particles.
Transition – the energy when revolution time does not depend on momentum, longitudinal focusing of off momentum particles is lost – in the current Booster it occurs at 4 GeV.
Phase Advance – Number of 2 oscillations a particle makes – per cell over a turn (machine tune) – always fractional # of oscillations to avoid resonances.
Betatron Oscillation in Longitudinal Direction
in FODO cell.
Jeff Eldred
S(m)
Notes: 4
4
4
4

## Slide 5
Aaron Fawley | Synchrotron Design and Methodical Cell Optics Study
5
Off-momentum Chromatic Correction: Sextupoles
Kick sext  x2
f
high/low Momentum is on outside/inside of ring per dispersion: dispersion defines central trajectory for off-momentum particles.
Blue: high momentum
Green: on momentum
Red: low momentum
f
kick is in the same direction on either side of reference orbit.
Sextupole corrects the focal length of off momentum particles and phase advance.
Zero out chromaticity independently in each plane with 2 families of sextupoles.
  one at high x and one at high y
p > p0
p < p0
p0
Adding a sextupole lens: focusing higher momentum, defocusing lower momentum; this is known as correcting chromaticity given by:
p > p0
p0
p < p0
Carol Johnstone
Notes: 5
5
5
5

## Slide 6
Linear vs. Higher Order Optics
Aaron Fawley | Synchrotron Design and Methodical Cell Optics Study
6
Large particle oscillations outside a stable, phase space area develop halo and beam loss on vacuum pipe and components.
Linear optics do not develop halo particles. Sextupoles distort the phase space ellipse, leading to particle loss at high amplitudes – this is known as a tune-shift-with-amplitude.
Phase-space diagrams (prod. with MAD-X)
Linear optics (without sextupoles)
Higher Order Optics (with sextupoles)
Notes: 6
6
6
6

## Slide 7
PUFF Cell Phase Advance Study
Aaron Fawley | Synchrotron Design and Methodical Cell Optics Study
7
PUFF – Particle Undulation Form Factor
Method to study higher order effects on particle orbits.
Can be normalized to dispersion and beta function at sextupoles to account for varying sextupole strength.
Notes: 7
7
7
7

## Slide 8
Dependence of Normalized PUFF on Cell Phase Advance and Sextupole Placement
Your Name | Title of your Presentation
8
| = Half integer resonance
| = Third integer Resonance
| = Sextupoles in every cell
| = Sextupoles in every other cell
| = Sextupoles in every third cell
Notes: 8
8
8
8

## Slide 9
Imaginary Transition Lattice
Aaron Fawley | Synchrotron Design and Methodical Cell Optics Study
9
Reference pathlength depends on the closed orbit trajectory determined by the dipoles.
Off-momentum depends on offset from the central trajectory as follows.
where
Transition – is the energy, t, all momenta have the same revolution time, and this represents a localized instability during the acceleration cycle.
Notes: 9
9
9
9

## Slide 10
Imaginary Transition Lattice
Aaron Fawley | Synchrotron Design and Methodical Cell Optics Study
10
Circumference = 563.57m
2 – 16 GeV protons
Power = (Intensity * Energy / Ramp Time) * Charge of Proton
Power = (5 (batches)*3.65E13 p/sec*120 GeV / 1.467s)*1.609E-19 C = 2.4 MW
Upgraded Linac will allow for even greater increases.
Notes: 10
10
10
10

## Slide 11
Imaginary Transition Lattice
Your Name | Title of your Presentation
11
PUFF plot for igtc lattice
*Normalized to beta function and dispersion at sextupole.
Notes: 11
11
11
11

## Slide 12
Sextupole Placement in RCS Lattice
Aaron Fawley | Synchrotron Design and Methodical Cell Optics Study
12
Sextupoles in every 3rd cell Sextupoles in every center cell
6 with sextupole, 1 without
Notes: 12
12
12
12

## Slide 13
Summary of Project
Aaron Fawley | Synchrotron Design and Methodical Cell Optics Study
13
Fermilab is in the planning stage for a new RCS for DUNE and other future experiments.
The PUFF metric developed in this study can be used to evaluate lattice optics in terms of machine performance which is particularly useful for next-generation transitionless lattices.
Applying PUFF to an RCS lattice design
guides choice of cell layout and properties
to optimize machine performance.
PUFF can be expanded to
develop a more rigorous estimate of
stable dynamic aperture and include a
metric for off-momenta performance.
*Poletip fields based on 3.25 in diameter beam pipe
**Injection based on multi-turn injection in previous ring
Email: afawley@services.fnal.gov
Notes: 13
13
13
13

## Slide 14
Backup Slides
Aaron Fawley | Synchrotron Design and Methodical Cell Optics Study
14
BACKUP
Notes: 14
14
14
14

## Slide 15
PUFF Cell Phase Advance Study
Your Name | Title of your Presentation
15
PUFF PLOTS of basic FODO lattice
Notes: 15
15
15
15

## Slide 16
Aaron Fawley | Synchrotron Design and Methodical Cell Optics Study
16
Phase-space at Transition
Left side of peak pre-transition
Right side post-transition
Jeff Eldred
Jeff Eldred
Notes: 16
16
16
16

## Slide 17
Aaron Fawley | Synchrotron Design and Methodical Cell Optics Study
17
Single Turn Injection Diagram

Horz and Vert cell tunes ~0.75 (270)
14 cells
For a 10m straight dispersion reached 10m
Sextupoles cannot be placed every cell considering injection/extraction
Sextupoles are 180 + integer apart every other cell
  Horz sextupoles every other cell
  Separate horz and vertical sextupoles
Travels off center through a focusing quad
Beam injects via a septum magnet
An electrostatic kicker is pulsed and puts the injected beam on the closed orbit
Carol Johnstone
Notes: 17
17
17
17

## Slide 18
Aaron Fawley | Synchrotron Design and Methodical Cell Optics Study
18
Single Turn Injection Diagram

Thin ferromagnetic steel plate separates injected beam trajectory from circulating beam trajectory
Single turn injection with kicker gap
  Can’t overlay identical beams
  This is the reason for H- stripping injection
Stray fields in the circulating region are common with a magnetic septum
  Electrostatic septa are weaker but no stray fields
Septum magnet concept
Beam injects via a septum magnet
X
Circulating beam trajectory
X
Injected beam
Carol Johnstone
Notes: 18
18
18
18

## Slide 19
Aaron Fawley | Synchrotron Design and Methodical Cell Optics Study
19
Single Turn Injection Diagram
  PAINTING VS SINGLE TURN INJECTION
  Two types of injection that do not involve charge changing
    a) Injection painting which fills a larger ellipse off axis.
    b) Beam injected off axis and a high voltage kicker kicks (x’) the one-turn injected beam on the reference trajectory usually N/2 in phase away from injection point.
3rd
1st
2nd
INJ
~0.25 machine tune, injection turn #
X
Kicker
Carol Johnstone
Notes: 19
19
19
19

## Slide 20
Aaron Fawley | Synchrotron Design and Methodical Cell Optics Study
20
Fermilab Accelerator Complex
Short Baseline Neutrino:
MicroBooNE, ICARUS, SBND
Long Baseline Neutrino:
NOvA, (LBNF/DUNE)
Muon Campus:
(g-2, Mu2e)
SwitchYard 120:
SpinQuest, test beam (FTBF)
A.Valishev
Notes: 20
20
20
20

## Slide 21
Aaron Fawley | Synchrotron Design and Methodical Cell Optics Study
21
PIP-II
An 800-MeV superconducting H-, CW-compatible Linac
Beam transport of 800-MeV H- from the SRF Linac to the Booster.
A new injection area in the Booster
Modifications to the Booster, Main Injector, and Recycler Ring to enable >1 MW power on LBNF target for 60-120 GeV.
Associated conventional facilities. The linac enclosure is compatible with upgrades.
A.Valishev
Notes: 21
21
21
21

## Slide 22
Aaron Fawley | Synchrotron Design and Methodical Cell Optics Study
22
Lattice Specification and Considerations
Normal Conducting
  1.5T for ramping
Required straight Sections
  RF
    Currently 11 straight sections, or 66 m total
    Dispersion suppressed or periodic placement of RF cavities
  Injection and Extraction
    10m straight section
    Single turn injection
      Assumes a separate accumulator ring for H- to proton conversion
Periodic Lattice
   24 cells, transition either < or > 2 GeV or transitionless
Notes: 22
22
22
22