## Slide 1: MTA Beam Line Commissioning
05/23/2011 Update

## Slide 2: Added Temporary SWIC Immediately Upstream of Experiment’s Collimator
New SWIC (S8) is read out using cables from MW5 and MW6 – chose to do this instead of pulling new cables.
Horizontal plane is read out through MW5; vertical plane is read out through MW6.
MW7 is approximately 20 feet upstream of S8.
H- beam is stripped as it passes through vacuum window, leaving a positive beam.
Able to steer beam using final bend.

## Slide 3: Added Two Correctors to Aid Steering
Added second Booster corrector to form dog-leg. This allows one to set position and angle on final focusing triplet.
Added additional dipole. Initial single dipole was inadequate to achieve 1.6 deg bend.
MW7
S8