## Slide 1: Thoughts on Photodetection Options for IOTA Andrey Elagin 07/24/2020

## Slide 2: Required Input to Find Optimal Solution
Expected photon rate
  I assume it’s low (e.g. <1kHz)
Maximum allowed dark count rate (photo-cathode induced noise)
Expected wavelength range
  My current assumption is ~1000 nm now and ~500nm later
QE
  I assume that 5-30% is acceptable
Required position resolution
  1/400, i.e. ~100mm for PLANACON-size device and 0.5-1mm for LAPPD-size
Required timing resolution
  Doesn’t seem to be important (but is, for example, 100ns OK?)

## Slide 3: Option 1: LAPPD with properly working 60-channel readout electronics
Expect ~700mm position resolution over 20x20cm (also single PE timing is ~50ps)
Cons:
Visible light only - can not be used for IR photons
Larger dark box is needed
Electronics is not ready yet
Pros:
There are several LAPPDs already at Fermilab
  E.g. Tile-51 was purchased from Incom with IOTA in mind
Huge progress on electronics over the last month
  Evan Angelico has done great job
  The same electronics is needed for ANNIE (now a dedicated firmware expert is working on it in UK)
  The same electronics is needed for the TOF setup at the TestBeam
I believe this is the fastest option IF visible light photons were available now

## Slide 4: Option 2: Acquire PLANACON-type device with cross delayed line anode (4 channels) through SSL Berkeley or Photonis
Expect <100mm position resolution over 5x5cm (timing varies)
Cons:
Could be expensive to get (working on estimate)
Potentially a long lead time order (will find out)
Pros:
Available in red and IR light
Smaller footprint for the dark box
Low number of electronics channels (e.g. 4)
Several ‘identical’ modules can be ordered
I believe this is the best option for red and IR photons

## Slide 5: Examples of photo-cathodes for the Option 2:

## Slide 6: Option 3: An actively pumped vacuum chamber with 2 Quantar sub-modules consisting of MCPs + the “four-corners” resistive anode. A custom Cs- Sb photo-cathode would be synthesized separately by UC ‘air-transfer’
Expect <100mm position resolution. Sub-module active area is ~3cm in diameter.
Cons:
Photo-cathode synthesis is tricky…
  QE won’t be high at the first try
  Unexpected delays are common when starting from
  scratch
Won’t be cheap (but it’s money for on-site labor)
Larger footprint for the dark box
Pros:
Could be a perfect match to UC goals to bring ‘air-transfer’ process to Fermilab
Tunable and adjustable if the requirements change
The ‘four-corners’ resistive anodes + MCP stack are available commercially
Low number of electronics channels
This would be very exciting for me, but it may not be the best option for IOTA