## Slide 1: Transduction for New Regimes in Quantum Sensing
Snowmass CPM - AF5 organization with contributors
Oct. 5, 2020
Emilio Nanni – nanni@slac.stanford.edu
LOI:
SNOWMASS21-IF1_IF2-AF5_AF7_Nanni-162
Heinz, Nanni, Safavi-Naeini, Schleier-Smith, Welander

## Slide 2: Efficient Quantum Transduction Needed to Link Quantum Systems
  Quantum computing at 102 qubit scale; needs 106 qubits for applications
  Efficient optical quantum memory systems; leading QC candidates are superconducting microwave qubits
  Quantum advantage (ADMX, DM Radio, CASPER) of dark matter detectors up to 10s µeV scale Dark Matter BRN goes to meV
  A scalable solution: utilize nonlinear high-kinetic inductance materials
    Two pump photons, ωp = (ωmm − ωµwave)/2 , combine with microwave photon to produce a mm-wave output
Google
M. Pechal, et al. Phys. Rev. A 96, 042305 (2017).
106-109 Increase in Conversion Efficiency
Four-Wave Mixing Transduction

## Slide 3: Transduction for New Regimes in Quantum Sensing
Exploring mm-wave regime as an intermediate quantum transduction channel between microwave/optical devices and quantum sensors
Transduction allows for sensing at higher frequencies, higher operation temperature, very high quantum efficiency, fast measurement, large bandwidth
Theory of Quantum State Transduction: Three coupled nonlinear resonators
Pechal and Safavi-Naeini, Phys. Rev. A 96, 042305 (2017)
First mm-wave superconducting resonators
Preparing to test multi-frequency resonators
Microwave photon in
mm-Wave photon out
mm-Wave pump
Developing microwave input air-gap capacitor
X-Wing
Y-Wing
~50/100 GHz
Multani, Stokowski, Das
Notes: Bottom Right: False color SEM of air-gap capacitor in development
blue = Nb top plate,
Red = silicon dioxide (capacitor dielectric/sacrificial layer for releasing)
cyan = Niobium GND plane
green = contact pad
Funds Received $490k covers full period of award FY20/FY21
No deviation from expected budgetary expenditures or from proposed scope

## Slide 4: Opportunities in the Emerging QIS Landscape (1/3) RF and Cryogenic Instrumentation
Strong connections between QIS and accelerator technology
  Leveraging accel. fabrication capabilities for vacuum/cryo windows, waveguide, cavities, coatings
Partnering w/ QIS leaders to pursue new opportunities:
3D SRF Cavities
w/ Thin Films
van Bibber
Vacuum/cryo windows from mm-wave accel. R&D
mm-Wave Mediated Atomic Transitions
Zhang, Schleier-Smith
Research Technology for QIST
QIS-based Quantum Devices
Feedback to Accelerator R&D: Improved SC films and cavity coatings; low-loss mm-wave/THz waveguides and mode convertors
Notes: trap cold atoms in high-Q superconducting mm-wave Fabry-Perot
induce strong coupling between cavity mode and resonant atomic transition
cavity mode mediates effectively nonlocal atom-atom interactions
applications to quantum computation and simulation

## Slide 5: Opportunities in the Emerging QIS Landscape (2/3) System Architecture and Test
High Capacity Dilution Refrigerator (Support single cell L-band Cavity)
As technology develops we should be the first to utilize it
Sources of high quality devices coming online (SLAC = DMF/Nano-X)
Infrastructure for multiple cryogenic systems
Investigate Q-LAN for experiments in distributed computing, communication and sensing
Fiber-linked and networked quantum data center
Integrate Process Development for Tools in Nano-X and DMF
Bluefors LD400
Cryogenics Lab Layout at SLAC:
Occupancy w/ 5 Large Volume Dilution Units
One unit on site; Q-NEXT has funding for additional two

## Slide 6: Opportunities in the Emerging QIS Landscape (3/3) Sources of Entanglement & Precision Beams
Source of Entanglement:
Entanglement of photonic sources can provide dramatic enhancement in sensitivity (quantum illumination)
Explore implementing w/ e- beams
  Purcell-like enhancement of multi-photon transitions between Landau levels
arXiv:1910.12277
Demo e- beam generation of Color-Centers
Vuckovic
Defect Creation:
SiV-SiC defects created by MeV e- beams as a qubit platform
Challenge – precision placement (<100 nm) and coherence