## Slide 1
George Lolov
8/20/2020
Simcenter Ansys Integration
TSD Topical Meeting

## Slide 2: Relevant Files (Uploaded to Sharepoint)
Start with just original part and follow along
Compare your results to .fem and .sim files at the end

## Slide 3: Choosing the Correct NX License
Remove NX license bundles
Add Simcenter (SC) license bundles
Make sure no parts are loaded yet or the “select bundles” option will not appear

## Slide 4: Open The NX Geometry and Enter Pre/Post Application

## Slide 5: Create a New Fem and Simulation

## Slide 6: Select Correct Dialog Info for FEM/SIM Creation
Select ANSYS as solver
Choose correct analysis type (structural in this case)
Make sure to create an idealized part to work with so that the original part remains unchanged

## Slide 7: Promote Geometry to be Analyzed
Make sure you are working with the idealized part (i.prt)

## Slide 8: Prepare Geometry for Meshing
In this case, bolt head/washer faces were sketched on the top/bottom of this geometry (use “divide face” to make them separate faces)
Make any idealizations in the modeling application

## Slide 9: Using Divide Face to Create Bolt Head/Washer Faces
Select which faces you’d like to divide (highlighted in orange)
Select the sketch/objects you’d like to use to divide the faces (sketched circles in this case)

## Slide 10: Bolt Head and Washer Faces Now Divided
Bolt Heads
Washers

## Slide 11: Transitioning Over to FEM
After idealization is complete, go to the Pre/Post Application
The easiest way to switch to the .fem is via the window selection dropdown
Once at the FEM, begin with the big 3…

## Slide 12: Managing Materials Used in Model
If the materials needed aren’t in the library, create custom materials by putting in the relevant info (density, YM, Poisson’s)

## Slide 13: Solids
Use property manager to create physical properties for solid elements
Simply name the solid elements

## Slide 14: Pretension Elements: Used to Apply Preload
Leave force value as 0 for now (preload will be specified later)

## Slide 15: Mesh Collector: Organizing Mesh Types
Mesh collectors are used to group meshes of the same type and material

## Slide 16: 3D Solid Element Mesh Collector
Choose material from dropdown if custom, or from library
Select solid physical property from dropdown
Name the collector

## Slide 17: PRETS179 Mesh Collector (Preload Beams)
Same for preload mesh collector (PRETS179 elements)
Choose bolt material and PRETS179 property created from before

## Slide 18: MPC184: Rigid Spider Links
Multiple Point Constraints (MPCs) are spider elements that will connect our bolt shaft (PRETS179) to the bolt head and washer faces
Need only specify material (bolt material) and give them a name

## Slide 19: 2D Shell Elements: Used for Seed Meshes
2D shell elements are not actually used in the model (in this case), just used to improve mesh
Properties/material does not matter for these

## Slide 20: Attempting to Mesh: 3D Tetrahedral Only
Select the bodies to be meshed
Use SOLID187 (Parabolic elements) for most accurate results
Change element size (and other settings) as needed
Don’t do this part yet

## Slide 21: Mesh Looks Good…But Could be Better
Hit ctrl+z if you created this mesh

## Slide 22: Use a Seed (Shell) Mesh on Fine Detail Areas
Create a seed mesh on the bolt/washer faces
Change element size/meshing method to produce a nicely distributed mesh
Remember to select the correct collector to group mesh under

## Slide 23: Create Seed Meshed on Other Important Areas
Make sure this is checked for curved surfaces

## Slide 24: Create Seed Meshes on Contact Areas as Well
Best practice is to seed mesh both contact faces together so the meshes are uniform

## Slide 25: Seed Meshes are Not Used in the Model
UNCHECK this option as the seed meshes will NOT be part of the model (only used to make 3D mesh better)
Highlight all seed meshes and right click

## Slide 26: Now Create a 3D Tetrahedral Mesh
Looks much more uniform than before

## Slide 27: Perform an Element Quality Check
Highlight all 3D meshes and check quality
Warning elements are OK, but refine mesh if any failed elements

## Slide 28: Setting up Preload: Create Center Nodes
Create center nodes at each bolt/washer location
Name them something convenient so easy to distinguish

## Slide 29: Create Bolt Shafts with PRETS179 Elements
Select top/bottom node (1 source, 1 target) and create PRETS179 beam

## Slide 30: Specify Pretension Node for PRETS179 Elements
Pretension node defines direction of preload
Node will need to be created somewhere in model
Resource

## Slide 31: Create MPC Spider Elements to Bolt/Washer Faces
Source is center node, target is nodes on face

## Slide 32: Change Key Options for MPC Meshes
MPC184 Info

## Slide 33: FEM Complete

## Slide 34: Create a Simulation (sim) File
Make sure to select ANSYS environment

## Slide 35: Click Through .sim Creation Dialogue

## Slide 36: Setting Up Boundary Conditions
In this case the bottom edges were fixed

## Slide 37: Applying a Bolt Preload Force
Select the 4 PRETS179 beams
Sign of force depends on pretension node and direction specified when creating PRETS179 elements earlier (in this case sign is negative for compression)

## Slide 38: Specifying Contact Areas
Manually select the source/target faces (interchangeable)
CONTA174 and TARGE170 elements created

## Slide 39: Exporting Model Data to ANSYS .inp file
As there is no ANSYS license associated with Simcenter, analysis will not solve
However, ANSYS input file will be written in model directory

## Slide 40: Open ANSYS Mechanical APDL Product Launcher
Make sure correct license is selected (depends on analysis type)
Select model directory and give job a name

## Slide 41: Load Model .inp File into ANSYS APDL

## Slide 42: Solving Through ANSYS
Analysis will solve through ANSYS and output will be a .rst file in working directory (the largest .rst file)

## Slide 43: Loading Results File into Simcenter
In the .sim file, right click on Structural under Results and click Specify
Specify location of .rst file and click OK
Double (left) click on Structural to display results

## Slide 44: Results are Displayed
Results are in dropdown bar on left side
Expand dropdown and double click on a result to see it

## Slide 45: Refine Contour Plot for Better Visuals
Play around with display options for better contour plots

## Slide 46: Good References
Use ANSYS Help manual for any element type questions (like those hyperlinked earlier)