## Slide 1: Status of High Pressure gas filled RF cavity beam test
K. Yonehara

## Slide 2: Goal of HPRF beam test
Study beam loading effect in dense hydrogen gas filled RF cavity by observing
modulation of RF pickup signal & optical signal during beam on & off with
various conditions

## Slide 3: First beam run plan
Beam intensity dependence
Gas pressure dependence
Gas species dependence
  H2, N2, He
  H2 + electronegative gas
Full linac beam intensity = 7 1012 protons/pulse @ 60 μs
Beam rep rate = 1 pulse/min
Total beam running time = 12 hours
# of beam pulses = 720 pulses

## Slide 4: MTA beam line and experimental apparatus
400 MeV
H- beam
Elastic scattered proton from
vacuum window (~20 events/pulse)
No energized device within 15 feet from HP cavity due to
hydrogen safety issue
Beam must be stopped in the magnet due to radiation safety
New apparatus:
New HPRF cavity
Collimator + Beam absorber
Luminescence screen + CCD
Beam counter
RF circulator + damper
(Ti)
Bound electrons of H- will be
fully stripped in the vacuum window
Ex) Thickness = 4.5 g/cm3 × 0.005 = 0.023 g/cm2
Stripping cross section ~ 10-18 cm2
0.023/47.9 × 6.0 1023 = 3 1020
3 1020 10-18 = 300 strip collisions
4
Beam intensity in the cavity is tuned by collimator and triplet
Triplet (7.3 meter upstream
from collimator

## Slide 5: New HPRF cavity and collimator
Current cavity is operated in low pressure region (≤ 1000 psi) due to pressure safety
  Commissioning cavity at 2nd RF station for beam test
  Investigate plasma-electron dynamics in breakdown
Plan to increase MAWP to 1600 psi for beam test
  Met new safety code
  Need to upgrade gas manifold system
Collimator
HPRF cell
RF coax line
beam
beam
Gas
inlet
RF
inlet
Support rail
Luminescence
screen
Loaded Q = 7,200

## Slide 6: Simulated residual dose level in experimental apparatus
collimator
RF cavity
Beam absorber
Surface residual dose rate at collimator
(red & blue) and Cu electrode
Inject full intensity linac beam for 1 beam pulse/min
12 hours operation
Less than 102 mrem/hr at 1 ft after 1 wk cooling
  → Class II radioactive material
  → Allow to remove apparatus without big issue

## Slide 7: Beam profile monitor
Snap shot of screen
Horizontal
Vertical
SWIC (cannot use for Hydrogen run)
Both beam profile
measurements show
very wide beam profile

## Slide 8: Collimator toroid signal
Chart: 
| 0.0195294117647059 | 0.0067 | 0.00473333333333333 | 0.00296078431372549 | 0.00206666666666667 | 0.00157
Max. Toroid Voltage vs Current | 0.0728 | 0.0288 | 0.0216 | 0.0144 | 0.012 | 0.0096
Downstream Toroid
pu volt (V)
Reference Current (A)
Upstream Toroid
Downstream Toroid
From reference curve, Downstream toroid pu voltage (V) = 3.5049 × Reference I + 0.0046
Measured toroid pu voltage = 0.007 ~ 0.009 V
Then observed current = 0.0007 ~ 0.0013 A
Beam intensity = (Observed I) 1.2 10-5 (s) /e = 5 ~ 9 1010 protons
We need better calibration since observed toroid pu voltage is lower
than the reference toroid voltage
Use well-calibrated toroid pickup (but slow response) and calibrate
fast response hand-made toroids

## Slide 9: Circulator + load
Load
Circulator
Cavity
RF Pickup#2
RF Pickup#1
Forward
Reflect
RF Pickup#2
Forward
Reflect
No load
With load
Circulator+load cleaned up
RF signals

## Slide 10: Current issue
Major upgrade of MTA beam line
  Expect delay ~ 2 wks
Hydrogen safety approval
  Need to pass all requirements related with hydrogen safety
    Cable configuration/assignment/termination
    15-foot-rule, LOTO
High pressure test
  Current MAWP 1,000 psi -> 1,600 psi for beam test
Fix/upgrade device
  Beam counter
    One channel is broken
  Toroid beam intensity monitor
    Better calibration
  Fix RF pickup probe
    Electric pickup probe has leak
  Optical system
    Voltage distribution box
    Replace to SiPM

## Slide 11: Summary
Physics rich program
  We have a strong physics analysis team
Almost all devices work properly
Concerning about major upgrade of MTA beamline
  We missed a connection between users and beam line designers
  I think that we have a rigid plan now
Hydrogen safety also needs to be done asap
  Keep contacting with Jim Kilmer to call for hydrogen safety inspection
We almost make it!

## Slide 12: Collaborator
Jana Mukti, Giulia Collura, Alan Bross, Ben Freemire,
Giovanni Pauletta, Yagmur Torun, Pierrick Hanlet, Leo Jenner,
Ajit Kurup, Dan Kaplan, Dave Neuffer, Gennady Romanov,
Moses Chung, Andreas Jansson, Alvin Tollestrup, Steve Geer,
Al Moretti, Rolland Johnson, Mike Neubauer, Gene Flanagan,
Masahiro Notani, Grigory Kazakevitch, Katsuya Yonehara