## Slide 1: MTA Update
6/6/2011

## Slide 2: Beam Line Changes and Calculations
UVB03
  Last vertical bend is 1.4 degrees (0.025 radian), based on survey.
  Require IDV to run at ~30 Amps.
  Possible with 150 Volt bulk supply.
UTH10/UTV10 Dog Leg
  With 150 Volt bulk, can achieve about 18 A, or 8 milliradian bend.
  Separation is 67”, which allows 14 mm movement; tune of 6/3/2011 put beam at -7 mm on Q10.

## Slide 3: Work List
UVB03
  Procure.
  Upgrade bulk.
  Add to ramp card.
  Change power supply type.
  Design and fabricate stand.
Dog Leg
  Add control card.

## Slide 4: Schedule
UVB03
  EE support – estimate one week.
  Mechanical support – estimate two weeks (design, review, procure, fabricate).
  Controls – estimate one week.
Dog Leg

## Slide 5: Resources
EE support – oversee electrician.
Mechanical support – coop student, 60%.
Controls – investigating.