## Slide 1
PIP2 ACLK Preliminary Design Review
Timing System Introduction
Gregory Vogel
AD/Controls
7 December 2021

## Slide 2: PIP-II Timing System
Introduction
The PIP-II Linac will be part of a larger accelerator complex involving 4 synchrotrons and associated beamlines supplying particle beams to high and low energy neutrino experimental areas (LBNF, LArTF & SBN), muon experimental areas (g-2 & Mu2e) and the experimental test areas fed via Fermilab’s Switchyard (Mtest, Mcenter & SpinQuest). It will be the task of the PIP-II Timing System to coordinate the operation of both the Linac and the rest of the accelerator complex by the distribution of the required clocks, machine resets, triggers and system state information.
  The repetition rate of the Linac beam pulse (macro pulse) will be 20 Hz.
  The macro pulse request (Booster Beam Resets) must be synchronized to the 60 Hz Booster mains frequency.
  The timing system will distribute timing system information (via ACLK, TCLK or LCLK) to all relevant machine locations.
  All PIP-II Timing System design & development is performed in accordance with all applicable Fermilab Standards (FESHM, FEM, FQAM, etc.)
  This review is of the ACLK subsection of the PIP-II Timing System.

## Slide 3: PIP-II Timing System Simplified Block Diagram

## Slide 4: PIP-II LINAC Timing System
The PIP-II timing system is planned to be a two part system. The first part is a global timing system (here called ACLK) that provides high level, event based timing for the whole Fermilab accelerator complex while the second part is a RF synchronized clock system unique to the PIP-II linac itself (here called LCLK). This two level clock system concept has been used at Fermilab (TCLK & individual machine Beam Sync Clocks) to support complex operations for over 30 years through both the Tevatron and Neutrino operational eras. This concept provided significant operational flexibility that allowed for the successful completion of both the Tevatron Collider and Minos Experimental runs, with both programs operating in parallel.
The two systems are planned to have similar hardware, with the LCLK generator hardware being a simplified version of the ACLK system. This is due to the LCLK Generator not requiring an interface with a Timeline Generator (TLG) to configure operational scenarios for the entire accelerator complex. It also does not require interfaces with other machine Beam Synchronous clocks, other machine Beam Permit Systems, Booster Reset timing signals, GPS receivers and various line locked inputs from a Master Clock Oscillator (MCO). It will also only be generating approximately 30 clock events versus the 200 events required on ACLK.
PIP-II Source, Linac, BTL and Booster Injection systems are expected to use LCLK as their clock system due to its beam synchronous nature.

## Slide 5: PIP-II LINAC Timing System
The systems are planned to have common Fanout and Decoding hardware.
General purpose clock decoders are expected to be designed in a PMC format comparable to the PMC-UCDs presently used for TCLK decoding by front ends around the complex and as a FPGA design that can be included in other designs.
The ACLK System will make use of an external 10 MHz signal source as a reference for its 650 MHz phase lock as it is the reference frequency for the TCLK output of the system (needed to support legacy hardware around complex).
LCLK will use a PIP-II Linac RF reference (162.5 MHz) from the Linac LLRF system to allow beam synchronized event placement. Appropriate TCLK/ACLK events will be decoded and reflected onto LCLK to support AD/Control System based data acquisition.
Both the ACLK and LCLK systems will have a clock output with a data frame of 16 event bits + 32 data bits with frames broadcast at 650 MHz, phase locked to the 10MHz reference in the case of ACLK and the PIP-II LLRF sourced 162.5 MHz reference in the case of LCLK.

## Slide 6: PIP-II LINAC Timing System
There will be console based applications developed to provide operator interface and system configuration for both systems.
  The ACLK system will have a significant software effort due to its required Timeline Generator (TLG) application and front-end code along with the UCD front-end code.
  The LCLK system will have minimal software associated with it. It is predominately a hardware system.

## Slide 7: PIP-II Timing System Common Hardware
The following hardware is planned to be common between the ACLK and LCLK-II systems. It is expected that this hardware will likely be used as part of ACORN (a recently initiated Accelerator Control System upgrade project) as well.
  LCLK/ACLK Fiber Fanout Units
  LCLK/ACLK Local Fanout Units
  MFTUs
  LCLK/ACLK PMC?-UCD
  LCLK/ACLK FPGA Decoder

## Slide 8: ACLK General Requirements
Highly reliable, fail-safe operation;
Compatible with the staged PIP-II commissioning;
Capable of logging and time stamping all changes of its state;
Capable of triggering loss of MPS/beam permit events to allow post mortem fault analysis
Restricted, documented privileges to access and modify configurations;
Expandable in order to support modifications and future upgrades such as new operational scenarios without major modifications
Events capable of being individually enabled/disabled
16 bit event + 32 bit data packet (total 48 bits of data in event frame)
Event data phase locked to 10 MHz external GPS disciplined reference
Standard encoding scheme (Modified Manchester)
TLG front end with console application and MDAT transmitter
UCD front end with console application (2)
Synchronized TCLK transmission (legacy accelerator hardware support)
ref: ACLK TRS (ED0013499)

## Slide 9: ACLK Clock System
ACLK will be sourced via a single Clock Generator and transmitted on optical fiber to the AD Computer Room, the PIP-II LCLK Generator Rack in the PIP-II source area and the AD MAC Room. The ACLK generator will also provide a TCLK output.
The ACLK source will be supplied with and decode LCLK, MIBS and RRBS.
ACLK will use a 10 MHz, GPS disciplined reference to provide synchronization for both its 650 MHz ACLK output and its 10 MHz TCLK output.
The ACLK system will have a single clock output with 16 bit event + 32 bit data field with frames broadcast at 650 MHz, phase locked with the 10 MHz reference. Some clock events will be reflected from the accelerator clock systems (LCLK, MIBS & RRBS).

## Slide 10: ACLK Clock System
All events on ACLK will be synchronized to (launched on the rising edge of) the 10 MHz external reference.
ACLK will broadcast reflected LCLK sourced beam events (Macro Pulse & Bunch markers, ACLK reflected events will not be beam synchronous).
ACLK will broadcast MPS sourced events (fall of various Beam Permits, Beam Permit Reset Events, etc.)
ACLK will broadcast MCO triggered/sourced events (20 Hz, 720 Hz, 1 Hz, BMIN, TPTS & variable rate).
ACLK will broadcast BSSB triggered events (pulse shift permitted, pulse shift inhibited, Linac study shift permitted, etc.)

## Slide 11: ACLK Input Sources
Main Injector Beam Sync Clock (MIBS)
Recycler Beam Sync Clock (RRBS)
LCLK
Booster Extraction Sync (BES from Booster LLRF)
Machine Beam Permits
  Main Injector
  Recycler
  Booster
  LBNF
  Muon
  Switchyard
  PIP-II MPS
Beam Switch Sum Box (BSSB)
10 MHz GPS Sync’d Reference Oscillator
Master Clock Oscillator (MCO)
Timeline Generator (TLG)

## Slide 12: ACLK Block Diagram

## Slide 13: ACLK Prototype Block Diagram

## Slide 14: ACLK Hardware
ACLK Generator Unit (2)
  Main (MAC Room) & spare/development system
TLG Front End (2)
  Main (MAC Room) & spare/development system
UCD Front End (3)
  2 Main (AD Computer Room) & spare/development system
ACLK Fiber Fanout Unit (?)
  ? In MAC Room, (1 in Linac LCLK Rack?)
ACLK Local Fanout Unit (?)
  1 unit in LCLK Rack
ACLK decoders (TBD)
  MFTUs (?)
  PMC-UCD (TBD)
  FPGA Design

## Slide 15: ACLK Software
TLG Software
  Front End Application & Console Application
  Based on existing system software (D69 & FE app)
UCD Software
  Front End Application & Console Application
  Based on existing system software (D33 & FE app)
ACLK Generator Interface Application
  Console Application
  Based on existing system software (T61)
  Allows enabling/disabling of individual clock events
  Allows delay setting for clock triggered events
  Allows manual triggering of individual clock events

## Slide 16: ACNET TLG System

## Slide 17: ACNET UCD System

## Slide 18: ACNET Clock Interface

## Slide 19: ACLK Cost & Basic Schedule
M&S $250,833
Labor 7294 manhours
Preliminary Design FY22
Prototype Design FY22-FY23
Hardware Procurement begins FY23
Assemble & Test Prototype System FY23
Final Design FY23-FY24
Assemble & Test Final System FY25
PIP-II Warm Front End Commissioning FY26
Note: Work on ACLK is interleaved with LCLK Development

## Slide 20
PIP2 ACLK | PDR
12/7/2021