## Slide 1: SWFA demonstrators with integrated technologies for future large-scale machines
Goal: Demonstrate technology integrations needed for large-scale SWFA-based machines (steppingstone facilities and ultimately linear colliders)
Key performance of one module (20 total) | 
Accelerator concept | Two Beam Acceleration
RF power from decelerator | 26 GHz, 1 GW
Accelerating gradient | 270 MV/m
Main beam energy gain | 150 GeV
Staging acceleration | 50 stages, 38 ACCs/stage
AC-to-RF efficiency | >30%
3-TeV Argonne Flexible Linear Collider (AFLC)
500 MeV demonstrator
2 stage, 2 structures/stage
3 GeV demonstrator
4 stage, 6 structures/stage
13 GHz main beam, 20% η
3 GeV demonstrator
30% η with advanced klystron
5-GeV Multi-beam XFEL
Key performance of one beamline (10 total) | 
Accelerator concept | Collinear Wakefield
Transformer ratio | 5
Accelerating gradient | 100 MV/m
CWA energy doubler
180 GHz, 2 structures
SWFA roadmap

## Slide 2: SWFA demonstrators with integrated technologies for future large-scale machines
500 MeV demonstrator fitting into AWA’s current bunker
70 MeV drive beam to two stages
2 x 8-bunch trains, 40 nC/bunch
Decelerated to 20 MeV by 2 PETS in each stage
15 MeV main beam
Single bunch
Accelerated to 500 MeV by 4 accelerators
14.5 m x 1.5 m testing area at AWA
Key technologies integration: 1) high charge drive beam generation and transportation; 2) advanced wakefield structure; 3) high fidelity staging acceleration
CWA energy doubler fitting into AWA’s current bunker
40 MeV drive beam
100 MeV main beam
50 MeV shaped drive beam
50 MeV main beam
Key technologies integration:
1) high charge drive beam shaping; 2) high frequency structure with BBU control; 3) staging acceleration
A. Zholents et al. IPAC2018
J. Shao et al. NAPAC2019