## Slide 1: Short-pulse wakefield structure R&D for high gradient and high efficiency acceleration in future large-scale machines
Goal of LOI: Identify directions of structure R&D to increase gradient and efficiency in short-pulse wakefield acceleration
Advanced structure R&D
High gradient
(0.3-1 GeV/m)
High efficiency
(AC-to-RF >30%)
High group velocity
High shunt impedance
Dielectric loaded
Metamaterial
Most developed, simple geometry, low cost
Dielectric disk
Target: Develop fully functional structure for TeV-scale linear collider
X. Lu et al. PRL 122, 014801 (2019)
B. Freemire et al. To be published

## Slide 2: Short-pulse wakefield structure R&D for high gradient and high efficiency acceleration in future large-scale machines
mm-wave/THz structure R&D enabled by advanced fabrication
GV/m capability
Target: Develop mm-wave/THz conceptual layouts and technology for linear colliders
400 GHz dielectric-loaded structure
180 GHz metallic disk-loaded structure
320 MeV/m
Under development
Fundamental gradient limits study with short RF pulse
RF breakdown
Multipacting
Field emission
Others
X-band single-cell powered by 9 ns RF pulse, no breakdown at 250 MV/m acc gradient*
* Preliminary result
Target: Explore and understand fundamental limits in short-pulse regime
B.D. O’Shea et al. Nat. Commun. 12763 (2016)
A. Zholents et al. IPAC2018