## Slide 1: Photonic Crystal (PhC)-based Dielectric Laser Accelerator (DLA)
G. Torrisi1, L. Celona1, S. Gammino1, G. S. Mauro1, D. Mascali1, G. Sorbello1, 2,
A. Locatelli3,4, C. De Angelis3,4,
A. Gallo5, M. Bellaveglia5, M. Diomede5, L. Piersanti5,
G. Della Valle6,
A. Bacci4
1INFN-LNS, Catania, Italy
2University of Catania, Catania, Italy
3University of Brescia, Brescia
4 INFN-LASA, Milano, Italy
5 INFN-LNF, Frascati, Italy
6 Politecnico di Milano, Milano, Italy

## Slide 2
Laser
beam
2D longitudinal Photonic Crystal
Directional Coupler
Photonic Crystal (PhC)-based Dielectric Laser Accelerator (DLA)
LoI Core Ideas:
Hollow-core waveguides for high power handling
High interaction impedance Zc and accelerating gradient
Continuous wave (CW) laser operation (1-5 µm)
Collinear co-propagating laser and beam
Sub-wavelength features for sub-relativistic particles
Integrated nano-proton-source for proton-DLA
beam
o
TM01
TE10
DLA high-Q photonic-crystal cavity
[courtesy of C2N]
RFQ-like 2D Longitudinal PBG
for tabletop proton-DLA
modulation of the
dielectric “electrode”
3D Silicon Woodpile mode launcher
beam
o
TM01
TE10
TE10
3D woodpile mode converter side-coupler
Laser
beam
Notes: I can certainly refer to Joel's slides on DLA on chip since the goal and the concept are the same:
a cost-effective tabletop dielectric accelerator: based on a laser-driven optic-integrated chip.
In our LoI we propose dielectric Photonic Crystals (PhC) hollow-core waveguides
since such “interaction structures” can support a suitable synchronous electromagnetic guided mode or resonant mode capable to accelerate charged particles.
This interaction structures can be also viewed as an alternative to the transversely illuminated PRD configurations which have an intrinsically limited interaction length, because they require a plane wave that impinges laterally throughout the whole structure's length [2, 3].
structures consisting in a collinear structure that employees the same path for the accelerating electromagnetic field and for the particle beam
In order to have both high laser-induced accelerating gradients and adequate interaction length, it could be very helpful to use extended accelerating structures (with possibly co-linear propagation of the accelerating electromagnetic field and the particle to be accelerated [5]).
In particular, in presence of guided modes or resonant cavity modes, the interaction can be extended on relatively long distances in order to achieve adequate final energies.
Si possono commentare le differenze tra i due couplers: guida TLC ed ACC parallele in un caso
ortogonali nell’altro: convesione completa del modo da TLC ad ACC
once the conversion has taken place
The coupler satisfies the following requirements:
the input waveguide perpendicularly couples the power propagating in the TE10-like mode of the waveguide into the accelerating TM01-like mode of the beam channel
it excites only the fundamental accelerating mode having an excellent uniformity, avoiding higher order modes
it can handle high power without breakdown being based on an hollow-core diel
- Different interaction structures for different particle velocity.
low beta ( 0.02< 𝛽<0.5) section of the integrated DLA :
Silicon On Insulator (SOI) wafer to form subwavelength grating slot waveguides (

## Slide 3
woodpile
copper box
high speed and precision dicing saws
silicon wafers 850 µm thick with resistivity > 3 kΩcm
stacking together 9 silicon layers
geometrical tolerance of 10 µm
Simulated vs Experimental
S-parameters
Silicon woodpile waveguide
Fabrication & cold test at scaled mm-wave frequencies
TEAM
INFN-LNS, INFN-LNF, UniBs & UniCT: Accelerator design
PoliMi, Politecnico di Milano: Laser Source
INFN-LASA: beam dynamics
C2N, CNRS,Université Paris-Saclay design & manufacturing
Manufactured dielectric PhC woodpile structure
waveguide port