## Slide 1: Active Plasma Lenses
1
Snowmass AF6 meeting
September 24th, 2020
Office of Science
S. K. Barber1, J. van Tilborg1, A. J. Gonsalves1, S. Steinke1, K. Nakamura1, C. G. R. Geddes1, C. B. Schroeder1, E. Esarey1, M. Ferrario2, R. Pompili2, C. A. Lindstrøm3, J. Osterhoff3, and H. Milchberg4
1Lawrence Berkeley National Laboratory, Berkeley, California 94720, USA 2Laboratori Nazionali di Frascati, 00044 Frascati, Italy 3Deutsches Elektronen-Synchrotron DESY, Notkestraße 85, 22607 Hamburg, Germany44 4University of Maryland, College Park, MD 20742, USA
Notes: 12.54am
1.18am (24 minutes)

## Slide 2: Active plasma lens an “old” concept for ion beams1. Excellent complement for plasma accelerated beams
2
Office of Science
r
J
r
B
~ r
~ 1/r
R
R
e-beam
Discharged capillary
Ampere’s law
Uniform current
Example: D=0.5mm, L=3cm, I=430 A
1400 T/m, F=4cm for 500 MeV electrons
Active Plasma Lens
Radially symmetric focusing
Tunable, up to ~1 kA (“active”)
Gradients >3000 T/m (!)
Compact
1Panofski et al. RSI 1950
van Tilborg et al. Phys. Rev. Lett. 115, 184802 (2015)
Notes: 12.54am
1.18am (24 minutes)

## Slide 3: Many potential applications for APLs in HEP related areas
3
Office of Science
Areas of Impact
Inter-stage transport for multi-stage plasma accelerators1
  5GeV+5GeV experiments planned at BELLA using APL, groundwork for collider
Final focus of collider
  symmetric focusing reduces chromatic effects, potentially more compact system
High gradient positron focusing
New diagnostics specifically tailored to LPA environments2
  specialized diagnostics improve beam characterization
Facilitates rapid research on complex topics
Future APL specific developments
Increased discharge repetition rates needed for collider (currently ~Hz need ~kHz)
High rep rate, ultra thin plasma mirror for laser/electron beam separation
Continued study of emittance growth from scattering, wakefields, current in-homogeneity, etc.
1Steinke et al. Nature 2016
2S. K. Barber et al. Appl. Phys Lett. (2020)
Notes: 12.54am
1.18am (24 minutes)