## Slide 1
Laser-Plasma Accelerator Linear Collider
C. B. Schroeder∗1, F. Albert2, C. Benedetti1, J. Bromage3, D. Bruhwiler4, S. S. Bulanov1, E. M. Campbell3,
N. M. Cook4, B. Cros5, M. C. Downer6, E. Esarey1, D. H. Froula3, M. Fuchs7, C. G. R. Geddes1, S. J. Gessner8,
A. J. Gonsalves1, S. M. Hooker9, K. Krushelnick10, R. Lehe1, W. B. Mori11, K. Nakamura1, J. Palastro3, M. Palmer12, J. Power13, B. A. Shadwick8, M. Thevenet14, A. G. R. Thomas10, J. van Tilborg1, N. Vafaei-Najafabadi15, J.-L. Vay1, S. Webb4, T. Zhou1, J. Zuegel3
September 23, 2020 - AF6 LOI Meeting – Collider Concepts Session
1Lawrence Berkeley National Laboratory, Berkeley, California 94720 USA
2Lawrence Livermore National Laboratory, Livermore, California 94550, USA
3University of Rochester, Laboratory for Laser Energetics, Rochester, New York 14623, USA
4RadiaSoft LLC, Boulder, Colorado 80304, USA
5CNRS, LPGP, Universit ́e Paris-Saclay, 91405 Orsay, France
6Department of Physics, University of Texas, Austin, Texas 78712, USA
7Department of Physics and Astronomy, University of Nebraska, Lincoln, Nebraska 68588, USA
8SLAC National Accelerator Laboratory, Menlo Park, California 94025, USA
9Department of Physics, Clarendon Laboratory, University of Oxford, Parks Road, Oxford OX1 3PU, UK
10Center for Ultrafast Optical Science, University of Michigan, Ann Arbor, Michigan 48109, USA
11Department of Physics and Astronomy, University of California, Los Angeles, California 90095, USA
12Accelerator Test Facility, Brookhaven National Laboratory, Upton, New York 11973, USA
13Argonne National Laboratory, Lemont, Illinois 60439, USA
14Deutsches Elektronen Synchrotron, Notkestraße 85, 22607 Hamburg, Germany
15Stony Brook University, Department of Physics and Astronomy, Stony Brook, New York 11794, USA

## Slide 2
Basic configuration of a laser-plasma-based linear collider
Preliminary designs that yield required IP parameters have been produced to guide R&D
R&D focus has been on developing laser-plasma accelerator technology
Integrated design study needed
Linac: staged laser plasma accelerators (LPAs):
Design (optimizing operational plasma density) yields 5 GeV/stage (100 stages/linac for 1 TeV):
    Compact laser coupling between stages yields geometric/average gradient = 2.3 GV/m
Time structure at IP:
    single bunches, separated by 20 μs
Short (~10 μm rms) beams:
    beamstrahlung reduction (reduces power):
    𝞂z< β*
Flat or round beams may be accelerated
Laser energy recovery possible for high efficiency
Key characteristics of a LPA-based collider:
2
Leemans & Esarey Phys. Today (2009)
Main advantage of laser-plasma accelerator technology: compact linac footprint (high gradient and compact laser coupling of stages)

## Slide 3
Requirements for efficient multi-TeV colliders: guided laser-plasma accelerator and laser development
3
C.B. Schroeder et al., PRST-AB (2010) and (2012); NIM-A (2016)
Example: 0.5 TeV Linac Length
Tradeoff: stage gradient vs. number of stages
  Minimum linac length sets density ~ 1017/cm3
  Consistent with optimal efficiency/charge
Hundreds of 10 GeV-class stages
  Each requires 10 Joule,10’s of kHz laser
  (for laser tech development, see K. Liani LOI])
Luminosity at TeV scale requires development of 10 J, 100 fs class lasers at ~50 kHz rep. rate
BELLA (LBNL)
HAPLS (ELI)
CoReLS (Korea)
fiber
kBELLA (Ti:Sa)
Tm:YLF
fiber
peak power [TW]
average power [kW]
collider
requirement:
50 kHz
> 30% effic.
Key step
technically
feasible
today: kHz
existing
laser
systems:
few Hz
2µm – 4x stages
LPA 100 m
5 GeV/m
CLIC~14km

## Slide 4
R&D timeline towards a collider
DOE HEP AAC Roadmap (2016)
  US AAC community outlined R&D goals in 2016 roadmap
  Progress on all R&D goals
  Roadmap to be updated
Critical technologies requiring R&D [see A. Gonsalves, LOI]:
  Plasma cell development: TRL3
  Multi-GeV/cell acceleration: TRL4
  Staging of LWFAs: TRL3
  Positron acceleration methods: TRL2
  Stability: TRL3
  Alignment: TRL2
4
Laser technology development required [see L. Kiani, LOI]
Promising technologies:
  Coherent combination of fiber lasers
  Tm:YLF
few kW average power feasible today

## Slide 5
Laser-driven plasma accelerators:
  Ultra-high gradient accelertor technology: ~10 GV/m
  Goal: e-/e+/gamma linear collider at TeV energy scale (and beyond), with much reduced footprint (and cost)
  Longer-term collider option
  Integrated collider design required (e.g., injector, cooling, focusing systems, etc.)
Experimental facilities required to advance R&D in next 5-10 years.
  Planned facilities: kBELLA (US), EuPRAXIA (Europe), etc.
  kHz rep rates will enable precision
Laser-plasma accelerators potential to play role in other collider systems:
  Rapid muon acceleration, high-brightness beam generation [see C. Benedetti, LOI], laser-plasma-based beam cooling [see S. Bulanov LOI], compact plasma-based focusing and beam delivery [see S. Barber, LOI], gamma collider
Near- and mid-term applications (LPA-driven X-FEL, compact gamma-ray source, ion acceleration for medical applications, etc.) are actively being pursued [see J. van Tilborg, LOI]
  Near-term applications are important demonstrations of technology that will advance collider R&D
Sustained R&D following Roadmap required to realize potential of laser-plasma accelerator technology
5
LOI Summary

## Slide 6
Thank you.
6
Work supported by the U.S. DOE, Office of Science, Office of High Energy Physics, under Contract No. DE-AC02-05CH11231

## Slide 7
Back up
7

## Slide 8
Laser technology requirements for collider applications
Laser energy/pulse [J]
rep. rate [kHz]
Two promising laser architectures for collider applications:
  Coherent combination of fiber lasers (1 micron). R&D at Jena, Michigan, LBNL, LLNL, et al.
      ~40-60% wall-to-laser efficiency
  Tm:YLF (1.9 micron) – (4x as many LWFA stages). R&D at LLNL
100 kW
10 kW
1 kW
kBELLA
(Ti:Sa)
fiber
fiber
Tm:YLF
BELLA (LBNL)
HAPLS (ELI)
CoReLS (Korea)
8
existing laser system
technically feasible today
collider requirement
+

## Slide 9
Laser-driven plasma wakefield accelerators
Main advantage of laser-plasma accelerator technology: compact linac footprint (both accelerating plasma cell and drive laser beam)
Wakefield (plasma wave) driven by the ponderomotive force of a resonant laser pulse in plasma
Focusing and acceleration provided by plasma wave
Characteristic size of accelerating field:
    Plasma density n0=1017 cm-3 yields E=30 GV/m
Uses short duration, high intensity drivers [laser drivers rely on Chirped Pulse Amplification (CPA) – Nobel prize 2018]
Compact coupling (< 1 m) of laser drivers using plasma mirrors
9
electron plasma density
laser driver
particle beam
plasma wavelength
Esarey, Schroeder, Leemans, Rev. Mod. Phys. (2009)

## Slide 10
Status of experimental R&D
  Single stage achieved multi-GeV acceleration: 8 GeV in 20 cm (40 GV/m)
  Proof-of-principle staging
Compact driver coupling using plasma mirrors
  Proof-of-principle experiment demonstrate 100 MeV energy gain
  Multi-GeV staging experiments are planned / being commissioned
divergence:
150 mrad
Plasma lens focusing of beam
  1 Hz rep. rate
  Reproducibility limited by laser fluctuations (at ~100 Hz)
discharge-capillary plasma waveguide
10
2019 (LBNL)
2014 (LBNL)
2006 (LBNL)
Energy gain (GeV) in LWFA stage
Operational plasma density (x1018 cm-3)
Gonsalves et al. PRL (2019)
Steinke et al. Nature (2016)
2013 (TPW)
2013 (GIST)

## Slide 11
Potential Facility Table
Laser-plasma collider - e-/e+ |  | 1 TeV cme | 3 TeV cme | 30 TeV cme
Beam Energy | TeV | 0.5 | 1.5 | 15
Luminosity (10^34) | cm-2 s-1 | 1 | 10 | 1000
Int. Luminosity | ab-1/yr | 0.18 (5000hrs) | 1.8 (5000hrs) | 18 (5000hrs)
Beam dE/E at IP |  |  |  | (Y>>1 regime)
Transv. Beam sizes at IP x/y | nm | 50 / 1 | 10 / 0.5 | 0.2 / 0.2
Rms bunch length / beta* | mm | 0.0085 / 0.1 | 0.0085 / 0.1 | 0.0085 / 0.2
Crossing angle | urad |  |  | 
Rep. frequency | kHz | 47 | 47 | 47
Bunch spacing | us | 21 | 21 | 21
# of IPs |  | 1 | 1 | 1
# of bunches |  | 1 | 1 | 1
Length (2x main linac tunnel) | km | 0.44 | 1.3 | 13
Facility site power (2 linacs) | MW | 105 | 315 | 3151
Cost range | $B US |  |  | 
Timescale till operations |  | >30 years | >30+ years | >30++ years
requires laser tech maturity before estimate
11
1 um laser wavelength
1017 cm-3 plasma density
Schroeder et al. NIMA (2016)
TBD: similar to conventional collider designs
Laser rep. rate not available with present laser technology
Upgrade potential: Same laser system for 1, 3, 30 TeV
ALL PARAMETERS NEED SYSTEM-INTEGRATED DESIGN STUDY

## Slide 12
Key accelerator R&D challenges
12
Laser technology development
  Coherent combining of fiber lasers
  Development of Tm:YLF
  kW average power systems feasible today
Robust e+ acceleration configuration
  Proposed configurations (hollow plasma channels, plasma columns) require experimental demonstrations
Beam matching/coupling between stages
  Strong focusing forces in plasma: β~ 0.01 - 0.1 m
Alignment
  Small structures (~10-100 um) place severe (~nm) alignment tolerances
Stability in main linac
  Transverse stability (BBU) is issue in strong wakefield regime
  Proposed mitigation methods (ion motion, plasma focusing chirp) require R&D
common challenges for advanced accelerator concepts