## Slide 1: The First Report
You need to present
  The place of your group’s work in a larger picture of Fermilab’s activities.
    The audience is supposed to have a general knowledge about Fermilab
  Briefly describe the physics of phenomena you deal with
  The audience is supposed to have a general knowledge in physics
  The goal of the project you participate in
  Explain the importance of the project (if so)
  The time frame of the project
  What do you expect to accomplish
  Try to be more specific about your personal goals

## Slide 2
The report should be prepared in Power Point and presented in English
  The total number of slides is not more than 5
  The length of the presentation is not more than 5 min
  The presentation is expected to be uninterrupted
    All questions follows the presentation
  The report should be ready by 8 AM of the presentation day
This presentation can be included as the first part of your final report
The First Report

## Slide 3: Drag rate measurements in the Recycler electron cooler
Summer student meeting
July 13, 2011
Ivanov, Novosibirsk State University
Supervisor: John Smith, AD/Recycler department

## Slide 4: Electron cooling in the Recycler ring
The Recycler is a 8 GeV storage ring sharing the 3.3 km tunnel with the Main Injector
  Presently the role of the Recycler is to accumulate antiprotons coming form the Antiproton source and to cool them for the shots to the Tevatron
  Antiprotons are cooled by two methods, stochastic and electron cooling
Electron cooling is a process of a thermal exchange through Coulomb scattering between hot heavy particles (antiprotons) and cold electrons
  For cooling to be effective,
    the electron beam has to be cold
    average velocities of both beams should be precisely matched

## Slide 5: Drag rate measurements
Cooling properties of the electron beam can be characterized by drag rate measurements
  A coasting antiproton beam is cooled down to an equilibrium
    RF is turned off, so that the only longitudinal force comes from electron cooling
  Electron energy is shifted
    In the rest frame, electrons start moving with respect to antiprotons and accelerate (“drag”) them
  The drag rate is recorded as a time derivative of the average antiproton momentum after the electron energy jump
Ve and Vp are the average velocities of electrons and antiprotons, correspondingly, in the frame moving with the initial speed of beams.
Time
Ve, Vp

## Slide 6: Goal
We plan repeat the drag rate measurements using a recently improved procedure and measure
  Dependence of the drag rate as a function of the voltage jump amplitude
  Drag rate at various positions across the electron beam
My personal goals are
  Participate in the measurements
  Write a MathCad program fitting the results to a model
  Estimate measurement errors
  Present my results at the Recycler departmental meeting