## Slide 1: MTA Beam Line Commissioning
07/11/2011 Update

## Slide 2: Since Last Update
Final bend (UVB03) inadequate for 1.6 degree bend.
  Replaced Booster Corrector UVB03 with Main Injector IDV corrector.
  Upgraded bulk supply to achieve higher voltage.
  Ramping all vertical bends and final vertical dogleg.
  Excellent work by EE and Mechanical Support groups!
Increased separation between vertical dogleg.
S8 (SWIC immediately upstream of collimator) no longer used – rely on phosphor screen.
Several studies to characterize beam.

## Slide 3
Moved corrector upstream to increase lever arm.
Replaced Booster Corrector with Main Injector IDV corrector and stand.
Uncabled S8.

## Slide 4: Status
Able to achieve 100% transmission to collimator (approximately 2x1012 H- over 10 microseconds).
After collimation, beam is approximately 1011 H- over 10 microseconds.