## Slide 1: LAr Cryostat Design and Qualification
G. Vallone, E. Anderssen, D. Boettcher, M. Leitner
DUNE Cryostat Qualification Meeting
10/30/20

## Slide 2: Index
Introduction
LAr Cryostat
  Design Description
  Structural Analysis
  Frame/Window Joint Design
Qualification Plan
Conclusion

## Slide 3: Introduction
A LAr cryostat is being developed for the DUNE project:
  We can’t really proceed with the design/test/calculations unless we agree on the applicable standards and limits
  The main result of this (and future) discussion should be the Memorandum of Agreement document, listing the applicable standards for design, manufacturing, assembly, and the test and commissioning plan
Meeting topics:
  LAr structure design description and preliminary FEA results
  Applicable standards discussion
  Experimental test plan
  Work plan
Further documentation (drafts):
  Memorandum of agreement
  Experimental test plan

## Slide 4: Index
Introduction
LAr Cryostat
  Design Description
  Structural Analysis
  Frame/Window Joint Design
Qualification Plan
Conclusion

## Slide 5: Plate Design
Liquid Argon enclosed by stainless steel plates / Polyurethane sandwich
One side covered by a composite window (described later) to reduce the impact on the particle beam
Window size: L8156*W3810*T372 (max)
Steel Frame
Detector
Polyurethane
Steel Plate 1
Steel Plate 2
Liquid Ar
Composite Window
Box Beams

## Slide 6: Plate and Joint Design – More Details Later
Plate design:
  25 mm thick fiberglass skins, polyurethane core
Joint design:
  Box beam around the plate for torsional stiffness
  Scarf joint to transition to fiberglass. A tapered lap joint would not able to satisfy the strength requirements (with a reasonable length).
  Production process is more complicated
Design process:
  Finite element models: 2D analysis to quickly optimize the geometry, detailed analysis on a 3D model, 3D submodels for critical regions
  Experimental verification Update Finite Element models

## Slide 7: Scarf Joint – Production Process
  Lay-up the bottom face sheet on the steel c-joint bottom half
  Glue the bottom joint steel ‘shoe’
  Glue the core
  Glue the top joint steel shoe
  Lay-up the top face sheet
  Weld the c-joint, then weld to the box beam
1
2
3
4
5
6

## Slide 8: FEA Model Description – Geometry and Material Properties
Geometry:
    YZ symmetry
    Steel plates, frame: shell elements
    Composite plate, foam: solid elements
  Foam properties:
      Density = 90 kg/m3
      E = 10 MPa – Seems a reasonable order of magnitude
      𝜈 0.5 (incompressible)

## Slide 9: FEA Model Description – Boundary Conditions and Loads
Boundary conditions:
  Floor b.c. only on y, but probably friction will lock also the other directions
  Interfaces: everything bonded
Loads:
    Liquid Argon Hydrostatic Load - Density = 1400 kg/m3 - Liquid Level Height = 4.5 m w.r.t. membrane floor
    Overpressure Load = 350 mbar
    Gravitational Acceleration

## Slide 10: Structural Analysis – Displacements
Contact elements on the bottom of the cryostat:
  Similar results with friction (0.1) and frictionless
  There is some lifting close to the corners. This allows for some additional rotation of the corner.
Adding stiffeners in the corners can further reduce the deformation
Anchoring the floor can reduce the deformation from 12 mm to 8 mm
Anchored to the Floor
Simply Supported

## Slide 11: Structural Analysis – Stress Analysis
Negligible stress on the plate
Stress on the steel structure is low almost everywhere
  Few joints see local stress spikes (still lower than the yield limit)
  Max stress ~ 180 MPa on the square beam joint
    This can be reduced adding local reinforcements (as in ProtoDUNE)
    Preliminary results, beams/joints to be verified following structural codes

## Slide 12: Scarf Joint – 2D Model Results - Compliance
Joint compliance is almost all in the box beam constraint
  This is what we want, and a joint behaving like this will guarantee similar results to the one provided by the 3D analysis
Negligible stresses in composite components
Local stresses in steel:
  May need some reinforcement / higher radius
  We might decide to accept a small amount of plastic deformation there
  Here we are considering an ‘exaggerated’ scenario where there is no longitudinal support

## Slide 13: Scarf Joint – 2D Model Results – Glue Strength
Stress allowed in the glue:
  5 MPa average on shear stress
  10 MPa average on tensile
We are ~1 order of magnitude below
  Also the maximum stress in the glue is lower than our average criteria

## Slide 14: Structural Analysis – Stress Analysis on the Joint
Joint submodel analysis:
  displacements interpolated from the global model and applied on the cut boundary
Stress allowed in the glue:
  5 MPa average on shear stress, 10 MPa average on tensile
Max frictional stress ~ 6 MPa, Max. tension ~ 5 MPa
Criteria satisfied with significant margin

## Slide 15: Index
Introduction
LAr Cryostat
  Design Description
  Global Structural Analysis
  Frame/Window Joint Design
Qualification Plan
Conclusion

## Slide 16: Applicable Documents/Standards - 1
Fermilab Safety Manual (April 2020):
  FESHM 5031.7: Membrane Cryostats
  FESHM 5031.7: Requirements for Membrane Cryostats
  TA5031.7 – Form for membrane cryostats
Applicable codes:
  EN-14620 (December 2006): Design and manufacture of site built, vertical, cylindrical, flat-bottomed steel tanks for the storage of refrigerated, liquified gases with operating temperatures between 0 °C and -165° C
  Warm support structure, steel components:
    EU codes (Equivalence to US codes from: Acceptance of Steel and Aluminum Structures Designed per the Eurocodes at Fermilab):
      Eurocode 1990 (April 2002): Basis of structural design
      Eurocode 1991-1-1 (April 2002): Actions on structures – Part 1-1: General actions – Densities, self-weight, imposed loads for buildings
      Eurocode 1993 (May 2005): Design of steel structures:
        Part 1-1: General rules and rules for buildings
        Part 1-8: Design of joints
    Eurocode 1998 (December 2004): Design of structures for earthquake resistance
      Loads from USGS design maps for FNAL

## Slide 17: Applicable Documents/Standards - 2
Applicable codes (continues):
  Warm support structure, steel components:
    EN 1090-2: Technical requirements for the execution of steel structures
  Warm support structure, steel/window joint:
    EN1990 Annex D – Design Assisted by Testing
  Warm support structure, composite window:
    ASME RTP-1-2013 – Reinforced Thermoset Plastic Corrosion-Resistant Equipment

## Slide 18: Applicable Documents/Standards – Covers - 1

## Slide 19: Applicable Documents/Standards – Covers - 2

## Slide 20: Applicable Documents/Standards – Covers - 3

## Slide 21: General Plan
Membrane cryostat, steel structure:
  FESHM, EN14620, EN1990/3/8 satisfied following protoDune/SBND
Manufacturing and Assembly
  Manufacturing and assembly following EN1090-2, which provides requirements for the execution of steel structures, to ensure adequate levels of mechanical resistance and stability, serviceability and durability
    The structures follow a strict quality control, inspection and testing plan as per EN1090 (i.e. quality of welds execution attested by an authorized independent inspection agency)
  Quality control of the composite parts (joints and window) will follow ASME RTP-1
Tests and commissioning
  Destructive test for the weakest structural part of the steel frame
  Stiffness and strength tests of the steel to composite joints
  Structural tests of the window laminate required by ASME RTP-1
  Pneumatic test of the cryostat
  Hydrostatic + overpressure (up to design gas overpressure, 350 mbar) test
    Gradual load increase with step-by-step comparison with FEA results
    Acoustic emission will not be used (stress ratio 9 on laminate, per ASME RTP-1)

## Slide 22: Joint - EN1990 Annex D – Design Assisted by Testing
EN1990 Sec 5.2 used to design the steel/window joints:
Design may be based on a combination of tests and calculations.
Testing may be carried out, for example, in the following circumstances:
  if adequate calculation models are not available;
  to confirm by control checks assumptions made in the design.
Test scope:
  Determine the stiffness and strength of the frame/window joint
  Window (glass fiber reinforced plastic) verification based on BPVC
  Test plan will be described in a dedicated talk
EN1990 Sec 5.2 - Annex D:
  Conversion factor for scaling, etc.
  Partial factor as appropriate (joints, see EN1993-Part 1-8)
Conversion
Factor
Partial
Factor
Coeff. of
Variation
Average

## Slide 23: Composite Sandwich Plate – ASME RTP-1
Materials:
  Allows for flat cored plates but requires:
    Polyester or vinyl ester resins – might be required because of corrosion resistance (we do not need that), and might not be the best ones for our use case
    Balsa wood core – great mechanical performances, but might not be necessary…
      We could prove that our material choice has equivalent performances
Design:
  Design by analysis, with stress ratio 9 if no Acoustic Emission is performed
    8 otherwise, but we are not sure on how AE acceptance criteria would interact with the steel structure. Also, requires multiple fillings to verify the AE variation.
  Strength: Tsai-Wu or first play failure
Testing:
  Requires mechanical tests on the laminate
  Pressure test: fill at full designated liquid capacity
    Compatible with FHSM requirements and tests/commissioning procedures defined for protoDune/LBNF

## Slide 24: Composite Sandwich Plate - Alternatives
Three possible paths for the composite components (not the joints, already covered in EN1990):
ASME BPVC Sec X, Fiber-Reinforced Plastic Pressure Vessels:
  Might be classified as class 2 vessel
  Sandwich construction not considered
  Special joints not considered
ASME RTP-1, Reinforced Thermoset Plastic Corrosion-Resistant Equipment:
  Allows for a flat sandwich plate
  Special requirements on the materials, core might be an issue – must be balsa core, polyester or vinyl ester resins
  Special joints not considered
Euro guidance - Prospect for New Guidance in the Design of FRP or European recommendations (e.g. CUR96):
  Harmonized with the Eurocode
  Materials ok
  T has to be > -20 C
We can satisfy the requirements from one of these standards AND Eurocode 1993 AND EN-14620
We might need to write our design criteria specifying with more detail which rules are applied where

## Slide 25: Conclusion and Next Steps
Conclusion:
A preliminary design was discussed, with relative preliminary FEA results
We have identified a set of standards and a procedure with key steps
Frame/window joint verification:
  A preliminary test plan was already defined, discussed in the next talk
Next steps:
Iterate based on committee feedback

## Slide 26
Back-up slides

## Slide 27: Window Design: Which are the Available Parameters?
Sandwich design
  Better than locally stiffened designs for distributed loads (e.g. pressure)
Available parameters:
    Skin thickness / Core thickness
    Skin material
    Core material
  Carbon and Aluminum outperform other materials, but they are much more expensive

## Slide 28: Window Design: Surface Density Contribution of the Window
Surface density of each component
  Target (total) is ~ 50 g/cm2
Composite window contribution ~ 16% of the total
  Advantage on steel:
    factor ~2.5 on average
    1 order of magnitude on the beam locations
Layer | Material | thickness | rho | rho*t | Contrib.
/ | / | mm | kg/m3 | g/cm2 | %
Liquid | Argon | 300 | 1396 | 41.9 | 62.7%
Plate | Steel | 2 | 7000 | 1.4 | 2.1%
Insulation | Polyurethane | 808 | 90 | 7.3 | 10.9%
Window | Composite | 372 |  | 16.2 | 24.3%
Steel Avg. | Steel | 58.3 | 7000 | 40.8 | 
Steel Max. | Steel | 372 | 7000 | 260.4 | 
Total |  |  |  | 66.78 | 100%

## Slide 29: Secondary Support – Possible Designs
Comparison ‘corrugations’ vs ‘small beams’
  ‘Square region’ case / similar performances expected on the rectangular one
  The role of these reinforcement is to contain the local deformations
  It is a ~secondary structure
  Corrugations were adopted for simplicity in SBND
Might be wort to estimate an equivalent plate stiffness for our beam model

## Slide 30: Secondary Support
Max. deformation is in the middle of the non-reinforced region for the beam
Corrugation design 1 has better performances, but also more material
Design 2 has same mass and similar performances
  Performances driven only by the maximum distance between stiffeners minimize
  We can go for the corrugation design
Design 1
Design 2

## Slide 31: Structural Analysis – Impact of the frame on the displacement
Plate stiffness – simply supported and fixed on the outer edge
  Displacement: 7.9 mm or 2.6 mm
  Most of the deformation is coming from the frame!
    Edge rotation ~ 3.3 mm
    Support motion ~ 2 mm
Fixed
Supported

## Slide 32: Structural Analysis – Stress Analysis
Negligible stress on the plate
Stress on the steel structure is low almost everywhere
  Few joints see local stress spikes (still lower than the yield limit)
  Max stress ~ 180 MPa on the square beam joint
    This can be easily be reduced adding local reinforcements (as in ProtoDUNE)

## Slide 33: Applicable Documents/Standards - 3

## Slide 34: Work Plan - Description
Our current work plan divided in 3 ‘phases’:
  Phase I is the discussion with the committee:
    We can’t really proceed with the design/test/calculations unless we agree on the applicable standards and limits
    The main result of this discussion will be the Memorandum of Agreement document, listing the applicable standards for design, manufacturing, assembly, and the test and commissioning plan
  In Phase II we can proceed with:
    Structural calculations
    Test campaign for the composite parts and steel/composite joints
  Phase III will produce the ‘deliverables’:
    Test results summary
    Calculation note
    Quality control and acceptance testing plan (Quality assurance)
    Fabrication and erection plan

## Slide 35: Loads Definition - 1
Loads can be defined following:
  Eurocode 1991-1-1: Actions on structures – Part 1-1: General actions – Densities, self-weight, imposed loads for buildings
  ASCE/SEI 7 document (Minimum Design Loads for Buildings and Other Structures)
  In both cases, we get a series of coefficients that we need to apply to define two ‘load-cases’:
    Serviceability Limit State (SLS): related to deformations/vibrations/damages that might affect appearance/discomfort. In our case would be related to the detector performances
    Ultimate Limit State (ULS): limit that concern the safety of people and of the structure
  Design value for the actions considers a characteristic value (F), possible unfavorable deviations from the average value (𝜓>1) and a combination coefficient (𝛾<1)
𝜓 values are in three ‘tiers’ with growing ‘likelihood’. In our case is not very interesting as all our load combinations (permanent loads) should be very predictable ~ (e.g. no snow, wind, traffic…)

## Slide 36: Load Definition – 2 – Ultimate Limit State
For ULS load combination:
In our case:
  Self-weight: 1 or/and 1.3
  Hydrostatic pressure: 1.3
  Overpressure: 1.5
  Sloshing load, horizontal acceleration (should also be G): 1.5 – what if engine fails?
  Note: we must check if self-weight is favorable w.r.t. pressure/overpressure
SBND: 1.35, 1.35, 1.4 – slightly different than expected
Permanent
Loads
Prestress
Variable
Loads

## Slide 37: Load Definition – 3 – Serviceability Limit State
For SLS load combination:
Other combinations are considered in the standard, with different coefficients for the variable actions Q, which we are not considering
Seismic design situations:
Characteristic Combination

## Slide 38: Material Selection and Limits
Steel selection – properties from EN1993-1-1
SBND used S355, start from the same material and evaluate costs in the meanwhile:
  fy = 355 MPa, fu = 470 MPa
Material resistances must be scaled with safety coefficients:
  𝛾M0 = 1 (resistance), 𝛾M1 = 1 (stability), 𝛾M2 = 1.25 (connections/joints)

## Slide 39: Connections/Joints – 1 – Joint Classification
Flexibility: in our beam model we can connect different beams with rigid, semi-rigid or flexible (pins) joints
  If Ks>20EI/L we can use rigid joints (we did this until now)
Strength: full, partial, flexible – with respect to the members connected

## Slide 40: Connections/Joints – 2 – LAr Design Joint Types
We are using 4 types of connections:
  3 welded, 1 bolted connection
  Need to check if this is complete or if we want to change it
  Need to check each connection ‘type’
Beam to column connection: alternating weld/bolts with reinforcement plates
Column
Beam
Plate C1
Weld Type 1

## Slide 41: Connections/Joints – 2 – LAr Design Joint Types
Corner connection for beams: welded with reinforcement plates
Corner connection for columns: welded with reinforcement plates
Weld Type 2
Weld Type 3

## Slide 42: FE Modeling
Beam model, more suited for ULS under development
  Used to extract actions and verify strength and stability per EN provisions
  We will have to add also the prison frame to this model
  Joints must be modelled as rigid/semi-rigid/flexible based on the classification results
SLS considerations from shell model (presented at CDR) still valid