## Slide 1
SPL CAVITY DEVELOPMENT
G. Olry (IPN Orsay)

## Slide 2: outline
Introduction
  SPL layout
  Working group
Beta=0.65 & Beta=1
  RF design
  Tuning system
  Lorentz forces detuning
  HOM studies
  - RF coupler
  Mechanical design of beta=1
Short-cryomodule
Poster MOP021: H-M. Gassot
Poster MOP034: J. Plouin
Poster TUP002: G. Devanz
Poster MOP040: W. Xu
Poster MOP059: W. Xu
Poster MOP005: V. Parma
Talk this morning THIOA06: O. Capatina
+ data from ESS/SPL collaboration meetings
Notes: Cavité = souvent premier objet de R&D sur les projets d’accélérateurs

## Slide 3: SPL layout
  ~500m driver for new physics facilities @ CERN such as neutrinos and radioactive ion beams.
  HP-SPL main beam characteristics : 5 GeV, 4 MW, 40 mA, 50Hz
  SC cavities
  60 beta 0.65, 704MHz, 5-cell elliptical cavities
  184 beta=1, 704 MHZ, 5-cell elliptical cavities
Entrance to new Linac 4 tunnel
Notes: Cavité = souvent premier objet de R&D sur les projets d’accélérateurs

## Slide 4: collaboration: who is doing what?
Beta 1.0
CEA/Saclay: 1 cavity with Titanium Helium vessel
Stainless Steel Helium vessels and tuning systems for the CERN cavities
CERN: 4 cavities with Stainless Steel vessels
2 ≠ RF coupler types
BNL: 1 « Universal » cavity
Beta 0.65
IPN Orsay: 1 cavity with Titanium Helium vessel
HOM
Rostock U.: HOM coupler design
Royal Holloway U. of London: Cavity-to-cavity coupling effects
BNL: Cavity-to-cavity coupling effects & HOM coupler design
SHORT-CRYOMODULE
CERN & IPN Orsay
Notes: Cavité = souvent premier objet de R&D sur les projets d’accélérateurs

## Slide 5: Beta 0.65
RF design
 Operating gradient: 19 MV/m
  Epk/Eacc<2.6 (<-> Epk=50 MV/m)
  Bpk/Eacc<5.2 mT/(MV/m) (<-> Bpk=100 mT)
EM calculations
  1/ in 2D with SUPERFISH
  2/ in 3D with CST MWS  RF coupler integration
E field
f (MHz) | 704.0
Epk/Eacc | 2.63
Bpk/Eacc (mT/MV/m) | 5.12
K (%) | 1.45
r/Q (Ohm) | 275
G (Ohm) | 197
Vacc @g & 1 Joule (MV) | 1.11
Qo (@2K, Rres=2n) | 3.9 1010
Transit Time Factor | 0.65
Notes: Cavité = souvent premier objet de R&D sur les projets d’accélérateurs

## Slide 6: Beta 0.65
Mechanical design
Von Mises stresses for 1.5 bar @ 300K < 50 MPa with 4mm
Lorentz forces detuning factor : KL~ -1.6 Hz/(MV/m)²
Cavity walls = 4mm
 Niobium cost ~70 k€
46 MPa
Poster MOP021: H-M. Gassot
94mm
beam axis
1 stiffening ring
Notes: Cavité = souvent premier objet de R&D sur les projets d’accélérateurs

## Slide 7: Beta=1
RF design
 Operating gradient: 25 MV/m
  Epk/Eacc<2 (<-> Epk=50 MV/m)
  Bpk/Eacc<4 mT/(MV/m) (<-> Bpk=100 mT)
Poster MOP034: J. Plouin
EM calculations
  1/ in 2D with SUPERFISH
  2/ in 3D with HFSS RF coupler integration
J. Plouin – High beta cavity for SPL- ESS/SPL collaboration meeting, Saclay, 30 june – 01 july 2011
Frequency [MHz] | 704.4
Bpk/Eacc [mT/(MV/m)] | 4.20
Epk/Eacc | 1.99
G [Ohm] | 270
Cell to cell coupling | 1.92 %
r/Q [Ohms] | 566
Lacc = Ngap.b.l/2 [m] | 1.0647
Notes: Cavité = souvent premier objet de R&D sur les projets d’accélérateurs

## Slide 8: Beta=1
Tuning system
Saclay V type with 1 piezo
Tuning sensitivity of 164 kHz/mm
Lorentz forces detuning factor : KL~ -1.2 Hz/(MV/m)²
9 tuning systems delivered in May 2011
J. Plouin – High beta cavity for SPL- ESS/SPL collaboration meeting, Saclay, 30 june – 01 july 2011
1 ring
Notes: Cavité = souvent premier objet de R&D sur les projets d’accélérateurs

## Slide 9: Beta 0.65 & Beta=1 common features
Orders: end of 2011
Same helium vessel design and same end-groups
 Final test in horizontal cryostat with the same auxiliary components (tuning system + RF coupler)
CEA Saclay beta=1
IPN Orsay beta 0.65
Titanium He vessel
CRYHOLAB
Notes: Cavité = souvent premier objet de R&D sur les projets d’accélérateurs

## Slide 10: Beta=1
Talk this morning THIOA06: O. Capatina
Same RF design as the CEA Saclay beta=1 cavity
Notes: Cavité = souvent premier objet de R&D sur les projets d’accélérateurs

## Slide 11: “universal” Beta=1
For any kind of high current applications (e-, p, CW, pulsed...)
Fundamental mode: maximizing R/Q & G
HOMs damping optimizations:
  very large beam tube aperture (up to 11cm),
  6 HOM couplers (3/end-pipe)
  tapers: avoid cavity-to-cavity coupling
 propagation and power extraction of almost all monopole, dipole and quadrupole modes
Poster MOP040: W. Xu
Poster MOP059: W. Xu
Parameters | BNL3
Frequency [MHz] | 703.79
Number of cells | 5
Geometry factor [Ω] | 283
(R/Q)/Cavity [Ω] | 506.3
Epeak/Eacc | 2.46
Bpeak/Eacc [mT/MV/m] | 4.27
Coupling factor [%] | 3.02
Qext of dipole HOMs.
10E+4
Notes: Cavité = souvent premier objet de R&D sur les projets d’accélérateurs

## Slide 12: HOM studies
Beam-HOM interactions studies
  Influence of parameters like HOM frequency spread, substructured pulses (=chopping patterns), cavity alignment, beam jitter…on long. and trans. planes stability
  No major effects on trans. plane
  Long. plane: chopping patterns could affect the beam
  HOM couplers are recommended with Qext<105
M. Schuh et al., Influence of Higher Order Modes on the Beam Stability in a High Power Superconducting Proton Linac, PRST-AB 14, 051001 (2011)
Cavity-to-cavity coupling
  Simulation on 4 beta=1 cavities
   Check the influence of different taper geometries
Notes: Cavité = souvent premier objet de R&D sur les projets d’accélérateurs

## Slide 13: HOM studies
Multipacting (MP) simulations
Rostock 1st model shows MP barrier  geometry change (bumps)
H.-W. Glock, Universität Rostock
Notes: Cavité = souvent premier objet de R&D sur les projets d’accélérateurs

## Slide 14: Short-cryomodule
Design and construct a ½-length cryomodule with 4 beta=1 cavities and auxiliary components (as close as possible to a machine-type cryomodule)
Test with all components assembled: mid-2014
Cylindrical type (LHC like)
« Tunnel » type
Vacuum vessel alternatives
Poster MOP005: V. Parma
V.Parma Joint ESS/SPL meeting, CEA, 30 June – 1 July 2011
Notes: Cavité = souvent premier objet de R&D sur les projets d’accélérateurs

## Slide 15: Short-cryomodule
Supporting scheme
 RF coupler double-walled tube as cavity support
Max: 0.12 mm
Intercavity supports
RF coupler double-walled tube flange fixed to vacuum vessel
Last cavity support
Body deformation amplified 300x
Self-weight vertical sagitta
V.Parma Joint ESS/SPL meeting, CEA, 30 June – 1 July 2011
Notes: Cavité = souvent premier objet de R&D sur les projets d’accélérateurs

## Slide 16: acknowledgments
CEA Saclay: J. Plouin
CERN: O. Capatina, V. Parma
BNL: I. Ben-Zvi
Thank you for your attention