## Slide 1: SRF Development for High Energy Physics
Mark Champion
SRF 2011

## Slide 2: Introduction
The HEP community has shown increasing interest in SRF technology in recent years
  ILC R&D program
  Project X at Fermilab
  Neutrino factories and muon colliders
However, the application of SRF technology to HEP research has a long history
Now let’s go back in time and take a look at that history

## Slide 3: Stanford High Energy Physics Laboratory (HEPL) a.k.a. Hanson Experimental Physics Laboratory
1962: First measurements of superconducting cavity performance
  Lead-plated S-band 2856 MHz muffin tin cavities
  Qo ~ 1e8-1e9, Bp ~ 100 G (10 mT), 4 K
1965: First acceleration of electrons with a superconducting cavity
1972: First superconducting accelerator
  Based on L-band 1300 MHz niobium cavities
  Cavity performance limited by multipacting
    the elliptical cavity shape was not yet developed

## Slide 4: HEPL 1300 MHz Cryomodule Pair
Courtesy of T. Smith, HEPL

## Slide 5: Layout of HEPL Cryomodule
55 cell, 1300 MHz, bi-periodic structure
~2.5 MeV/m

## Slide 6: TRISTAN and KEKB
TRISTAN was an electron-positron collider constructed at KEK in the 80’s
32 five-cell 508 MHz elliptical SC cavities housed in 16 cryomodules
Installed in 1988 – 1989 (augmented existing NC cavities)
Eacc = 5 MV/m, Qo = 2e9 at 4.2 K, continuous wave
TRISTAN was shut down in 1995
KEKB was an asymmetric-energy electron-positron collider constructed at KEK in the 90’s
Reused much of the TRISTAN infrastructure and components
8 single-cell 508 MHz SC cavities housed in 8 cryomodules
Ecavity = 1.2 – 2 MV, Qo ~ 1e9 at 4.2 K, continuous wave
Heavy beam loading and HOM loading ( IB = 1.4 A )
KEKB has been shut down and is being upgraded to SuperKEKB

## Slide 7: Cryostat for TRISTAN SRF Cavities
http://accelconf.web.cern.ch/accelconf/SRF89/papers/srf89g29.pdf
Courtesy of N. Toge, KEK

## Slide 8: Cryomodules in the TRISTAN MR Tunnel
From KEK Annual Report 1988 - http://www-lib.kek.jp/ar/ar.html
Courtesy of N. Toge, KEK

## Slide 9: Cryostat for KEKB SRF Cavities
http://epaper.kek.jp/p99/PAPERS/THBL2.PDF
Courtesy of N. Toge, KEK

## Slide 10: Cryomodules in the KEKB Tunnel
KEK Annual Report 1998 - http://www-lib.kek.jp/ar/ar.html
http://www-acc.kek.jp/kekb/pictures/KEKB_photo/ring1.jpg
Courtesy of N. Toge, KEK

## Slide 11: DESY HERA 500 MHz Cryomodules
Electron-proton collider
16 SC cavities commissioned in electron storage ring in 1991-1992
  Augmented 84 NC 500 MHz cavities to increase beam energy
Bulk niobium, RRR 300, 4-cell, 500 MHz elliptical cavities
Eacc = 5 MV/m, Qo = 2e9 at 4.2 K, continuous wave
Two klystrons, combined, drive all 16 cavities (vector sum RF control)
HERA experiment concluded in 2007
The initiation of the TESLA Test Facility coincided approximately with the successful commissioning of the HERA SC cavities
Courtesy of W-D Moeller, DESY

## Slide 12: HERA Cavities and Cryomodule
Courtesy of W-D Moeller, DESY

## Slide 13: LEP Superconducting Cavities
The LEP electron-positron collider at CERN was upgraded with SC cavities in the period 1992-1999
Beam energy increased from ~46 GeV to ~100 GeV
Final configuration: 288 four-cell cavities
  272 niobium sputtered onto copper cavities
  16 bulk niobium cavities
  48 copper cavities (originally 128)
352 MHz, 4.5 K, continuous wave
8 cavities per 1.3 MW klystron
LEP cryomodules were removed in 2000-2001 to make way for the LHC

## Slide 14: LEP 352 MHz Cavity and Cryomodule
Courtesy of CERN
4 cavities / cryomodule
72 modules going into storage

## Slide 15: Achieved Gradients in LEP Cu/Nb Cavities in 1999
P. Brown et al., “Performance of the LEP200 Superconducting RF System,” SRF1999.
Highest performance achieved at end of run
Operated cavities near their limits
Increased limits via RF conditioning
< Eacc > ~ 7.2 MV/m
Qo ~ 3e9 at operating gradient

## Slide 16: LHC Superconducting Cavities
400 MHz, single-cell, niobium sputtered onto copper cavities, 4.5 K, continuous wave
Four cavities per cryomodule
Sixteen cavities total
2 MV / cavity (5.3 MV/m), Qo > 1e9
One klystron per cavity

## Slide 17: LHC SC Cavity
P. Maesen, “LHC Superconducting Cavities,” CWRF2008

## Slide 18: LHC Cryomodule
Courtesy of CERN

## Slide 19: CESR – Cornell Electron Storage Ring
Electron-positron collider completed in 1979
Upgraded with four SC cavities in the period 1997 – 1999 (replaced NC cavities)
  500 MHz, single-cell, one cavity per cryomodule
  Eacc = 6 MV/m, Qo > 1e9 at 4.2 K, continuous wave
  Heavy beam loading and HOM loading ( IB ~ 0.8 A max)
  Cavity and Cryomodule design was industrialized with Accel (now RI) and sold to several light sources world wide
  AES is presently fabricating two of these systems
Courtesy of Cornell University

## Slide 20: CESR-B 500 MHz Cryomodule
Courtesy of Cornell University

## Slide 21: Future HEP Applications of SRF Technology
International Linear Collider
  Approximately 17,000 cavities over 31 km
Project X
  3 GeV continuous-wave H- linac followed by 8 GeV pulsed H- linac
Large Hadron Collider upgrades
  Crab cavities for interaction region
Muon Collider / Neutrino Factory
  Project X driver plus downstream acceleration of muon beam

## Slide 22: International Linear Collider Layout

## Slide 23: ILC Cavities and Cryomodules
Each cryomodule contains (8 cavities + 1 magnet) or (9 cavities)
Total ~2000 cryomodules, ~17000 cavities.

## Slide 24: Project X Reference Design

## Slide 25: PX SRF Linac Technology Map
b=0.11
b=0.22
b=0.4
b=0.61
b=0.9
325 MHz
2.5-160 MeV
b=1.0
1.3 GHz
3-8 GeV
ILC
650 MHz
0.16-3 GeV
Section | Freq | Energy (MeV) | Cav/mag/CM | Type
SSR0 (G=0.11) | 325 | 2.5-10 | 18 /18/1 | SSR, solenoid
SSR1 (G=0.22) | 325 | 10-42 | 20/20/ 2 | SSR, solenoid
SSR2 (G=0.4) | 325 | 42-160 | 40/20/4 | SSR, solenoid
LB 650 (G=0.61) | 650 | 160-460 | 36 /24/6 | 5-cell elliptical, doublet
HB 650 (G=0.9) | 650 | 460-3000 | 160/40/20 | 5-cell elliptical, doublet
ILC 1.3 (G=1.0) | 1300 | 3000-8000 | 224 /28 /28 | 9-cell elliptical, quad
CW
Pulsed
Courtesy of Bob Kephart, Fermilab

## Slide 26
Courtesy of S. Geer, Fermilab

## Slide 27: Summary
HEP has been a driver for the development of SRF technology for many years
  Starting at Stanford in the early 60’s
  Successful implementation at HERA, CESR, TRISTAN, KEKB, LEP, and LHC
HEP has continued this role in recent years with the ILC R&D program and Project X
HEP plans for future accelerators require SRF technology
  ILC, Project X, LHC upgrades, and Muon collider / Neutrino factory
Substantial overlap with non-HEP applications is driving collaborations world wide
  Spallation neutron sources, nuclear physics, light sources, and Accelerator Driven Systems

## Slide 28: Acknowledgements
Thanks to all of the colleagues in the SRF community for 50 years of effort to develop and utilize SRF technology
Thanks for the many publications, from which I have obtained the information for this presentation
Special thanks to Wolf-Dietrich Moeller, Todd Smith, and Nobu Toge