## Slide 1: 200 kT Water Cherenkov Detector Vessel Liner
50% Conceptual Design Review

## Slide 2: Outline
Vessel Liner Background
CNA Phase 2 Recommendation
Key Concerns
Conceptual Vessel Liner Design
Comparative Leakage Rates
Constructability
Testing

## Slide 3: Vessel Liner Background
Initial Options
  Free-standing
  Rock-supported
  Pressure-balanced
Phase 1 Down-select to 2 options:
  2A: Rock-supported, cast-in-place concrete vessel
  1E: Free-standing steel vessel

## Slide 4: CNA Phase 2 Evaluation
Eliminate Option 1E
Add Option 2C: Rock-supported with liner directly on shotcrete
Both have drainage layer(s) behind waterproofing membrane
Experiment water and native groundwater separated

## Slide 5: CNA Phase 2 Options
Concept 2C
Concept 2A

## Slide 6: Option 2C Floor Detail

## Slide 7: Key Concerns
Drainage Layer Facilitates Leakage
Liner Penetrations
Complexity of Design
CQA

## Slide 8: Conceptual Design Tasks
Review previous work
Recalculate for 200 kT WCD
Research alternatives
  High head
  Leakage control
  Seaming
  Attachments to vessel
Assume polyethylene in contact with water

## Slide 9: Recommended Conceptual Design A
Exp’t Water
Membrane
GCL
Shotcrete
Mag. Coils
Excavation Damage Zone
GW Control

## Slide 10: Geosynthetic Clay Liner
Geotextile
Bentonite
HDPE
Geotextile

## Slide 11: Recommended Conceptual Design B
Exp’t Water
Membrane
Concrete
Mag. Coils
Drainage Layer
Excavation Damage Zone
GW Control
Shotcrete

## Slide 12: Concept A Floor Detail
Membrane
GCL
Shotcrete
Mag. Coils
Concrete
Drainage Layer
Sump

## Slide 13: Conceptual Panel Layout
Floor
Walls

## Slide 14: Panel Mounting Options
“Velcro”
Polyethylene Plate

## Slide 15: Conceptual Design Features
Leakage minimized 3-6 orders of magnitude
Simplified construction
Minimized penetrations for attachment
Smooth walls to minimize strain on membrane

## Slide 16: Testing
Material compatibility
Liner lifetime
Liner creep
Leak testing
  Seams
  Penetrations
Water interactions