## Slide 1: Study of Dielectric Loaded RF Cavity
MAP meeting - September 23, 2011
Jessica Cenni

## Slide 2
September 23, 2011
Jessica Cenni
1
CONTENTS
Why a Dielectric Loaded (DL) RF cavity?
Characterization of a dielectric loaded RF cavity
Standard Condition – Simulation
Standard Condition – Test Description
Standard Condition – Data analysis and results
Cryogenic Condition – Simulation
Cryogenic Condition – Test Preparation
High Power (HP) configuration study
What’s next?
Achieved during my
summer program

## Slide 3
September 23, 2011
Jessica Cenni
2
Why a Dielectric Loaded RF cavity?
MUON ACCELERATOR
Objective: muons production, beam formation and acceleration within few milliseconds
Possible solution: helical cooling channel (=>RF structure inside a solenoid)
Consequent requirements for RF cavity:
short length
high electric field gradient (>20MV/m)
small radial dimension
first mode of resonance matched with external power source (Fermilab klystrons: 800 MHz)
But:
So:
Standard vacuum cavity DOESN’T work!

## Slide 4
September 23, 2011
Jessica Cenni
3
Insertion of dielectric material same frequency, smaller radius
Why a Dielectric Loaded RF cavity? (2)
Pillbox cavity
εr: relative dielectric permittivity
μr: relative magnetic permeability
But also lower quality factor
Cavity completely filled
with dielectric
where:
ε’: real part of
dielectric constant
ε’’: imaginary part of
dielectric constant
GOAL: large εr
GOAL: tgδ<10-4

## Slide 5
September 23, 2011
Jessica Cenni
4
Characterization of a DL RF cavity
Analysis of two main parameters:
  Resonance frequency
  Quality factor
Conditions considered:
  Standard - low power, room temperature
  Cryogenic - low power, cryogenic temperature (T=77K)
  High power
Means of the analysis:
Simulation in Superfish
Real Tests
Al2O3 ring
E field direction

## Slide 6
September 23, 2011
Jessica Cenni
5
For Real Tests
Stainless steel 316
covered with copper
L = 8.128 cm
D = 22.86 cm
Pillbox cavity
Rin=3.5cm
Rin=5.325cm
L
=
5.2
cm
L
=
7.75
cm
Al2O3 99.5%
Dielectric rings
Characterization of a DL RF cavity (2)
Small cylinder
Big cylinder

## Slide 7
September 23, 2011
Jessica Cenni
6
Standard Condition - Simulation
Empty cavity:
f = 1003.87 MHz
Q = 22772.3
Dielectric loaded cavity:
Frequency
897.27MHz
823.53MHz

## Slide 8
September 23, 2011
Jessica Cenni
7
Standard Condition - Simulation (2)
Quality Factor
Qsmall = 16123.6
Qbig = 12310.1

## Slide 9
September 23, 2011
Jessica Cenni
8
Cavity set up
- Cavity assembled through stainless steel bolts
- Systematic control of locking torque through torque meter
- Measurement through Network Analyzer (loop coupler)
Measurements for each configuration
- resonance frequency
 good correspondence with simulation
- loaded quality factor (derivation of unloaded quality factor through coupling coefficient)
 much lower than simulation (30-40% less)
Standard Condition – Test Description

## Slide 10
September 23, 2011
Jessica Cenni
9
Std Condition – Data analysis and results
Model used to analyze the data:
- lower Q = higher wall resistivity
 estimate an equivalent resistivity for the cavity
- Introduce this value in the model for the dielectric loaded cavity
 extract dielectric properties of the ceramic rings
Final results:
SMALL CYLINDER
BIG CYLINDER
f = 897.96 (±0.97) MHz
Q = 11823.1 (±1037.1)
f = 814.30 (±0.81) MHz
Q = 9415.89 (±828.6)
ε = 8.925 (±0.125)
tgδ = 7.28E-5 (±4.92E-5)
ε = 9.595 (±0.134)
tgδ = 8.17E-5 (±5.52E-5)

## Slide 11
September 23, 2011
Jessica Cenni
10
Cryogenic Condition – Simulation
Quality Factor
Qsmall = 28361.7
Qbig = 18966.9

## Slide 12
September 23, 2011
Jessica Cenni
11
Cryogenic Condition – Test Preparation
System set up:
proper bucket to contain the LN2
temperature sensor
feeding probe for He
Location choice
ODH requirements
need for power supply
TEST
First result:
Qempty = 23774.2

## Slide 13
Future High Power Tests
Location: MTA
Only big cylinder (for the smaller one the frequency shift is too small)
Teflon holder for the ceramic ring
Cavity filled with gas
September 23, 2011
Jessica Cenni
12
HP condition – Special requirements
PTFE
Cavity
Ceramic ring
avoid
breakdown
GOAL: study the feasibility of using a gas filled dielectric loaded RF cavity at HP

## Slide 14
September 23, 2011
Jessica Cenni
13
CONCLUSIONS
Achievements:
LOW POWER ANALYSIS
Description of the behavior of a dielectric loaded RF cavity under different conditions through simulation
At room temperature:
  Realization of a complete set of test for the empty cavity
  Analysis of the data and extraction of the dielectric properties of the ceramic
    quite good agreement with expected value, provided by the company, both for εr (exp. ≈ 9) and loss tangent (exp. ≈ 10-4)
    ERROR: mainly due to the sensitivity of the measurements to variation in real resistivity of the cavity
At cryogenic temperature:
  Set up of the equipment and definition of the procedure to follow for the test
  Realization of test for the empty cavity
HIGH POWER ANALYSIS
Design of Teflon holder for the ceramic ring to use during HP test

## Slide 15
September 23, 2011
Jessica Cenni
14
CONCLUSIONS (2)
What’s next?
Complete cryogenic tests and analyze the data to extract how the dielectric properties of the ceramic ring change with temperature and how this affects the behavior of the cavity
Complete the set up of HP configuration and run the test
Good resource for muon collider realization
If all the goals of the study will be achieved
Dielectric material:
  εr > 9, tgδ < 10-4
Electric gradient
  > 20MV/m
We’ll prove the feasibility of a HPDL RF cavity
such a cavity could allow the realization
of a helical cooling channel
AND
it could be applied also to other type
of muon cooling channel