## Slide 1: Progress of High Pressure RF Cavity Test
K. Yonehara
On behalf of HPRF test group
APC, Fermilab

## Slide 2: High pressure RF cavity test program
Demonstrate potential of HPRF cavity for cooling & accelerating a muon beam
  Study breakdown in a dense gas with a high RF gradient at a strong magnetic field
  Study influence of an intense beam on the cavity
  Investigate fast electronegative gases
  Study feasibility of gas filled dielectric loaded RF cavity
  Make an RF cavity for a real cooling channel

## Slide 3: Goal of first beam test
Does the cavity breakdown with an intense beam?
What is the influence of beam on the cavity?
How long does it take to recover RF field?
Study plasma dynamics in a dense gas at a high RF gradient
Search any clues to improve RF system

## Slide 4: Collaboration
C. Ankenbrandt, A. Bross, J. Cenni, M. Chung, G. Collura, G. Flanagan,
B. Freemire, P. Hanlet, R. P. Johnson, D. Kaplan, G. Kazakevitch,
A. Kurup, A. Moretti, J. Mukti, M. Neubauer, D. Neuffer,
M. Notani, G. Pauletta, M. Popovic, G. Romanov, A. Tollestrup,
Y. Torun, R. Sah, T. Schwarz,
+ AD external beam division
+ AD mechanical design
+ Machine shop
+ Rad/Hydrogen safety committees
+ Director/Division Heads
+ Operators & Technicians
Supported for many years by the DOE HEP SBIR-STTR program
m
Muons, Inc.

## Slide 5: MTA beam line and HPRF cavity
400 MeV H- beam transport line
RF cavity
+ collimator
in SC magnet
400 MeV H-
beam line
400 MeV H- beam
Beam pulse length 7.5 μs
5 ns bunch gap
109 H-/bunch
20 % of transmission at the collimator system
2 108 protons/bunch passes through the cavity
RF power inlet
Gas inlet
RF cavity
Circulator
+ RF damper

## Slide 6: High pressure RF cavity & collimator
Collimator
HPRF cell
RF power coax line
beam
beam
Gas
inlet
RF
inlet
Support rail
Phosphor
screen

## Slide 7: Assemble cavity, collimator, and toroid
HPRFCavity
2nd Collimator + Toroid
1st Collimator & Chromox-6
1st Collimator

## Slide 8: Beam profile monitor
CCD image
σhorizontal, x = 2.6 mm
σvertical, y = 3.9 mm
1st Collimator & Chromox-6
Mukti

## Slide 9: Observed beam intensity
Chart: 
Downstream toroid (handmade)
Upstream toroid (handmade)
Linac toroid 3 (UTR03, commercial)
Collimator
Gas filled RF cavity
Beam absorber
400 MeV
Proton beam
Upstream/Downstream
toroid pickups
RF pickup
Linac toroid 3 pickup
(commercial)
8/8/11
Maximum transmission efficiency at
the collimator (2mmφ) is 20 %.
By tuning the upstream beam
element, transmission efficiency
goes down to 2 %.
Ben Freemire
Beam intensity is measured by
a handmade toroid pickup coil
Beam intensity per beam pulse
# of beam pulses

## Slide 10: Taken data per pulse
Spectroscopic light (656 nm)
White light (656 nm)
RF pickup
Downstream toroid
RF pickup after beam (15 Hz)
CCD screen shot
RF forward
RF Refrected
Upstream toroid
Oscilloscopes are triggered by MTA beam signal
CCD screen shot was taken by hand(!)
We also monitored beam signal from a telescope
counter
Very clean RF signal due to
circulator + damper!
RF signals are cleaned by
circulator + damper!

## Slide 11: Run log
Date | Gas species | Pressure (psi) | Beam intensity*1
7/12 | N2 | 500 | High
7/14 | H2 | 800 | High
7/15 | H2 | 950 | High
7/19*2 | H2 | 500 | High
7/22 | H2 | 500 | High
7/25 | H2 | 800 | Low
7/27 | H2 | 500, 800, 950 | Medium
8/08 | H2 H2+N2 H2+SF6 | 950 950*3 500, 800, 950*3 | High
*1: “High” = 20 %, “Medium” = 7 %, “Low” = 2 % of transmission efficiency
*2: RF pickup probe was broken
*3: Concentration is 0.01 % at GH2 pressure 950 psi

## Slide 12
Study interaction of intense beam with dense H2 in high gradient RF field
Beam signal
(7.5 μs)
RF power is lost
due to plasma loading
RF power is recovered
when beam is off
RF pulse length
(80 μs)
p + H2 → p + H2+ + e-
Ionization process
1,200 e-/cm are generated by
incident p @ K = 400 MeV
ν= 802 MHz
Gas pressure = 950 psi
Beam intensity = 2 108 /bunch
Plasma loading in pure H2 gas
Equilibrium condition
Electron production rate
= Recombination rate

## Slide 13: Compare with breakdown event
RF power reduction
due to beam
RF power reduction
due to RF breakdown
RF breakdown light
Beam induced light
RF pickup and optical signals are quite different from these
at the breakdown event
Ne in beam induced plasma = 1014 electrons/cm3
Ne in breakdown plasma = 1019 electrons/cm3
PMT is saturated

## Slide 14: Model of RF power deposition per ionized electron
Alvin
Electron mobility in GH2
[V/cm/mmHg]
[cm/sec]
Power absorption of electron
For example, E0 = 20 MV/m, GH2 pressure = 950 psi
[Joules/electron/cycle/cm]

## Slide 15
Preliminary estimation of plasma loading effect in HPRF cavity for cooling channel
ν= 802 MHz
Pure H2 gas
Gas pressure = 950 psi
Beam intensity = 2 108 /bunch
From RF amplitude reduction rate,
RF power consumption by plasma
can be estimated
Joules/RF cycle
@ E = 20 MV/m
Hence, energy consumption by one
electron is (including with initial beam intensity change)
Joules/RF cycle/e/cm
electrons@ t = 200 ns
Both experimental result and model are excellent agreement within 20 %

## Slide 16: Estimate the number of ionized electron in the cavity from G4beamline simulation
Tom Schwarz
Proton momentum distribution as a function
of radial position in the cavity is taken into
account
Estimated # of ionized electrons per proton ~ 1200 e/cm

## Slide 17: Study electronegative gas effect
SF6 removes residual electrons

## Slide 18: Electron capture time in dopant
Electron capture rate =
# of electrons in the cavity at equilibrium RF signal
# of yield electrons by proton beam per second
It is NOT a 1/e time constant

## Slide 19: Compare with muon beam structure
E/p in helical 6D cooling channel is 1.6 V/cm/mm Hg
Electron capture time is fast enough to hold an E field in the cavity

## Slide 20: Radiation length in GH2 with 0.01 % SF6
Based on PDG
In case of SF6
[g/cm2] @ 1 atm
Mixture gas
ωj: fraction by weight
[m]
200 atm GH2 with 0.01 % SF6
[m]
200 atm GH2
10 % shorter than that in a pure GH2

## Slide 21: (Near) future plan
Run HPRF cavity with denser gas condition
  Presently, the maximum pressure is limited up to 1000 psi
  Ramp up the maximum pressure up to 1600 psi
Study more electronegative gas
  F2 and O2 are a very attractive electronegative gas
  Lowest Flammable Limit of O2 in GH2 is 7 %
  It is possible to mix O2 in GH2 with a reliable gas monitor system
Re-take HPRF cavity in a strong magnetic field
  E×B force will induce a plasma instability that will break dense plasma condition in the cavity

## Slide 22: Survey residual radiation dose level
Mukti
Observed residual dose level at the MTA beam line (on contact)
One day after ~200 beam pulses (beam tuning test at 3/25/11)
Note: There was no vertical corrector magnet
Beam went toward upper side of the beam pipe

## Slide 23: Conclusion
First beam test has been done
Energy deposition of single electron from RF power is 4.9 10-17 Joules/RF cycle/e/cm at E = 20 MV/m
So far, we do not see any crucial problems (show stopper) of practicality of HPRF cavity for cooling channel
Denser gas makes better RF recovery in pure GH2 condition (analysis is still underway)
Electronegative gas works extremely well
Need to investigate more electronegative gases
Plan to have another beam test
  B field effect
  Real pillbox cavity