## Slide 1: The Electron Ion Collider: Physics, Accelerator and Detector Technologies
Elke-Caroline Aschenauer (BNL)
Co-Associate Director for the Experimental Program

## Slide 2: The EIC Physics
How do color-charged quarks and gluons, and colorless jets, interact with a nuclear medium?
How do the confined hadronic states emerge from these quarks and gluons?
How do the quark-gluon interactions create nuclear binding?
gluon
emission
gluon recombination
?
How does a dense nuclear environment affect the quarks and gluons, their correlations, and their interactions?
What happens to the gluon density in nuclei? Does it saturate at high energy, giving rise to a gluonic matter with universal properties in all nuclei, even the proton?
=
How are the sea quarks and gluons, and their spins, distributed in space and momentum inside the nucleon?
How do the nucleon properties emerge from them and
their interactions?

## Slide 3: Deep Inelastic Scattering
large kinematic coverage:
center-of-mass energy √s: 28 – 140 GeV
access to x and Q2 over a wide range
Deep Inelastic Scattering (DIS):
As a probe, electron beams
provide unmatched precision of
the electromagnetic interaction
Direct, model independent
determination of parton
kinematics of physics
processes
s: center-of-mass energy squared
Q2: resolution power
x: the fraction of the nucleon’s
momentum carried by the
struck quark (0<x<1)
y: inelasticity

## Slide 4: What is needed to make this happen

## Slide 5: EIC Machine Parameters
Double Ring Design Based on Existing RHIC Facilities |  | 
Hadron Storage Ring: 40 - 275 GeV |  | Electron Storage Ring: 2.5 - 18 GeV
RHIC Yellow Ring and Injector Complex |  | Many Bunches, Large Beam Current - 2.5 A
Many Bunches, 1160 @ 1A Beam Current 9 ns bunch spacing |  | 9 MW Synchrotron Radiation
Bright Beam Emittance exp= 9 nm |  | Superconducting RF Cavities , 10MW Power
Flat Beam, Requires Strong Cooling |  | 
High Luminosity Interaction Region(s) |  | Electron Rapid Cycling Synchrotron
25 mrad Crossing Angle with Crab Cavities |  | Spin Transparent Due to High Periodicity
CDR: https://www.bnl.gov/ec/files/EIC_CDR_Final.pdf

## Slide 6: The EIC: A Unique Collider
EIC
LHC /RHIC
collide different beam species: ep & eA
consequences for beam backgrounds
  hadron beam backgrounds,
  i.e. beam gas events
   synchrotron radiation
asymmetric beam energies
boosted kinematics
  high activity at high |h|
Small bunch spacing: >= 9ns
crossing angle: 25mrad
wide range in center of mass energies
factor 6
both beams are polarized
 stat uncertainty: ~ 1/(P1P2 (L dt )1/2)
collide the same beam species: pp, pA, AA
 beam backgrounds
  hadron beam backgrounds,
  i.e. beam gas events, high pile up
symmetric beam energies
kinematics is not boosted
  most activity at midrapidity
moderate bunch spacing: 25 ns
no crossing angle yet
LHC limited range in center of mass energies
factor 2
RHIC wide range in center of mass energies :
 factor 26 in AA and 8 in pp
no beam polarization
 stat uncertainty: ~1/(L dt )1/2
Differences impact detector acceptance and possible detector technologies

## Slide 7: General Purpose Detector in EIC-CDR
Hadron Storage Ring
Electron Storage Ring
Electron Injector Synchrotron
Possible on-energy Hadron
injector ring
Hadron injector complex
Two possible locations – IP6 and IP8 – for detectors and Interaction Regions.
IP6 is the planned detector location for the project detector
7
electron beam
p/A beam
Backward
Forward

## Slide 8: EIC Detector Concept

## Slide 9: What is needed experimentally?
experimental measurements categories to address EIC physics:
Parton Distributions in nucleons and nuclei
Spin and
Flavor structure of nucleons and nuclei
QCD at Extreme Parton Densities - Saturation
Tomography
Spatial Imaging
Tomography Transverse Momentum Dist.
inclusive DIS
measure scattered lepton
multi-dimensional binning: x, Q2
reach to lowest x, Q2 impacts
Interaction Region design
semi-inclusive DIS
measure scattered lepton
and hadrons in coincidence
multi-dimensional binning:
x, Q2, z, pT, Q
particle identification over entire region is critical
exclusive processes
measure all particles in event
multi-dimensional binning:
x, Q2, t, Q
proton pt: 0.2 - 1.3 GeV
  cannot be detected in main detector
  strong impact on Interaction Region design
machine & detector requirements
∫Ldt:
1 fb-1
10 fb-1
10 - 100 fb-1
QCD at Extreme Parton Densities - Saturation

## Slide 10: EICUG: Yellow Report (YR) Initiative
Detector requirements and design driven by EIC Physics program and defined by EIC Community
Physics Topics ➝ Processes ➝ Detector Requirements
Physics Working Group:
  Inclusive Reactions
  Semi-Inclusive Reactions
  Jets, Heavy Quarks
  Exclusive Reactions
  Diffractive Reactions & Tagging
Detector Working Group:
  Tracking + Vertexing
  Particle ID
  Calorimetry
  DAQ/Electronics
  Polarimetry/Ancillary Detectors
  Central Detector: Integration & Magnet
  Far- Forward Detector & IR Integration
  Provides critical input for detector proposals – handoff between Physics & Detector Working Groups in “interactive detector matrix”: Collects physics requirements “real time”, lists all technologies for a given region, and links to studies that established the numbers
The EIC Users Group: EICUG.ORG
Report: https://arxiv.org/abs/2103.05419

## Slide 11: YR: Detector Requirements

## Slide 12: EIC General Purpose Detector: Concept
Forward-h
Backward-h
very low Q2
scattered lepton
Bethe-Heitler photons
for luminosity
particles from nuclear
breakup and
from diffractive reactions
electron beam
p/A beam
inclusive DIS:
Low Q2-Tagger
Luminosity Detector
Central
Detector
Lepton
Endcap
ECAL
HCAL
Tracking
HCAL
ECAL
Tracking
Magnet
Hadron
Endcap
PID
PID
ECAL
HCAL
PID
semi-inclusive DIS
Tracking
ZDC
Forward Tracking
exclusive DIS

## Slide 13: EIC Experimental Equipment
Any general purpose EIC Detector is complex
Overall detector requirements:
Large rapidity (-4 < h < 4) coverage; and far beyond in especially far-forward detector regions
High precision low mass tracking
  small (m-vertex) and large radius (gaseous-based) tracking
Electromagnetic and Hadronic Calorimetry
  equal coverage of tracking and EM-calorimetry
High performance PID to separate p, K, p on
track level
  also need good e/p separation for scattered electron
Large acceptance for diffraction, tagging, neutrons from nuclear breakup: critical for physics program
  Many ancillary detector integrated in the beam line: low-Q2 tagger, Roman Pots, Zero-Degree Calorimeter, ….
High control of systematics
  luminosity monitor, electron & hadron Polarimetry
Integration into the Interaction Region is critical

## Slide 14: Requirements
EIC-UG Yellow Report results:
Detailed subdetector simulations and technology performance evaluations tabulated
  Interactive version: https://physdiv.jlab.org/DetectorMatrix
performance difference for different magnetic fields (1.4 T vs. 3 T) were evaluated
Example of physics and detector technology requirement for IR/Roman Pots in backup
B = 3 T

## Slide 15: EIC General Purpose Detector
EIC general purpose Detector around a new 3T Solenoid with hermetic coverage
Important to note:
low multiplicity per event: < 10 tracks
h > 2: avg. hadron track momenta @ 141 GeV: ~20 GeV
No pileup from collisions 500 kHz @1034 cm-2s-1  coll. every 200 bunches
radiation environment much less harsh than LHC
electron
p/A

## Slide 16: Subdetector Technology Choices
Alternatives to primary technologies for the different subdetectors
fulfilling the requirements
 risk reduction

## Slide 17: MAPS mVertex
For primary and secondary vertex reconstruction
Low material budget: 0.05% X/X0 per layer
High spatial resolution: 10 mm pitch MAPS
 ref. Alice ITS3
Compromise:
  20 mm (or smaller) pixels and ~0.3% X/X0 per layer
Barrel+ Disks for endcaps

## Slide 18: Endcaps: MPGDs
To improve momentum resolution at large rapidities.
Spatial resolution well below 100 mm
Large-area detectors possible
Cost efficient compared to silicon
EIC R&D: large 2D GEM module
~900mm

## Slide 19: Electro-Magnetic Calorimeter
Applications
  Scattered electron kinematics measurement at large |h| in the e-endcap
  Photon detection and energy measurement
  e/h separation (via E/p & cluster topology)
  p0/g separation  may also consider a highly segmented preshower combined with ToF and tracking  three in one
Anticipated stochastic term in energy resolution & available space
Other considerations
  Fast timing
  Compactness (small X0 and RM)
  Tower granularity
  Readout immune to the magnetic field
h | [-4 .. -2] | [-2 .. -1] | [-1 .. 1] | [1 .. 4]
sE/E | ~2%/√E | ~7%/√E | ~10-12%/√E | ~10-12%/√E
space | ~50 cm | ~50 cm | ~30 cm | ~40 cm
EIC Yellow Report

## Slide 20: Crystals
High resolution EmCal in the electron-endcap for the scattering electron measurements
PWO where space is tight, and the highest possible energy resolution is required
Scintillating glass (EIC R&D) otherwise
  More cost efficient, easier manufacturing
  Potentially better optical properties
Feb 2020: 2cm x 2cm x 20cm (7 X0)
2019: 2cm x 2cm x 4cm
2018: 1cm x 1cm x 1cm
Example: SC1 glass
CRYTUR
SICCAS
PWO: vendor characterization
Dec 2020: 2cm x 2cm x 40cm ( 10-20 X0)

## Slide 21
EIC PID
needs
are more demanding
then your
normal
collider detector
EIC
needs absolute
particle numbers at
high purity and low
contamination
E

## Slide 22: Particle ID
In general, need to separate:
Electrons from photons  4p coverage in tracking
Electrons from charged hadrons  mostly provided by calorimetry
Charged pions, kaons and protons from each other  Cherenkov detectors
  Cherenkov detectors, complemented by other technologies at lower momenta
P [GeV]
Pythia MC
Rapidity | π/K/p and π0/γ | e/h | Min pT (E)
-3.5 − -1.0 | 7 GeV/c | 18 GeV/c | 100 MeV/c
-1.0 − 1.0 | 8-10 GeV/c | 8 GeV/c | 100 MeV/c
1.0 − 3.5 | 50 GeV/c | 20 GeV/c | 100 MeV/c
Physics requirements:
Illustration of PID detectors achievements:
Need more than one technology to cover the entire momentum ranges at different rapidities

## Slide 23: DIRC
Radially compact ( ~ 5cm)
high-performance DIRC with better optics and <100 ps timing (/K up to ~6 GeV/c)
Re-use BaBar quartz bars ?
Integration into a 4 detector can be challenging
hpDIRC
Detector Surface
Solid Radiator
Particle
Track
Cherenkov Photon Trajectories
Focusing Optics
Mirror

## Slide 24: Dual radiator RICH
Hadron PID in the forward/hadron end-cap
Use a combination of aerogel and CmFn with indices of refraction matching EIC momentum range in the forward endcap
Similar to LHC-b, HERMES, JLAB/Hall-B, …
  Continuous >3s p/K separation up to 60 GeV/c and K/p separation to higher momenta
  >3s e/p separation up to ~15 GeV/c
e/p
p/K
K/p

## Slide 25: Modular-RICH (mRICH)
For hadron PID in the electron end-cap
Compact version of a conventional aerogel-based proximity focusing RICH
Expect p/K 3s separation up to 8-10 GeV/c
  Was also tested with SiPM readout
  LAPPD readout – spring 2021
~20 cm
3s

## Slide 26: High resolution timing technologies
UV-enhanced version
MCP-PMT / LAPPD
  QE routinely >20%
  >90% gain uniformity
  Single photon TTS <50 ps
  Performance in high B field is still of a concern
UV
(AC)-LGAD
UV-enhanced version -> TOF!
Argonne 10 mm
pore prototype
Expecting affordable detectors with <10ps
timing on the EIC CD-2 time scale
  Detectors can provide <20ps / layer
  AC-coupled variety gives 100% fill factor and potentially a high spatial resolution (dozens of microns) with >1mm large pixels

## Slide 27: Streaming Readout Architecture
6.10.08 & 6.10.09 Electronics & DAQ/Computing
EIC Yellow Report – Readout and DAQ FJ Barbosa, K Chen, J Huang
30 July 2020
Possible at EIC as data rates manageable
(500 kHz, O(100) Gbps)

## Slide 28: EIC Project Status
The EIC received in the 2015 Long Range Planning of the NSAC the following recommendation
“We recommend a high-energy high-luminosity polarized EIC as the highest priority for new facility construction following the completion of FRIB”
“… In summary, the committee finds a compelling scientific case for such a facility (the EIC). The science questions that an EIC will answer are central to completing an understanding of atoms as well as being integral to the agenda of nuclear physics today. In addition, the development of an EIC would advance accelerator science and technology in nuclear science; it would as well benefit other fields of accelerator-based science and society, from medicine through materials science to elementary particle physics.”
Released July 24, 2018
January 2020: CD-0 & site selection  BNL
January 2021: DOE CD-1 Review  Move forward to CD-1
Accelerator Technical Reviews | Spring -- Autumn 2021
Start Preliminary Design | April 2021
Detector Proposals Submitted | December 2021
Selection of Project Detector | March 2022
Start Earned Value Tracking | Summer 2022
Clarify In-kind Deliverables - Agreements | Summer/Fall 2022
Goal for CD-2 Approval | January 2023
Goal for CD-3 Approval Goal for CD-4 Early Project Completion | March 2024 July 2031

## Slide 29: EIC Experimental Equipment Planning
The DOE-NP supported EIC Project includes
one detector and one Interaction Region
  The total detector cost: $250M Dir+Bur+Esc excluding contingency
  The DOE part: $152M (Dir+Bur+Esc excluding contingency ) the rest is assumed in-kind
  Costs for one Interaction Region included in accelerator scope: ~$183M (Dir+Bur+Esc excluding contingency )
The EIC facility is capable supporting a science program that includes two detectors and two interaction regions.
  2nd IR & Detector
  All stakeholders agree that a second IR and detector within the same timeline is
  desirable and will enhance the science output of the facility
  Costs depend on the complexity, assuming IP2 similar to IP-1  $400 M
  Routes to make this possible are being explored.

## Slide 30: Experimental Program Preparation
Yellow Report and EIC Conceptual Design Report are both available and include the reference detector concept.
BNL and TJNAF Jointly Leading Process to Select Project Detector | BNL and TJNAF Jointly Leading Process to Select Project Detector | 
2020 | Call for Expressions of Interest (EOI) https://www.bnl.gov/eic/EOI.php | May 2020
 | EOI Responses Submitted | November 2020
 | Assessment of EOI Responses | On-going
2021 | Call for Collaboration Proposals for Detectors https://www.bnl.gov/eic/CFC.php | March 2021
 | BNL/TJNAF Proposal Evaluation Committee | Spring 2021
 | Collaboration Proposals for Detectors Submitted | December 2021
✔️ | Decision on Project Detector | March 2022
Current EIC Detector collaboration efforts
  ECCE: https://www.ecce-eic.org
  EIC@IP6: https://sites.temple.edu/eicatip6/
  Critical to have excellent detector proposals with science and technology complementarity integrated

## Slide 31: Take Away Message
Current
knowledge about
nucleon structure
and the glue
with EIC
Why EIC now?
“all stars align”:
theory developments will allow to obtain the answers to the big questions discussed
detector technologies allow for a collider detector with high resolution, wide acceptance and particle identification
BUT MOST IMPORTANTLY
accelerator technologies allow to built a collider with
  high luminosity
  highly polarized electron and light hadron beams
  a wide range in center of mass energies
  hadron beams with highest A
  demanding acceptance requirements can be realized in IR design
EIC science program will profoundly impact
our understanding of the inner structure
of the world around us
uniquely tied to a future high energy, high luminosity,
polarized ep / eA collider
never been measured before & will never without

## Slide 33: What is needed to address the EIC Physics
polarized electron and hadron (p, He-3) beams:
access to spin structure of nucleons and nuclei
Spin vehicle to access the spatial and momentum structure of the nucleon in 3d
Full specification of initial and final states to probe q-g structure of NN and NNN interaction in light nuclei
unpolarized nuclear beams: d to Pb
accessing the highest gluon densities  saturation
quark and gluon interact with a nuclear medium
high luminosity 1033-1034 cm-2s-1 :
mapping the spatial and momentum structure of nucleons and nuclei in 3d
access to rare probes, i.e. Ws
large kinematic coverage:
bridge between measurements in different regimes (s, x, Q2)
access to x and Q2 over a wide range
 center-of-mass energy √s: 20 – 140 GeV

## Slide 34: What is needed experimentally?
US-EIC:
polarization, ion species together with
its luminosity and √s coverage makes
it a completely unique machine world-wide.
Luminosity - √s Energy and EIC Physics:

## Slide 35: EIC Collider Concept
Design based on existing RHIC,
RHIC is well maintained, operating at its peak
Hadron storage ring 40-275 GeV (existing)
  RHIC Yellow Ring
  many bunches, 1160 @ 1A beam current
  bright beam emittance exp= 9 nm, flat beam
  need strong cooling
Electron storage ring (2.5–18 GeV, new)
  many bunches,
  large beam current (2.5 A) 10 MW S.R. power
  s.c. RF cavities
  Energy independent radiation damping
Electron rapid cycling synchrotron (new)
  1-2 Hz
  Spin transparent due to high periodicity
High luminosity interaction region(s) (new)
  L = 1034cm-2s-1
  Superconducting magnets
  25 mrad Crossing angle with crab cavities
  Spin Rotators (longitudinal spin)
  Forward hadron instrumentation
EIC@BNL

## Slide 36: Why a Crossing Angle
Brings focusing magnets close to IP
 high luminosity
Beam separation without separation dipoles
 reduced synchrotron radiation
But significant loss of luminosity
Solution: Crab crossing
Head-on collision geometry is restored by rotating the bunches before colliding (“crab crossing”)
Bunch rotation (“crabbing”) is accomplished by transversely deflecting RF resonators (“crab cavities”)
Actual collision point moves laterally during bunch interaction
Challenges
    Bunch rotation (crabbing) is not linear due to finite
    wavelength of RF resonators (crab cavities)
    Severe beam dynamics effects
    Physical size of crab cavities
Significant impact on main and
forward detector acceptance

## Slide 37: Worldwide Interest in EIC Physics
Formed 2016
February 2021: 1253 collaborators, 33 countries, 251 institutions
Map of institution’s locations
The EIC Users Group: EICUG.ORG
Size of EICUG has continuously grown since its formation, in particular after the award of CD0 / site-selection.
Expect growth to continue through the phases of EIC project.
Strong international representation

## Slide 38: IR Requirements from Physics
 | Hadron | Lepton
Machine element free region | High Luminosity  beam elements need to be close to IP EIC: +/- 4.5 m for main detector beam elements < 1.5o in main detector volume | 
Beam pipe | Low mass material i.e. Beryllium | 
Integration of Detectors | Local Polarimeter | Low Q2-tagger Acceptance: Q2 < ~0.1 GeV
Zero Degree Calorimeter | 60cm x 60cm x 2m @ ~30 m | 
scattered proton/neutron acc. all energies for ep | Proton: 0.18 GeV < pt < 1.3 GeV 0.5 < xL< 1 (xL = /EBeam) Neutron: pt < 1.3 GeV | 
scattered proton/neutron acc. all energies for eA | Proton and Neutron: Q < 6 mrad (√s=50 GeV) Q < 4 mrad (√s=100 GeV) | 
Luminosity | Relative Luminosity: R = L++/--/L+-/-+ < 10-4 Flexible spin patters for both beams 1: +-+--+-++-+- 2: -+-++-+--+-+ 3: ++--++--++-- 4: --++--++--++ | 
 |  | g acceptance: +/- 1 mrad  dL/L < 1%
 | Hadron | Lepton
Machine element free region | High Luminosity  beam elements need to be close to IP EIC: +/- 4.5 m for main detector beam elements < 1.5o in main detector volume | 
Beam pipe | Low mass material i.e. Beryllium | 
Integration of Detectors | Local Polarimeter | Low Q2-tagger Acceptance: Q2 < ~0.1 GeV
Zero Degree Calorimeter | 60cm x 60cm x 2m @ ~30 m | 
scattered proton/neutron acc. all energies for ep |  | 
scattered proton/neutron acc. all energies for eA | Proton and Neutron: Q < 6 mrad (√s=50 GeV) Q < 4 mrad (√s=100 GeV) | 
Luminosity | Relative Luminosity: R = L++/--/L+-/-+ < 10-4 Flexible spin patters for both beams 1: +-+--+-++-+- 2: -+-++-+--+-+ 3: ++--++--++-- 4: --++--++--++ | 
 |  | g acceptance: +/- 1 mrad  dL/L < 1%
most demanding

## Slide 39: EIC General Purpose Detector
EIC general purpose Detector around
a new 3T Solenoid
Hermetic coverage
 as close as possible to 4p
Coverage: 2o < Q < 178o (-4<h<4 ) with 2p in F
Technologies based on Generic EIC Detector R&D developed by EIC-UG members
https://wiki.bnl.gov/conferences/index.php/EIC_R%25D
9.0m
electrons
hadronic calorimeters
TPC
e/m calorimeters
PID/ RICH detectors
silicon trackers
GEM trackers
solenoid coils
Barrel Hadronic calorimeter not shown
hadrons
Flow down of Physics Requirements
to detector design has been determined in 2020 EIC-UG
Yellow Report Initiative
http://www.eicug.org/web/content/yellow-report-initiative

## Slide 40: Detector integrated in EIC Project
Space considerations versus Magnet size:
Conclusion:
to fit all detectors in the existing magnet with bore 2.8 meter will be challenging and it is possible some functionality has to give. For a new magnet, a bore of 3.2 meter is a safer option. Only in one of these four cases, we needed 5 cm more.

## Slide 41: Tracking/Material Budget
Vertex + central + forward / backward tracker layout ( moderate momentum resolution, vertex resolution ~20 mm)
At most 3T central solenoid field (maximize B*dl integral at high |h|)
Low material budget
  Minimize bremsstrahlung and conversions for primary particles
  Improve tracking performance at large |h| by minimizing multiple Coulomb scattering
  Minimize the dead material in front of the high resolution e/m calorimeters
Central area of beampipe (around IP):
  ~1.5m of beryllium to minimize multiple scattering for low Pt particles
Low-mass exit window for far-forward particles
Few % radiation length material thickness for the required angular range (low angle)

## Slide 42: Central tracker
Possible endcap upgrade for EIC
For momentum reconstruction
TPC: low material budget tracker
(similar to STAR, sPHENIX, ALICE... )
Sufficient spatial resolution
dE/dx for low-momentum PID
-1 < h < 1

## Slide 43: Sampling EmCal
~13.3%/√E + 3.5%
Light collection uniformity can yet be improved
Scintillating Fibers embedded in a W/epoxy mix
W/SciFi spacal
Pb/Sc shashlyk
Well established technology
  HERA-B, ALICE, PHENIX, PANDA, …
Medium energy resolution ~7..13%/√E
Compact (X0 ~7mm or less), cost efficient

## Slide 44: Hadronic Calorimeter
Main purpose: jet energy measurement
  Particle Flow Algorithm usage anticipated (where HCal role is identification and energy measurements of the neutral hadrons, namely neutrons and KL)
In general the “conventional” hadronic calorimetry is considered per default
Anticipated stochastic term in energy resolution & depth
Other considerations
  Space!
  Interplay with EmCal in a “binary” EmCal+HCal configuration
  Tower granularity (~10 x 10 cm2 suffices)
  Readout immune to the magnetic field
h | [-4 .. -1] | [-1 .. 1] | [1 .. 4]
sE/E | ~50%/√E + 10% | ~100%/√E + 10% | ~50%/√E + 10%
depth | ~5 lI | ~5 lI | ~6-7 lI

## Slide 45: Fe/Sc sandwich
HCAL in endcap
Compact LEGO-style design
  Can be used with a mixed Fe/Pb absorber
STAR 2019 Fe/Sc design
~60%/√E expected
EIC 2014 Pb/Sc prototype
~890mm

## Slide 46: Fe/Sc ( barrel)
Similar as used in sPHENIX
  Solid 32-sector steel frame, but only ~3.5 lI
  Moderate energy resolution
Scintillator plate with embedded WLS fiber
~6 m
2017 test beam data

## Slide 47: Additional e- ID
To improve e-identification for leptonic/semi-leptonic decays.
In addition to Calorimeters and Cherenkov detectors in the hadron-endcap considering TRD.
GEM -TRD/Tracker :
  e/p rejection factor ~10 for momenta between 2-100 GeV/c from a single ~15cm thick module.
  Very precise Tracking segment behind dRICH:
Thickness [cm]

## Slide 48: Far forward (hadron going) region
IP
p/A
Detector | Angular accept. [mrad] | Pt coverage
ZDC @ ~30m | <5.5 ( | pT<1.3 GeV
Roman Pots | 0*<<5.0 ( | *Low pT(t) cutoff (beam optics)
Off-Momentum Detectors | 0.0< < 5.0 ( | Low-rigidity particles from nuclear breakups
B0 forward spectrometer | (4.6< | High pT(t)
Detector | Angular accept. [mrad] | Pt coverage
ZDC @ ~30m |  | pT<1.3 GeV
Roman Pots |  | *Low pT(t) cutoff (beam optics)
Off-Momentum Detectors |  | Low-rigidity particles from nuclear breakups
B0 forward spectrometer |  | High pT(t)

## Slide 49: Far-forward detectors
(5.5 < 𝜽 < 20.0 mrad)
Warm space for detector package insert located inside a vacuum vessel to isolate from insulating vacuum.
Higher granularity detectors needed in this area ( MAPS) with layers of fast-timing detectors (LGADs)
Shape and coverage of B0 tracker needs to be further evaluated
Space for detectors
B0-spectrometer
Roman-Pots and Off-momentum detectors
Low Pt particles Pt < 1.3 GeV
RPs: movable, integrated into the vacuum system
Fast Timing and moderate granularity
(500x500
AC-LGADs
0.0* (10σ 𝑐𝑢𝑡) < 𝜽 < 5.0 mrad

## Slide 50: Call for Detector Proposals Issued
Call for proposals for
  Detector 1 is within the scope of the EIC project and should be based on the “reference” detector and must address the EIC White Paper and NAS Report science case.
  Detector 2 should address major parts of the science described in the EIC White Paper and possibly science beyond that and enable some complementarity to Detector 1.
Evaluation Criteria:
  science capabilities
  risk, cost, and schedule of the proposed experiment, specifically for detector technology, design choices
  strength of the collaboration
Who Evaluates:
  scientific-technical committee of renowned and independent subject matter experts
  Members of the Detector Advisory Committee
Call Details: https://www.bnl.gov/eic/CFC.php
Deadline: 1st of December
Selection of Detectors by Early 2022