## Slide 1: High Efficiency RF Source Development
Lawrence Ives, Calabazas Creek Research, San Mateo, CA. USA
.
100 kW, 1.3 GHz Magnetron w/ Phase and amplitude control
Magnetron frequency/phase control with varactors
100 kW, High efficiency, L-Band klystron
350 – 700 MHz, 200 kW Power Grid Tube RF sources
700 MHz Multiple Beam IOT

## Slide 2: A 100 kW, 1.3 GHz Amplitude and Phase Controlled Magnetron for Accelerators
Michael Read1, R. Lawrence Ives1, Brian Chase2, John Reid2, Chris Walker3 and Jeff Conant3
[1] Calabazas Creek Research Inc., San Mateo, CA 94404
[2] Fermi National Accelerator Laboratory Batavia IL 60510-5011
[3] Communications and Power Industries LLC, Beverly, MA, USA 01915
Funded by the US Department of Energy under SBIR grant DE-SC0011229

## Slide 3: Program
Develop 100 kW, 1.3 GHz magnetron with fast amplitude and phase control
Specifically for high Q (superconducting) cavities
Fast amplitude control by phase modulating the locking signal to shift power to side bands
  Side bands are rejected by high Q cavity
  Power into the cavity = Magnetron power less side band power

## Slide 4: CPI Magnetron
1.30 GHz
100 kW peak
10 kW average

## Slide 5: Packaged Magnetron System

## Slide 6: Phase Modulation
122° Modulation
60° Modulation
No Modulation
50 MHz Phase Modulation
2 MHz
2 MHz
1 MHz

## Slide 7: Amplitude Control
Required 316 W of drive power to lock

## Slide 8: Efficiency
Efficiency varied between 81% and 87%, depending on parameters

## Slide 9: Cost for 100 kW System
(Exclusive of high voltage supply)
Magnetron | $40,000
500 W SS amplifier | $17,000
Circulator w waveguide | $20,000
Controls | $10,000
Packaging | $10,000
Total | $97,000
Magnetron System Cost ~ $1/Watt
(Klystron cost ~ $4/Watt)

## Slide 10: Compact and Efficient Magnetron Source with Fast Phase and Frequency Control
Michael Read Calabazas Creek Research, Inc.
Lili Ma, Joseph Frisch
SLAC National Accelerator Laboratory
Chris Walker
Communications & Power Industries – Beverley
Funded by US Navy Contract N6833520C0822

## Slide 11: Goals
Develop S-Band, 5 kW magnetron with frequency and phase control
Minimize weight and power
Eliminate requirement for circulator

## Slide 12: Approach
Varactor tuning of magnetron by changing capacitance
Capacitor
3D MAGIC Simulation PI Mode Fields
(mm)
0.5 pF swing 5 MHz shift
Simulated Performance

## Slide 13
Spice Simulations Determined Diode Requirements
5 MHz
200 V
400 V
  20 diodes in series C = 0.2pF - 1.5pF
  Bias voltage 13V – 38V
  Frequency Shift 6 MHz
Microsemi GC1712

## Slide 14: Key Innovations
Adaptive feed forward for frequency tuning
Feed back to control low frequency phase error.
adaptive feed forward to cancel 44kHz power supply resonance.
Optional : analog loop for fast, high bandwidth control.
Digital Control system
Digital feed back
Adaptive feed forward
Fast Analog Control System
Phase error
Frequency step out
CCR preparing proposal for high power system for accelerators

## Slide 15: A 1.3 GHz 100 kW Ultra-high Efficiency Klystron
[1] Calabazas Creek Research Inc., 490 Port Drive San Mateo, CA 94404
[2] Leidos, Center for EM Manager DEOST, Billerica, MA 01821
Communications & Power Industries, LLC, Palo Alto, CA 95304
Funded by the US Department of Energy under SBIR grant DE-SC0017789.
Michael Read1, Aaron Jensen2, R. Lawrence Ives1, Thomas Haberman1, David Marsden1, and George Collins1

## Slide 16: Core Oscillation Method (COM)*
  Voltage 53.5 kV
  Current 2.46 A (0.2 mpervs)
  Cavities 7
  Simul. Efficiency 83%
  RF structure length 250 cm

## Slide 17: Assembly in Progress
Most all parts received
Cold test and assembly in progress
Test set being configured
Testing in February-March 2020

## Slide 18: Multiple Beam Power Grid Tubes for High Frequency and High-Power Operation
Lawrence Ives, Michael Read, David Marsden, Thuc Bui Calabazas Creek Research, San Mateo, CA. USA
Ricky Ho, Nileshwar Chaudar, Christopher McVey, Tom Cox Communications & Power Industries, LLC Palo Alto, CA 94304 USA
James M. Potter JP Accelerator Works Los Alamos, NM USA
This research funded by DOE SBIR Grant DE-SC0018838
.

## Slide 19: 25 kW 425 MHz Triode-based RF Source
YU-176 Triode
Efficiency 90% (Class C)

## Slide 20: Beam Power for 200 kW RF Source
Eight YU-176 grid cathode assemblies
230 kW of beam power

## Slide 21: 350 MHz Cavities
MB triode tube installs from top (blue)
Single input cavity below tube
Upper and lower output cavities with coax output between
Upper cavity is frequency tuning element
Lower cavity is variable output coupling element

## Slide 22: Output Cavity Simulation
Tuning range for output cavity (325 – 500 MHz)

## Slide 23: Gain
Gain ~14 dB for triode-based sources
Requires 6.5 kW driver 200 kW RF source
Driver options: - Solid State – expensive, may be difficult to find Developing Single-beam triode driver

## Slide 24: 200 kW CW, 350 MHz RF System
Net Gain 28 dB
Net Efficiency ~72%
High power tests scheduled for January – February 2021

## Slide 25: 200 kW CW RF Source Cost 350 – 700 MHz
Product Price Efficiency
15 kW Driver $45K 90% 200 KW MB source $55K 80%
Total $100K
Triode-based system $0.50/Watt ~72%
Klystron: ($4/W) 50-60% MBIOT: ($2-$4/W) 65-70% Solid State: ($4/W) ~50%

## Slide 26
HIGH-EFFICENCY, HIGH AVERAGE POWER INDUCTIVE OUTPUT TUBES
Work supported by the US Department of Energy Grant No. DE-SC0019800
H.P. Freund,1 R.L. Ives,1 W. D. Sessions2 and T. Bui1
1Calabazas Creek Research, San Mateo, CA
2Georgia Tech Research Institute, Atlanta, GA
Communications & Power Industries, LLC, Palo Alto, CA

## Slide 27
MBIOT SIMULATON
Adding 3rd harmonic to drive signal to increase efficiency
Six beam Design
f =700 MHz
30 kV/6.67 A
  Simulated efficiency with the 3rd harmonic » 91%
3rd harmonic power ½ of fundamental drive power
Performance as function of relative phase of fundamental and 3rd harmonic

## Slide 28
THE INPUT COUPLER
N-Beam, Coax-Conical-Coax Power Splitter
  Single RF Driver
  Direct coupling to individual guns
  Challenge: Include 3rd Harmonic Drive
Simulations via CST-MWS®
Input coupler for CPI-Thales 700 MHz MBIOT

## Slide 29
METAL GRID DESIGN
Current IOTs use pyrolytic graphite (PG) grids
Difficult to fabricate
Expensive
Relatively low yield
This MBIOT will use molybdenum grids
Reduced power loading with multiple beams
Thermomechanical analysis predicts good performance
Significantly cheaper with higher yield
Two-year program to design, build and test MBIOT started in August

## Slide 30: Summary
RF Sources and Key Features
Magnetron System 100 kW 1.3 GHz Amp/Phase Control $1/Watt
Completed
High Efficiency Klystron 100 kW CW 1.3 GHz 80% Freq/Pwr Scalable
Triode-base RF sources 200 kW CW 350–700 MHz $0.5/Watt compact Design complete – assembly in progress
Multiple Beam IOT 700 MHz 200 CW kW 80% Reduced cost Fully Funded – Final design in progress – high power testing 2022
Magnetron using varactors S-Band 5 MHz tuning Very compact Proof of principle design complete – proposals in progress