## Slide 1: Higher Efficiency High Power RF Generation
Erk Jensen/CERN

## Slide 2: Improving Energy Efficiency: a Duty and an Opportunity
www.iea.org: Energy Efficiency is one of the cornerstones of any strategy
Our obligations:
  Be aware and make aware of efficient energy use and energy conversion
  Make good design choices to minimize “waste”!
  Design and use energy-efficient equipment!
  Monitor and plan energy use (Energy Management)
  Recover otherwise “wasted” energy!
This is our duty to society, but also a necessity for acceptance of future projects!
The size of HEP projects, or , allows dedicated R&D. Benefits:
  Concepts and designs developed to improve energy efficiency in accelerators will be relevant for society at large.
  Significant savings in operational cost.
  From: European Strategy Open Forum, Granada 2019,”Energy Efficiency of HEP Infrastructures” https://indico.cern.ch/event/808335/contributions/3365146/

## Slide 3: Excerpt from Letter of Intent: Areas of R&D:
Higher efficiency klystron development involving modern concepts like “BAC”, “COM”, “CSM” and others. Application also to Inductive Output Tubes (IOTs),
Investigate stabilization, phase control and combination of magnetron RF sources for possible accelerator use.
Development of scalable power combiners to combine thousands of inputs (of kW level) in few stages to reach power levels necessary to operate large particle accelerators,
Development, jointly with industry, GaN-based SSPA modules, applying techniques to increase efficiency at high power levels (Class F, multi-harmonic terminations …)

## Slide 4: Example FCC-ee: Energy Needs
FCC-ee is a large (Ø 31 km) Electron-Positron Ring Collider
FCC-ee will be dominated by synchrotron radiation losses.
It requires 110 MW RF power in CW!
The yearly energy consumption for the FCC-ee alone (assuming 5500 h operation and an overall conversion efficiency of 50%) will be in the order of 1.2 TWh – the consumption of a small town!
Higher efficiency  less waste  gained resources!

## Slide 5: Example FCC-ee: Energy Conversion
Grid to DC:
RF power generation!
RF distribution!
losses in cavities
RF to beam
Note: largest impact by RF power generation

## Slide 6: A scalable problem – a scalable solution
The need to improve energy efficiency is most visible with a large, energy hungry installation like FCC-ee.
But 10 smaller infrastructures requiring “only” 10% of its energy, have the exact same problem.
… or 100 “small” infrastructures requiring only 1% of its energy need …
There exist maybe 30,000 smaller accelerators in the world (medical, industrial, …) with together a huge consumption and a large potential to save resources.
If we find a solution for higher efficiency RF sources, RF sources for all applications will potentially profit!

## Slide 7: High Efficiency Klystrons

## Slide 8: High-Efficiency klystron activities at CERN
Project |  | Technology | Design status | System status | Industrial partner | Prototype schedule
LHC 400 MHz, 350 kW CW | 70% *) | CSM | completed | ongoing | Thales | 18 months
FCC 400 MHz 600 kW CW | 88% | TS MBK or CSM | ongoing |  | Thales? | 36 months
FCC 800 MHz 1.3 MW CW | 88% | TS MBK or CSM | ongoing |  | Thales? | 
ILC 1.3 GHz 10 MW pulsed | 85% | TS MBK | completed |  | Thales/Canon/CPI | 
CLIC 1 GHz 24 MW pulsed | 85% | TS MBK | completed |  | Thales/Canon/CPI | 
X-band 8 MW pulsed | 56%*) | COM | completed | completed | Canon | 12 months
X-band 50 MW pulsed | 70%*) | COM | completed | completed | CPI | 24 months
36 GHz 2.5 MW | 35% | HOM MBK | completed | completed | On hold | 
Project |  | Technology | Design status | System status | Industrial partner | Prototype schedule
LHC 400 MHz, 350 kW CW | 70% *) | CSM | completed | ongoing | Thales | 18 months
FCC 400 MHz 600 kW CW | 88% | TS MBK or CSM | ongoing |  | Thales? | 36 months
FCC 800 MHz 1.3 MW CW | 88% | TS MBK or CSM | ongoing |  | Thales? | 
ILC 1.3 GHz 10 MW pulsed | 85% | TS MBK | completed |  | Thales/Canon/CPI | 
CLIC 1 GHz 24 MW pulsed | 85% | TS MBK | completed |  | Thales/Canon/CPI | 
X-band 8 MW pulsed | 56%*) | COM | completed | completed | Canon | 12 months
X-band 50 MW pulsed | 70%*) | COM | completed | completed | CPI | 24 months
36 GHz 2.5 MW | 35% | HOM MBK | completed | completed | On hold | 
*) Retrofit to existing tube, re-use of modulator, solenoid and frame.
  CSM: Core Stabilisation Method
  TS: Two-stage
  MBK: Multi-beam Klystron

## Slide 9: High-Efficiency klystron activities at CERN
S-band
Industry
X-CPI
50 MW
X-Canon
6 MW
X-Toshiba
PPM, 50 MW
L-MBK ILC, 10 MW
L-MBK CLIC, 20 MW
UHF-LHC
0.3 MW
Klystrons for science
L-ESS,1.5 MW
UHF-B-factory
1.25 MW
(µA/V1.5)
ITT 2960
33 MW
L-SNS, 0.55 MW
S-SLAC
65 MW
S-SLAC
150 MW
UHF-LHC
0.35 MW
X-BVERI
50 MW
X-CERN/CPI
50 MW
X-CERN/Canon 8 MW
L-FCC, 1.5 MW
HE industrial prototype ; off shelf
S-Canon
7.5 MW
L-MBK/TS
CLIC, 24 MW
HE design, CERN (PIC simulations)

## Slide 10: LHC RF System – a 1st step for validation
These 16 klystrons TH2167 provide the necessary RF power to accelerate the LHC beams to collision energy.
O. Brunner

## Slide 11: LHC RF System – a 1st step for validation
A. Beunas: “Towards High Efficiency Klystrons for LHC”, FCC Week, Brussels, 2019
TH2167
TH2167HE
CST PIC Simulation: output cavity to collector
KlyC simulations
A. Buenas, I. Syratchev, J. Cai

## Slide 12: KlyC.v5 and CGUN
Codes developed at CERN by Jinchi Cai (U. Lancaster) and Igor Syratchev. The codes are or will be in the public domain.
KlyC: 1.5 D klystron simulation and optimisation code, including EM model, coupled cavities module, monotron oscillations module, Poisson module, klystron optimizer module, parameter scaling module. Allows import of HFSS/CST data.
CGUN: Electrostatic and magnetostatic modules, suited e.g. for e-guns and two-stage klystrons, including e-beam tracking. Can be called from KlyC if needed.
https://indico.cern.ch/event/921325/contributions/3870852/
https://cds.cern.ch/record/2649486

## Slide 13: Recent L-band industrial prototypes
Canon E37503 6-beam MBK
Perveance:
Gain:
Thales TH1803 10-beam MBK
Perveance:
Gain:
G. McMonagle, I. Syratchev, J. Cai

## Slide 14: Two-stage MBK technology (TS MBK)
Specific features:
Bunching at low voltage (high perveance). Very compact RF bunching circuit.
Bunched beam acceleration and cooling (reducing p/p) along the short DC voltage post-accelerating gap.
Final power extraction from high voltage (low perveance) beam. High efficiency.
Additional advantages:
The 2nd stage can be operated in DC, simplifying the modulator and increasing its conversion efficiency.
Simplified feedback for the first stage pulsed voltage. Improved klystron RF phase and amplitude stability.
Gap’s accelerating DC voltage is a natural barrier for reflected electrons. Improved tube stability.
HV insulators
Post accelerating gap
TS MBK
Conventional HE MBK
Stage 1
Stage 2
Collector
Cathode
I. Syratchev, J. Cai

## Slide 15: Example: 1 GHz, 24 MW TS-MBK
DC gap
KlyC optimization results
selected
V total = 140 kV
Note the flat, cylindrical bunch
I. Syratchev, J. Cai

## Slide 16: Radial gap RF isolation
Straight gap
Gap with rejector filter
Without rejector, about -21 dB of beam power would leak through DC gap.
The dual-harmonic rejection filter reduces this to -57 dB. Required mechanical tolerance: to stay below -50 dB.
I. Syratchev, J. Cai

## Slide 17: Example: 1 GHz, 24 MW TS-MBK: Simulated overall performance
The record high efficiency of 82% is achieved in 3D PIC simulation
stage 1
stage 2

## Slide 18: Example: 1 GHz, 24 MW TS-MBK
TS MBK
E37503
Local oil tank
Main solenoid
Cathode ceramic (25 kV)
PA gap
2nd HV insulating ceramic (115 kV)
Magnetic circuit
Output waveguide
Beam collector
Collector coil
1st stage
2nd stage
Output coil

## Slide 19: Magnetrons?
Interesting, but I don’t feel competent to talk about magnetrons.

## Slide 20: Solid State Power Amplifiers (SSPAs)

## Slide 21: SSPA – today’s state of the art: CERN SPS 200 MHz
Present day technology: e.g. CERN SPS recent power upgrade: 4.6 MW with 32 SSPA towers, based on recent LDMOS technology and 80-fold cavity-combiners.
This approach was very successful, but was not (yet) optimized for energy efficiency.
E. Montesinos

## Slide 22: SSPA – how to get to MW levels?
The single transistor level will probably remain in the 1 to 2 kW range.
The space requirement for the SPS system:
19 m x 36 m x 12 m for 4.6 MW!
Scaling to 100 MW would lead to impractical size!
Scaling to 100 MW would require combination factors !
We need smaller, smart, scalable power combiners!

## Slide 23: SSPAs – how to get to high efficiency?
https://indico.uu.se/event/515/contributions/760/
Paul J. Tasker: “Technical limits of solid state efficiency,”
P. Tasker

## Slide 24: Efficiencies in SSPA’s
(power added efficiency)
(drain efficiency)
: dominated by mode chosen and impedance matching. Class F operation and matching multiple harmonics may lead to practical: 90%
: impact of knee voltage (), typical for GaN: 97%
: impact of matching/combining losses – target: 97.5%
Overall “realistic” but challenging target: 82%
G. Formicone (Integra): A Highly Manufacturable 75–150 VDC GaN-SiC RF Technology for Radars and Particle Accelerators https://ieeexplore.ieee.org/document/8440054
P. Tasker

## Slide 25: Thank you very much for your attention!