## Slide 1: MAP Feasibility Studies as the Basis for Future Capabilities
Mark Palmer for the Muon Accelerator Program (MAP)
Brookhaven National Laboratory
Drawing on work conducted by: the US Muon Accelerator Program (MAP), the International Design Study for a Neutrino Factory (IDS-NF), and the International Muon Ionization Cooling Experiment (MICE)

## Slide 2: Context
The MAP effort was formed in 2011 to address the key feasibility issues of muon collider and neutrino factory technology
  Leveraged prior decades of studies to identify a design path
    But not charged to deliver a design – specifically to look at the individual elements to determine whether “self-consistent” designs with the necessary performance were within the realm of possibility
  Focused on proton-driver based solution
    Other potential production paths, while having some appealing parameters would not deliver working luminosity for HEP
    Perhaps new eyes will identify an alternative, but we were unable to
    A special feature of a proton-driver path is that it intrinsically produces high brightness muon beams at relatively low energies a thus supporting a very broad range of physics applications
  Message for today – While the MAP Effort concluded “early,” the most critical feasibility issues were addressed – thus providing a strong foundation for a new international collaboration to move forward with a detailed design study.

## Slide 3: Can Muon Accelerators Address the HEP Community’s Needs?

## Slide 4: Why Muons?
Physics Frontiers
Intense and cold muon beams a unique physics reach
Precision sources of neutrinos
Colliders
Opportunities
Collider Synergies
High intensity beams required for a long-baseline Neutrino Factory are readily provided in conjunction with a Muon Collider Front End
Tests of Lepton Flavor Violation
Anomalous Magnetic Moment (g-2)
Next generation lepton collider
s-channel production of scalar objects
Strong coupling to particles like the Higgs
Reduced synchrotron radiation a multi-pass acceleration feasible
Beams can be produced with small energy spread
BUT the accelerator complex and detector must be able to handle the impacts of m decays
Beamstrahlung effects suppressed at the collider IP
Such overlaps offer unique staging strategies to guarantee physics output while developing a muon accelerator complex capable of supporting collider operations

## Slide 5: Collider Luminosity
For a muon collider, we can write the luminosity as:
For the 1.5 TeV muon collider design, we have
  N = 2×1012 particles/bunch
  sx,y ~ 5.9 mm, b* = 10 mm, ex,y(norm) = 25 mm-rad
  nturns~1000
  fbunch=15 Hz (rate at which new bunches are injected)
Detector and Physics Performance at a Muon Collider
N. Bartosik et al 2020 JINST 15 P05001

## Slide 6: MC Parameters as Developed by MAP
RAST, Vol 10, No. 01, pp. 189-214 (2019)

## Slide 7: Key R&D Challenges
Target
Front End
Cooling
Acceleration
Collider Ring
MDI/Detector
Multi-MW Targets
High Field, Large Bore Capture Solenoid
Ongoing >1 MW target development
Challenging engineering for capture solenoid
Energy Deposition in FE Components
RF in Magnetic Fields (see Cooling)
Current designs handle energy deposition
RF in Magnetic Field
High and Very High Field SC Magnets
Overall Ionization Cooling Performance
MAP designs use 20 MV/m  50 MV/m demo
>30 T solenoid demonstrated for Final Cooling
Cooling design that achieves most goals
Acceptance
Ramping System
Self-Consistent Design
Designs in place for accel to 125 GeV CoM
Magnet system development needed for TeV-scale
Self-consistent design needed for TeV-scale
Magnet Strengths, Apertures, and Shielding
High Energy Neutrino Radiation
Self-consistent lattices with magnet conceptual design up to 3 TeV
> ~5 TeV – n radiation solution required
Backgrounds from m Decays
IR Shielding
Further design work required for multi-TeV
Initial physics studies at 1.5 TeV promising
Issues
Status

## Slide 8: Target & Capture System
C Target Option
1 cm
Compact Taper Design

## Slide 9: Front End and Energy Deposition
9
Control of FE Energy Deposition
FE Energy
Deposition
Validation of FE performance with gas-filled cavities
Buncher and Phase Rotator Matched to a 325 MHz Initial Cooling Channel

## Slide 10: Cooling Methods
The unique challenge of muon cooling is its short lifetime
  Cooling must take place very quickly
  More quickly than any of the cooling methods presently in use
  a Utilize energy loss in materials with RF re-acceleration
MAP R&D Efforts:
  RF in High Magnetic Fields: MuCool Test Area (MTA) at Fermilab
  High Field Magnet Design and Development
  The International Muon Ionization Cooling Experiment (MICE)

## Slide 11: Ionization Cooling
Advanced techniques a Improved HF Luminosity Simplified Final Cooling requirements
MAP Higgs Factory Target
PIC assumed in Carlo Rubbia’s Proposal
Specification Achieved (simulations)
Initial
(Y)
Initial
(X)
VCC &
Hybrid
HCC
Final
MICE Cooling Channel
>50MV/m operation in up to 5 T B-field
VCC HTS Extrapolation

## Slide 12: Muon Ionization Cooling (Design)
Initial 6D Cooling: e6D 60 cm3 a ~50 mm3; Trans = 67%
6D Rectilinear Vacuum Cooling Channel (replaces Guggenheim concept):
eT = 0.28mm, eL = 1.57mm @488m Transmission = 55%(40%) without(with) bunch recombination
Hybrid Design: Equivalent performance with gas-filled cavity variant
Bunch Merge
Longitudinal Merge
Transverse Merge
eT
st
Trans

## Slide 13: Muon Ionization Cooling (Design)
Final Cooling with 25-30T solenoids (emittance exchange): eT = 55mm, eL = 75mm
Helical Cooling Channel (Gas-filled RF Cavities): eT = 0.6mm, eL = 0.3mm
Initial 6D cooling
325 MHz cooling
650 MHz
Matching
Late Stage w/ Induction Linac
World Record LTS-HTS Hybrid Magnet 32T on-axis field
NHFML

## Slide 14: Some Cooling Comments
MICE confirms our understanding of the ionization cooling process for muons
MAP design studies and R&D provide a basis for the technologies in a full-blown cooling channel
  But only piece-wise studies completed
  Technology deliverables were achieved a now need to move to next-gen design effort
Cooling has huge leverage on the overall machine design
  What proton power is required on target?
  What luminosities can be envisioned?
A fully integrated design study is now warranted
A demonstrator will allow us to study the performance of the cooling concepts at high intensity
Will leave a deeper dive into the cooling concept to Diktys Stratakis’ talk

## Slide 15: Acceleration
Technologies Include:
  Superconducting Linacs
  Recirculating Linear Accelerators (RLAs)
  Fixed-Field Alternating-Gradient Rings (FFAs)
  Hybrid Rapid Cycling Synchrotrons
EMMA
Hybrid RCS
Designs to 125 GeV CoM
Needed for
Multi-TeV Scale
CBeta @ Cornell
Accelerator suitable for Neutrino Factory Applications

## Slide 16: Acceleration to 125 GeV Center-of-Mass
top view
39.8 GeV
16.6 GeV
16.6 GeV
829 m
11.6 GeV/pass
5 GeV
28.2 GeV
39.8 GeV
51.4 GeV
63 GeV
RF: f = 650 MHz cells/cavity = 5 Gradient = 25 MV/m phase = 22∘
E=5-63 GeV

## Slide 17: Higgs Factory (125 GeV) Lattice Design Alexahin, et al., JINST 13 P11002
MC Higgs Factory: MAP design with a single IP

## Slide 18: Key Features/Challenges of MC Higgs Factory
Features:
  s-channel production
  Exquisite energy spread (dEb/Eb~4x10-5) allows direct probe of Higgs line shape
  Spin precession of m allows precise E calibration (Raja & Tollestrup, arXiv:hep-ex/9801004)
Challenges
  Higgs production rate with preliminary MAP assumptions (~13,500/Snowmass year) hasn’t been considered competitive
    However, VCC simulations already suggest we can do better than this
    Introduction of alternative techniques such as Parametric Ionization Cooling (PIC) offer the potential of further rate improvements
  Machine-Detector interface
    IR magnet aperture requirements
    Shielding detector from machine backgrounds
  Based on MAP R&D results, an updated design study is required to fully evaluate potential performance
Han & Liu, arXiv:1210.7803 [hep-ph]

## Slide 19: Backup Slides Follow

## Slide 20: TeV-Scale Acceleration
MAP identified concepts
  Final designs are not in hand
Challenges:
  Large energy bandwidth lattice at high energies
  Fast-ramping magnets
    Grain-oriented silicon steel?
    HTS?
  Power supply system and efficiency will determine the viability and energy efficiency of the accelerator systems
Hybrid Rapid Cycling Synchrotron Cell Concept
FNAL
12 T/s HTS
0.6 T max

## Slide 21: Collider Ring & Detector
MAP Optics Designs for
  Higgs Factory (125 GeV)
  1.5 TeV CoM
  3.0 TeV CoM
  6.0 TeV CoM [extrapolation]
Ring Magnet Designs
IR Design
Higgs
1.5 TeV
3 TeV

## Slide 22: Looking Forward...
Muon Colliders offer an energy-efficient path to multi-TeV CoM energies
Recent physics studies indicate that important collider physics is accessible
The MAP R&D Program has successfully demonstrated critical technologies for the cooling channel a Now ready for:
  Updated Cooling Channel Conceptual Design
  Demonstrator of a high intensity cooling cell
Other key developments to pursue for a TeV-class collider (pushing beyond the parameters and scope of MAP)
  Ongoing physics studies
  Detailed designs for TeV-class acceleration
  Full end-to-end conceptual design
  Mitigation approaches to minimize “n Radiation” issues at the exit point on the surface
A new international design effort is timely and ready to evaluate an important option for the HEP community

## Slide 23: Key References
Boscolo, Delahaye, Palmer, RAST, Vol 10, No. 01, pp. 189-214 (2019)
The JINST dedicated volume on Muon Collider Research and Technology: Muon Accelerators for Particle Physics https://iopscience.iop.org/journal/1748-0221/page/extraproc46
Demonstration of cooling by the Muon Ionization Cooling Experiment, Nature 578, 53-59(2020)

## Slide 24: Thank you for your attention!