## Slide 1: Neutrino Time of Flight measurements (with MINOS)
Phil Adamson
12th September 2012

## Slide 2: Back Story
In September 2011, OPERA measured neutrinos travelling from CERN to Gran Sasso (730 km) and arriving faster than light by
The world’s press noticed…
In February 2012, OPERA announced they had found a loose optic fibre which could cause this discrepancy
  Subsequent measurements by all CNGS experiments are consistent with the speed of light
  ICARUS (arXiv:1208.2629) ~2ns systematic error

## Slide 3: A neutrino beam
π-
π+
Target
Focusing Horns
2 m
675 m
νμ
νμ
15 m
30 m
120 GeV protons from MI
Decay volume
  π+ -> µ+ νµ
Beam Absorber
  Absorb hadrons
Muons range out in rock
  Neutrinos left
Primary proton beam on target
  Produce π,K
Magnetic focusing horns
  sign-select pions

## Slide 4: MINOS detectors
1 kT Near Detector
1 km from source
5.4 kT Far Detector
735 km from source
Magnetized steel/scintillator tracking calorimeters
  1” steel plates
  1cm scintillator (4.1cm wide strips)
Functionally eqivalent
  Same materials
  Same segmentation
  Same mean B field (1.3 T)
  Many systematics cancel

## Slide 5: Measuring neutrino velocity
Grade school:
Three detectors
  Near and Far (neutrinos)
  RWCM in beamline (protons)
But you can’t ever detect the same neutrino in each place
  Cross section very small
  Neutrino consumed in detection
distance
target
ND
FD
Neutrino to neutrino measurement
Ceramic break

## Slide 6: MINOS Beam structure
6 1.6 µs batches separated by ~100ns
Each batch has 81 bunches
  Bunch spacing 18.83 ns
  Bunch sigma ~1 ns
  MINOS detectors can resolve this
3.5 ns
~100ns
18.83ns

## Slide 7: Measuring time
Absolute time was never a very interesting number
  Use time of expected beam at Far Detector to suppress background events from cosmic rays
    Beam spill is 10 µs long, so timing only has to be good to 1 µs
Relative timing between scintillator strips important for distinguishing upward & downward-going muons from atmospheric neutrinos
distance
target
ND
FD
Neutrino to neutrino measurement

## Slide 8: Telling the time
Divide time measurement into 2 parts
  Time with respect to local clock
    Beam structure
    Electronics
      Accuracy
      Quantization
    Detector Latency
    Quality of local clock
Transferring time between two detector sites
  “Routine” for time labs
    Steve Jefferts, Stephen Mitchell talks
  TWTT over fibre (MI60 to ND, surface to ground)
  TWSTT
  GPS (PPP or Common View)

## Slide 9: Old GPS System
Good enough for background rejection
  But not for time of flight
GPS has a random-but-stable offset with respect to UTC
  Changes with each power cycle
  RMS 60 ns
See next talks for something better than this!
9
Intentional Power Cycles
of GPS receiver

## Slide 10: Detector latency
Remember those “functionally identical” detectors?
  The electronics is completely different
  Also larger Far Detector has
    Longer wavelength-shifting fibres
    Longer clear readout fibres
Can measure latency of each piece and sum, but then combine many uncertainties
  We measure latency of whole detector at once

## Slide 11: Auxiliary Detector
Build two identical simple, portable muon detectors
  2 1m x 1m MINOS-style scintillator planes and photomultipliers
  Coincidence of PMT dynode signals makes muon paddle
  Timestamp hits against local Cs clock with BI220 Time Interval Analyser
  Measure large detector timing signal against local Cs clock
Place behind MINOS ND, track muons into AD, measure offset between time in large detector and auxiliary detector
Take one apart, drive whole thing to Soudan and repeat with FD.
You now have a relative latency measurement between the two detectors, which is what you need for time-of-flight

## Slide 12: Latency measurement at FD

## Slide 13: Measuring distance
Talk later this morning from Virgil
3 components
  Surface measurement between sites
  Tie between surface and underground network at ND
  Same at FD
…and don’t forget that the Earth rotates
Far detector is the big challenge
  2341 feet down single mineshaft
    Bent, not vertical
    Usually has fog half way up
  Currently ~70cm uncertainty on inertial measurement
Time-of-flight requires significantly more accurate distance than oscillation measurements
distance
target
ND
FD
Neutrino to neutrino measurement

## Slide 14: Summary
Neutrino velocity measurement is conceptually simple, but technically challenging
  Grade school:
Challenge is to approach 1ns uncertainty
  Time transfer
  Distance measurement
Environmental chamber on surface at Soudan maintains temperature within 1 °F