## Slide 1
Cryocooler conduction-cooled SRF accelerator cavities
Ram C. Dhuley
Fermilab Engineers’ Retreat, 25 February 2021

## Slide 2
Expanding the application space of SRF technology
From basic science…
Electron beam radiation processing applications
Water/sludge/medical waste
decontamination
Flue gas cleanup
Medical device sterilization
Strengthening of asphalt pavements
Radiation processing requires:
Beam energy: 0.5-10 MeV
Beam power: >>100 kW
Industrial settings demand:
Low capital and operating expense
Robust, reliable, turnkey operation
http://accelconf.web.cern.ch/AccelConf/napac2016/talks/thb3io02_talk.pdf
to industry…

## Slide 3
Simplifying SRF cryogenics for industrial settings
R.D. Kephart, SRF2015. https://accelconf.web.cern.ch/srf2015/papers/frba03.pdf
Patents: US10390419B2, US10070509B2, US9642239B2, 63/023,811

## Slide 4
Outline – cryogen free SRF
Research and development at Fermilab
  Development of cavities and practical cw gradient demonstration
  Design and development of a cryogen free SRF accelerator
Activities outside Fermilab and opportunities
  Conduction cooling at other labs
  An example of SRF research enabled by conduction cooling
  Private industry ventures

## Slide 5
Development of conduction cooled SRF cavities at Fermilab
(supported by Fermilab LDRD 2016-19)
650 MHz Nb single cell
Fabricate cavity with Nb conduction rings
Welding of conduction rings: e-beam parameter development
RF surface processing, Nb3Sn coating, and cavity-link assembly
HPR, EP, 800 0C furnace
Nb3Sn coating
Assembly with thermal links
Design and FEA verification of thermal conduction linkages
5N aluminum
links bolted to
Nb conduction rings
R.C. Dhuley et al. (2018) https://doi.org/10.1016/j.cryogenics.2018.06.003
R.C. Dhuley et al. (2019) https://doi.org/10.1109/TASC.2019.2901252

## Slide 6
Progress with cavity performance characterization
(supported by Fermilab LDRD 2016-19, DOE HEP Accelerator Stewardship 2019-21)
R. Dhuley et al., (2020) https://doi.org/10.1088/1361-6668/ab82f0
Development of a conduction cooled SRF (CCSRF) cavity test stand at Fermilab-IARC
Work in progress to push Eacc to 10 MV/m cw
Globally first demonstration of practical cw accelerating gradients on an SRF cavity without using liquid cryogens
R. Dhuley, S. Posen, et al. (2020) https://doi.org/10.1088/1361-6668/ab82f0

## Slide 7
Design of a 10 MeV, 1000 kW (100 mA) module at Fermilab
(supported by DOE HEP Accelerator Stewardship 2019-21)
Courtesy : R. Kostin (Euclid Techlabs)
RF design of a 5-cell 650 MHz cavity
Beam transport simulations
(external injection 300 keV --> 10 MeV)
Estimation of 4 K heat load, cryocooler selection
Design and thermal simulations of conduction link
Cryostat design and integration (thermal and magnetic shield, vacuum vessel, couplers)
Cost assessment
8 x PT420 mounting pads
Courtesy : I. Gonin (Fermilab)

## Slide 8
Cryogen-free SRF electron accelerator development at Fermilab
(supported by US Army Corps of Engineers/ERDC; National Nuclear Security Administration)
Goal: Component production, integration, and demo of a 1.6 MeV, 20 kW accelerator
“1.5-cell” 650 MHz Nb3Sn cavity
Cavity with integrated e-gun
(design in progress)
Low heat leak
coupler
(to be tested)
Courtesy : S. Kazakov (Fermilab)
Thermionic
cathode
(to be tested)
Courtesy : I. Gonin, V. Yakovlev (Fermilab)

## Slide 9
Cryostat (design in progress)
20 kW SSA (to be installed
and commissioned)
Cryomech PT420 coolers
(to be commissioned)
Courtesy : M.I. Geelhoed (Fermilab)
Cryogen-free SRF electron accelerator development at Fermilab
(supported by US Army Corps of Engineers/ERDC; National Nuclear Security Administration)

## Slide 10
Fermilab is not alone!
Fermilab
650 MHz
welded niobium rings
Jefferson Lab
https://doi.org/10.1088/1757-899X/755/1/012136
1.5 GHz
Cold sprayed +
electrodeposited copper
https://arxiv.org/abs/2002.11755
Cornell University
2.6 GHz
Copper clamps

## Slide 11
Enabler for academia: SRF R&D without needing full
stack helium cryogenic systems
Osama Mohsen completed PhD research in 2020 using conduction cooled SRF apparatus at IARC@FNAL (https://arxiv.org/abs/2012.13388v1)
High repetition rate field emission source using a conduction cooled SRF cavity
More opportunities:
Study of Nb3Sn layer degradation due to electron bombardment from a cavity-integrated electron source
Cryocooler cuts down cooldown/warmup cycle time - enable fast turnaround experiments on new thin film coating techniques and material science for SRF

## Slide 12
Enabler for industry: Private ventures
Standalone cryomodule for QW resonators
S. Kutsaev et al. (2020),
https://ieeexplore.ieee.org/document/9119112/
SRF photogun for UEM/UED applications
R. Kostin et al. (2020),
https://indico.classe.cornell.edu/event/1806/contributions/1460/

## Slide 13
Acknowledgement
This presentation has been authored by Fermi Research Alliance, LLC under Contract No. DE-AC02-07CH11359 with the U.S. Department of Energy, Office of Science, Office of High Energy Physics.
Conduction-cooled SRF demonstration: J.C.T. Thangaraj, Fermilab LDRD
Accelerator design studies: R.C. Dhuley DOE HEP Accelerator Stewardship Award
Compact SRF accelerator development: T. Kroc, R.C. Dhuley NNSA and R.D. Kephart, US Army Corps of Engineers (ERDC)
Nb3Sn SRF R&D: S. Posen, Fermilab LDRD and DOE Early Career Award

## Slide 14
Thanks! Questions?

## Slide 15
Extra: Conduction link performance, cavity thermal stability
Increasing Pdiss with Eacc
Comparison of measured and simulated
link thermal conductance
Computed cavity surface temperature at steady state with 6.6 MV/m cw
Ring temperature = 7.2 K (boundary condition)
RF dissipation = 4 W (boundary condition)
ΔTspatial <0.15 K
Tmax < 9 K
Courtesy : R. Kostin (Euclid Techlabs)
Good match!

## Slide 16
Vacuum vessel
Magnetic shield
(~15 mG)
Thermal shield
(cooled by the 45 K stage)
Two-stage cryocooler
55 W @ 45 K
2 W @ 4.2 K
SRF cavity with Al link
(cooled by the 4 K stage)
RF system
- 10 W cw @ 650 MHz, 1.3 GHz
- Resonance locking
- Pf, Pr, Pt, τL measurements
Euclid Techlabs
0.8 m
Extra: IARC CCSRF test stand