## Slide 1: Near Site Conventional Facilities (NSCF)
Kate Sienkiewicz and Kennedy Hartsfield
Near Site Integration Workshop
16 March 2021

## Slide 2: Outline
Introduction to NSCF
NSCF Design
Near Detector Complex

## Slide 3: NSCF Technical Design Status
In last phase of Final Design
Near Detector requirements under configuration control
NSCF design up to date in the Near Site integrated 3D model
60% Final Design deliverable due next week (March 26th)
  Last chance to review design for facility and interface issues so we have time to resolve with you
    Space claims within Near Detector cavern, shaft, and ND Service Building
    Electrical and mechanical design meets your requirements
    Access and laydown areas meet your requirements
  Changes after NSCF design completion or during construction typically increase cost impact
60% Final Design Review period March 29 – April 16
  Page turns with stakeholders the first two weeks of April
  Comments due no later than Friday, April 16th
Construction note: Near Detector Complex AUP planned for July 8, 2026
NSCF Site Prep Construction – Summer 2020

## Slide 4: NSCF Team and Communication Lines
NSCF team members
Fabrice is our main point of contact for NSI and ND
  Work through him for changes and issues
Near Site integrated 3D model resource for interface discussions and clash detection
Ad hoc technical breakouts with NSI and ND stakeholders
  Recently discussed electrical load and equipment, grounding, controls, equipment coordination, mezzanine, roof hatch, ODH air flows
Page turns for 60% Final Design Review opportunity to discuss with NSCF team how the NSCF technical design meets the ND requirements

## Slide 5: NSCF Design
What does NSCF scope include?
  All the “civil” or “house” needs for the Near Detector Complex
  Building Code Design and Compliance
  Construction staging planning
  Environmental Permitting – Wetlands!

## Slide 6: Site Works
Parking
Contractor Laydown
Wetlands
Existing and New Site Utilities
Site Boundaries
Exterior Infrastructure (Cryo Foundations)

## Slide 7: Site Works

## Slide 8: Near Detector Complex (NDC)
Near Detector Service Building (NDSB -Above Ground)
Near Detector Hall (NDH - Underground)

## Slide 9: Near Detector Complex
~126 ft
~92 ft
~172 ft
~46 ft
~63 ft
38 ft
~50 ft
Near Detector Hall (NDH)
Near Detector Service Building (NDSB)

## Slide 10: Life Safety / Architectural
Emergency Egress, Lighting, Ventilation, & coordination with ODH
Building Code Analysis
  Occupancy Underground =
  46 People Maximum
Did you know Fermilab has our own Fire Department on site? A security department as well!

## Slide 11: Life Safety / Architectural
Fire Protection in NDH and NDSB
Double Interlock Fire Sprinklers over the detectors and
cryo mezzanine
Automatic wet pipe sprinkler system in non-detector spaces

## Slide 12: Overhead Bridge Cranes
NDH Crane – 60 US short Tons
Crane Hook Coverage
“Green Box” is space claim reservation for detectors. This is the “Envelope” provided for the detectors in which to live

## Slide 13: Overhead Bridge Cranes
NDSB Crane – 15 US short Tons
Crane Hook Coverage

## Slide 14: Structural Cavern Support
Dimensions to walls are given clear to face of final shotcrete
Spray Applied waterproofing to ceiling protects equipment and detectors from ceiling drips
Clear
Dimension
Waterproof Membrane
“Gun Shot” finish

## Slide 15: Mechanical HVAC
Control temperature, humidity, and air flow based on NSI and building code requirements
Coordinate location of ductwork with NSI/DUNE equipment – still ongoing

## Slide 16: Electrical Distribution & Grounding
NSCF provides power distribution from Kautz Road (KRS) to NDC
Coordinating with NSI for loads and distribution details within NDC
Standby Generator provided for life safety and other critical loads (sump pumps, cryo controls etc)
Building and detector ground requirements are being coordinated with NSI
KRS
Main Ring
Main Injector
NDC
13.8kV Power Route

## Slide 17: Plumbing & Dewatering
NDH is actively dewatered and pumped to surface
Drainage strips provided behind shotcrete to collect water
Backup pumps and standby generator provided
Trench Drains around perimeter collect seepage water
Waterproof membrane provided over equipment and detectors
Trench Drains
Sump Room

## Slide 18: Site and NDC Communications
NSCF provides fiber optic backbone for site communications.
  NSCF coordinates with FNAL Computing Division for installation of phones and network
NSCF provides cable tray routing and is coordinating on communications needs with NSI within NDC
NSCF provides space, power, and cooling for DAQ room
Cable Tray Routing
DAQ Room

## Slide 19: NDSB Layout
DAQ Room
High Bay Assembly Area
Helium Room
Main Access Shaft
Secondary Egress Shaft
Elevator
Cryo Foundation
Mechanical/Electrical Mezzanine Upstairs

## Slide 20: NDH Layout
Egress Passageway
Mezzanine
SAND Alcove
To Secondary Egress Shaft (Not shown for clarity)
Elevator
Sump Room
Mezzanine

## Slide 21: Summary
Communicate through Fabrice, our point of contact for NSI and ND
60% Final Design Review comments due no later than Friday, April 16th
Near Detector Complex AUP July 2026