## Slide 1: ND-GAr Update
LBNC
March 4th, 2021
ND-GAr

## Slide 2: Near Detector Requirements
Motivation for ND-GAr

## Slide 3: Overarching ND Requirements & ND-GAr
MPD contributes
MPD meets requirement
Unchanged from last presentation

## Slide 4: ND-GAr design status

## Slide 5: ND-GAr design update
Magnetized volume including high-pressure (10 atm) gaseous argon TPC + ECAL. Plus external muon tagger
  Copy of ALICE TPC (5m in diameter X 5m long active)
  1t fiducial target mass
Magnet: Solenoid with Partial Return Yoke (SPY)
  0.5T field
  Acts as pressure vessel for HPgTPC
HPgTPC surrounded by high-performance ECAL
  Optimization study underway
Muon tagger
  Outside return Fe
    Scintillator, RPCs or MicroMegas (tbd)

## Slide 6: ND-GAr
Yoke
Magnet
Pressure end seal
HPgTPC
ECAL

## Slide 7: ND-GAr cut-away
Magnet
Yoke
HPgTPC
ECAL

## Slide 8: HPgTPC details
Central readout chambers (2, new design)
ALICE (18-fold symmetry)
Pad readout ONLY. True 3D. No Wires
Readout Pads (ALICE)
  Inner chambers (36)
    4X7.5 mm2 (5504/chamber)
  Outer (36)
    Inner rows: 6X10 mm2 (5952/chamber)
    Outer rows: 6X15 mm2 (4032/chamber)
  Total pads: ~554k
Readout Pads (Central)
  Still under study
  Starting with 6X6 mm2 pads as reference
  ~125k
Total channels: ~680k
  Typical voxel occupancy/spill ~ 0.03%
Readout Electronics
  Front-end: Modification of LArPix (GArFastPix)
  Back-end: same

## Slide 9: ECAL Baseline Design
12-sided geometry
Key design features
  High granular layers based on CALICE R&D (AHCAL SiPM-on-tile design)
    2 mm Copper / 5 mm plastic scintillator tiles of 2.5x2.5 cm2
  Cross-striped layers in the back based on Mu2e
    4 cm width spanning the full module width/length (~few m)
  SiPM readout
  Estimated number of channels: ~1- 3M
Based on simulation studies
  Energy resolution ~ 6%/Sqrt(E) + 4%
  Angular resolution ~ 8o/Sqrt(E) + 4o
  Neutron detection eff. ~ 40%
Eldwan Brianne
Marco Oriunno

## Slide 10: ECAL Optimization
Baseline is uniform in q, f
  Is this needed?
Truth energy flow analysis in regions (US barrel, DS barrel, end caps for nmCC evts.
  Just neutrals here, n and g. KE plotted
Downstream barrel (34.3K entries)
Upstream barrel (12.4K entries)
Endcap (9.6K entries)
n
Vivek Jain

## Slide 11: ECAL Optimization
Baseline is uniform in q, f
  Is this needed?
Truth energy flow analysis in regions for nmCC evts.
  Barrel upstream (US), Barrel downstream (DS) and end caps
All secondaries
Excluding n & g
Stopping in end cap ECAL
Excluding n & g
Stopping in US barrel ECAL
∑ (P'true- Ptrue)
Excluding n & g Stopping in
US barrel or end cap ECAL
DP (GeV)
Assumption: all charged secondaries measured in
HPgTPC
Excluding n & g Stopping in
DS barrel ECAL
Under consideration

## Slide 12: Solenoid with Partial return Yoke (SPY)
Team at INFN, Genoa has been taking design forward
  Interacting with ASG Superconductor
Strengths over Helmholtz coil design
  ~ 1/3 stored energy (Cost ↓)
    C($) ∝ Es0.7
  Better central field uniformity
    Now ~ ± 2%
  Less stray field
  More natural incorporation of steel for muon tagging system
  Existing TDR
    75% scale model exists
Andrea Bersani, Don Mitchell, Colin Narug

## Slide 13: Software development: Analysis Framework proposal
New repository, Garana
  Condensed versions of GarSoft products
  Tools for reading class-based or flat trees
  Tools for class-based → flat tree conversion, consistency checking
  Standalone, lightweight event display
  Backtracking
  Support for C++ or Python analysis with ROOT
Make GarSoft depend on Garana
  Extensions for garana products to facilitate construction from nusimdata objects
  Class-based trees produced by new analyzer module, StructuredTree_module.cc
  Garana takes care of the rest
Chris Hilgenberg

## Slide 14: Framework status

## Slide 15: GarSoft: Custom Magnetic Field
Due to the ND-GAr magnet, we need to use a custom magnetic field to simulate non-uniformities and see the impact on tracking performance (also may be good to understand the impact of the fringe field on the ND-LAr)
Andrew Cudd nicely implemented this in
  edep-sim (see PR: https://github.com/ClarkMcGrew/edep-sim/pull/10)
  GArSoft as a standalone art service (MPDMagneticField_service.cc)
  He demonstrated that it works perfectly with edep-sim
GArSoft is currently in code-review (branch bfield)
Eldwan Brianne

## Slide 16: HPgTPC Workshop
Workshop held January 11th - 13th
  ~ 80 registered for the meeting
  Focus was on the HPgTPC, but included ECAL
  Three working groups, but included cross-cutting discussion sessions
Physics/simulation
  GArSoft
  ND-GAr lite
  Single drift
  dE/dx resolution
  m catcher
  Calibration & concept of Fluorescence tagging
Mechanical
  Plans for scintillation light studies
  Temps and gas properties
  ECAL calibration
  TPC calibration thoughts
    perhaps for a ND-GAr calibration task force soon?
  Muon system
Electrical
  Requirements
  Interfaces
  System design
  Digitiser ASIC options
  Aggregator
  Timing

## Slide 17: R&D Plan
HPgTPC (DOE Research Consortium Proposal)
  Gas Mixture studies
  Electronics and DAQ
  Central Readout chamber design
  Mechanical engineering
  Field cage and HV
  Gas & Cooling system
  Calibration and slow controls
  Light collection
  Test stands
ECAL
  Starting with CALICE engineering
    Detailed design and optimization will come with TDR
    Initial engineering resources are now coming from SLAC
Magnet (coils & yoke)
  Preliminary design being developed in Genoa with engineering support from FNAL
    In consultation with ASG
Muon detector
  TBD ➛ Technology choice and then mostly development.

## Slide 18: ND Configuration at beginning of ops
TMS as ND-GAr lite

## Slide 19: Day 1 Configuration currently imposed by resource constraints

## Slide 20: TMS: ND-GAr lite

## Slide 21: Alternative TMS: ND-GAr-Lite
ND-GAr-Lite
  SC Magnet including partial return-yoke
  Scintillator tracking planes
    Update of MINERvA
    Similar electronics as SSRI
  ECAL modules could be added (but may degrade performance)

## Slide 22: Tracker plane concept

## Slide 23: TMS: ND-GAr-Lite Nominal Design
Simple reconstruction
  Require 3 hit scintillator planes
  planes at z = {-240, -150, 0, 150, 240} cm
Not optimised for low-p muons
  will bend to not hit third plane
Larger cross section for muons than ND-GAr
Optimisation needed
  Geometry
  Tracking reconstruction

## Slide 24: Performance: Acceptance and Momentum Resolution
2.5% resolution, with tails due to misassigned hits
Better fit and hit selection quality cuts will improve tails
GEANT4 simulation plus simplified realistic reconstruction
Muons from neutrino interactions in ND-LAr
Includes ND-LAr-contained muons
ND-GAr-Lite muons crossing first plane

## Slide 25: Performance: Charge-sign Determination
excellent capability to determine charge sign

## Slide 26: Optimisation
Increase efficiency/acceptance for low momentum muons by adjusting the scintillator plane spacing -- closer planes at the upstream end.
Adjusting the plane spacing will affect the momentum resolution, primarily by changing the lever arm available for measuring a track.
Some spacing configurations can make the efficiency or resolution better/worse for particular momentum ranges.
Andrew Cudd

## Slide 27: Optimisation
Results from 2000 scintillator plane arrangements
Efficiency and average momentum resolution for all “reconstructed” tracks.
Metrics are not ideal:
Give a useful look at overall behavior of the plane spacing
Nominal

## Slide 28: Optimisation
Work in progress!
Aim for improved efficiency with minimal degradation in momentum resolution
Nominal
Random
Nominal (5 planes)
Random (5 planes)
Random (6 planes)

## Slide 29: ND-GAr lite & ND-LAr
Additional instrumented
plane?

## Slide 30: Preliminary schedule
Technically limited estimate but does include detailed schedule input from external projects that have similar components
  Magnet system
    Genoa group (Bersani, Fabbricatore) met with ASG management:
      Sergio Frattini – Managing Director
      Antonio Pellecchia - Commercial Manager Magnets & Systems unit
      Giovanni Grasso - Business Development Manager, MgB2 wire unit
      Daniele Magrassi - Engineering and R&D Manager, Columbus MgB2 unit
    Input based on completed magnet for MPD experiment at NICA heavy-ion accelerator at JINR
  Tracking system
    Obtained “as-built” estimates from Craig Dukes (Mu2e Cosmic-ray Veto L2 manager)

## Slide 31: ND-GAr lite schedule
Preliminary, technically limited

## Slide 32: Participating Institutions
Georgia
  The Georgian Technical University
Germany
  DESY
  University of Mainz
  MPI, Munich
  RWTH-Aachen
India
  Bhabha Atomic Research Center
  Tata Institute for Fundament Research
  University team forming
Italy
  INFN, University of Genoa
Poland
  University of Warsaw
Spain
  Santiago
  Valencia
UK
  STFC
  Imperial College
  Queen Mary
  Royal Holloway
  University College London
  University of Oxford
  University of Edinburgh
  University of London
US (next page)

## Slide 33: US Institutions
Univ. of Mississippi
Univ. of Pittsburgh
Univ. of Rochester
Rutgers Univ.
SLAC
Univ. of Texas, Arlington
Univ. of Wisconsin, Madison
Wichita State
William and Mary
Abilene Christian Univ.
ANL
Univ. of CA, Santa Barbara
Univ. of Colorado
Fermilab
Indiana Univ.
Univ. of Iowa
LBNL
Univ. of Minnesota

## Slide 34: Conclusions

## Slide 35: QUESTIONS?

## Slide 36: ND-GAr’s strengths: An example
Case study: Genie, NuWRO differ greatly in pion production channels
  Genie model fit to NuWRO “fake” data leads to enormous biases in extracting dCP. Case study of unknown, unknowns.
ND-LAr will to some extent be able to measure/correct such a discrepancy inclusively in accordance with capabilities at FD. Issues:
  Secondary interaction effects and thresholds
  Non-trivial acceptance corrections
ND-GAr can perform detailed channel decomposition and correction with cleanly separate the channels
  The precision tracking capability of the HPgTPC allows ND-GAr to accurately identify and separate final states in neutrino interactions. Measuring various kinematic distributions for these exclusive final states allows deficiencies with the interaction model to be identified and fixed.
Seb Jones
102. I am puzzled by this whole procedure. What is this intended to show? If you just wanted to show that GENIE and NuWro
give different results, you wouldn't need to reweight one to look like the other, would you?

## Slide 37: Muons from nmCC events in gas (LBNF beam)
Correct hits assigned to track
  Pattern reco in development
No noise
Full pad response
  Drift/Diffusion simulated
Point resolution needs optimization
Kalman fit
  Needs optimization
Track stitching across cathode
Tom Junk

## Slide 38: Funding sources/opportunities
INFN is committed to support the MPD magnet coil design using current funding.
US groups have submitted a R&D Consortium Proposal to the DOE that will focus on the development of the HPgTPC and will produce a technical design report.
  3 years and $1.7M.
  Currently under review.
UK groups are preparing a ND DAQ proposal
German groups are preparing a targeted R&D proposal for the ECAL.
  To be submitted in November.
Indian groups are looking for funding for the partial-return yoke and muon tagging detectors
Not needed at Day 1 for m spectrometer

## Slide 39: Muon catcher -- Requirements
Design is obviously coupled to that of ECAL and magnet
Preliminary study with 20 cm Fe. Some conclusions
  Muons and pions stopping in ECAL can be separated by range with nearly 100% efficiency
  μID is required to get right-sign CC purity above 95%
  20cm iron μID gets ~100% purity for high-momentum tracks
  Backward μID is not needed if there is a backward ECAL
  Increasing the number of ECAL layers would improve the purity in the 400-500 MeV/c momentum range
Detailed design is in progress.
FHC nmCC purity (m-/p-)
Note: Raw ≡ Select highest P track
from ms and ps
Chris Marshall

## Slide 40: m purity vs. Fe thickness
For each case, the
steel was segmented
into 3 sections:
3.3, 6.6, 10 cm