## Slide 1
Optical Link and Component Testing
Alan G. Prosser
Fermilab
Feb. 11, 2021

## Slide 2
Project: To investigate the feasibility of implementing 10 Gbps optical links at LiAr Temperatures
Approach: Perform testing of COTS components at LiN temperatures to start.
Following earlier work by Southern Methodist University, we are beginning with
edge-emitting lasers (EELs) (which showed more promise in the tests carried out
about 10 years ago)
SMU is performing tests of VCSELs to see if recent devices perform better than did
those tested 10 years ago.
Agenda:
1. Give an overview of the testing setup to be utilized
2. Give some brief information on the kinds of information to be obtained from these tests
3. Illustrate some of the technology that has been developed/evaluated over the years
4. Outline some emerging technology that may be of interest (optical modulators)
Safety Approvals for Testing at Feynman Computing Center are being pursued (D. Christian, A. Prosser)

## Slide 3
Cold
Volume
Single Mode
Optical
Fibers
SFP+ Transceiver
SMA
Connectors
Coax
cables
SMA
Connectors
SFP+ Transceiver
Tx
Rx
Tx
Rx
Tx
Rx
Rx
Tx
Rx
+
-
l = 1310 nm
3.3 V DC
BERTScope
Bit Error Rate
Tester
Pattern
Generator
(PRBS)
Error
Checker
LC
Connectors
COTS SFP+
Evaluation
Board
In this configuration, the
bit error rate performance of
the uplink including the
Device Under Test (DUT)
within the cold volume
can be measured.
COTS SFP+
Evaluation
Board
This approach more faithfully
represents an upstream link
Tx
Coax
cables
Reference Rx Device
Basic Link Functional Verification

## Slide 4
Cold
Volume
Single Mode
Optical
Fibers
SFP+ Transceiver
SMA
Connectors
Coax
cables
SMA
Connectors
Tx
Rx
Tx
Rx
Tx
Rx
+
-
l = 1310 nm
3.3 V DC
BERTScope
Bit Error Rate
Tester
Pattern
Generator
(PRBS)
Error
Checker
LC
Connectors
In this configuration, measure-
ments of the DUT Tx optical
signal can be obtained including:
1. OMA
2. Extinction Ratio
3. Eye Height
4. Rise and Fall Times
5. Deterministic Jitter
6. Total Jitter
COTS SFP+
Evaluation
Board
Digital Signal
Analyzer
Clock Reference
and Pattern
Synchronization
FC
Connector
Complete Tx Characterization

## Slide 5
Cold
Volume
SFP+ Transceiver
SMA
Connectors
Coax
cables
Coax
cables
SMA
Connectors
SFP+ Transceiver
Rx
Tx
Tx
Rx
Tx
Rx
Tx
Rx
Tx
+
-
l = 1310 nm
3.3 V DC
BERTScope
Bit Error Rate Tester
Pattern
Generator
(PRBS)
LC
Connectors
COTS SFP+
Evaluation
Board
In this configuration,
measurements of the DUT
Rx channel eye in the
cold can be made including:
Rise and fall times
Eye amplitude
Deterministic and total
jitter
Single Mode
Optical
Fibers
COTS SFP+
Evaluation
Board
Digital Signal
Analyzer
Clock Reference
and Pattern
Synchronization
Reference Tx Device
Complete Rx Characterization

## Slide 6
Cold
Volume
SFP+ Transceiver
SMA
Connectors
Coax
cables
Coax
cables
SMA
Connectors
SFP+ Transceiver
Rx
Tx
Tx
Rx
Tx
Rx
Tx
Rx
Tx
Rx
+
-
l = 1310 nm
3.3 V DC
BERTScope
Bit Error Rate
Tester
Pattern
Generator
(PRBS)
Error
Checker
LC
Connectors
COTS SFP+
Evaluation
Board
In this configuration, the
bit error rate performance as
a function of the Optical
Modulation Amplitude
delivered to the DUT Rx port
(varied by introducing
optical impairment through
the VOA) will permit a measure-
ment of the DUT
Receiver Sensitivity in the
cold.
Single Mode
Optical
Fibers
FC
Connectors
JDSU Variable Optical
Attenuator (VOA)
COTS SFP+
Evaluation
Board
Rx Sensitivity

## Slide 7
Eye Pattern Measurements (Optical and Electrical)
Jitter Composition Measurements (Optical and Electrical)
Rx Sensitivity
Measurements

## Slide 8
Hardware For First Tests at DUNE
SFP+ Evaluation Board
SFP+ Module
Fiber Patch Cord
LC Connector
FC Connector
1 Tx (transmitter)
1 Rx (receiver)
2 fibers with LC Connectors
10 Gbps capable
Multimode and Single Mode Variants

## Slide 9
Hardware For First Tests at DUNE

## Slide 10
Test Equipment For First Tests at DUNE
Alan will perform checkout of the system and components starting today or tomorrow.

## Slide 11
COTS SFP+
CERN VTRx
Rad Hard TRx
CERN VTTx
Rad Hard
Twin
Transmitter
CERN/PSI/ETH/FNAL
Pixel OptoHybrid (POH 7Ch Tx)
CMS Phase 1 FPix
Digital Level Translator (DLT)
(Custom)
Multi-Channel
Laser Driver
(Custom)
Mitsubishi 1310 nm
Transmitter Optical SubAssembly (TOSA)
(COTS)
Some Single Channel Technology

## Slide 12
Early VTRx+ Prototype (Front End Element)
(This example has 2 transmitters, 1 receiver)
Devices and evaluation card from CERN
NOTE: This effort even involves the development
of custom optical packaging
SAMTEC FireFly Tx/Rx Pair…
… with Y cable (terminates
in a single 24 fiber MTP connector)
Back End Element (COTS*)
Front End Element
(custom)
HL-LHC Components (Versatile Link Plus Project)
14 Gbps
10.24 Gbps upstream
2.56 Gbps downstream

## Slide 13
Reminder: An Optical Link is Very Much a System Concept

## Slide 14
Analog Optical Data Communication
Yesterday, we heard from DarkSide on their plans to pursue an analog solution
The approach is founded on the desire to preserve the signal to noise ratio of the measured signals.
The link uses:
1. 1310 nm LED (wavelength is not a source of noise in LiAr)
2. 200 micron core diameter optical fiber (the numerical aperature in LiAr could be an issue for 9
micron core single mode fibers)
3. Photodiode and Transimpedance Amplifier on the outside
We are looking into components that might be useful for similar testing here at FNAL:

## Slide 15
Some Evolving Technology
Direct Modulated Laser Diode systems are reaching the limits of performance
Indirect Modulated devices are in use already (Lithium Niobate Mach-Zehnder Modulators)
Newer devices are being investigated to combine the high-speed, low-power promise of indirect
modulation with Wavelength Division Multiplexing (WDM) for compact high throughput links
with enhanced utilization of fiber resources. These developments are part of the emerging
technology known as Silicon Photonics.

## Slide 16
Some Evolving Technology – Example
Ring Resonator Modulators
No lasers on the
front end (low power)
Not without issues:
1. Thermal
dependence
2. Polarization
sensitivity
Multiple wavelengths
1 fiber (CW)
This approach has
attracted interest
from members of the
community operating
in cryogenic environ-
ments.