## Slide 1
DUNE Cryogenic Optical Links
Dave Christian (FNAL)
Andy Liu (SMU)
Alan Prosser (FNAL)
Jingbo Ye (SMU)
March 17, 2021

## Slide 2
Introduction
Initial testing has so far failed to produce an SFP+ module (either Tx channel or Rx channel)
that functions suitably when tested in LN2.
There is some indication that electronic issues are behind at least some of the failures.
Therefore, we propose to construct test hardware with selected components to try to
identify the sources of failures and to identify suitable components out of which a
custom CryoLink component might be produced.
FNAL will start with DFB-equipped TOSAs (modules with these performed best last week)
and laser drivers suitable for driving those TOSAs.
We are working with Southern Methodist University (Versatile Link partners) who add
valued knowledge and experience in this effort.

## Slide 3
COTS SFP+
Versatile Link VTRx
Transceiver
Versatile Link VTTx
Twin Transmitter
GBLD
(Laser Driver ASIC)
Flexible Circuits
TOSA
ROSA (GBTIA Inside)
GBLDs
TOSAs
Flexible Circuits
GBLD: GigaBit Laser Driver
GBTIA:
GigaBit TransImpedance
Amplifier
TOSA:
Transmitter Optical SubAssembly
ROSA: Receiver Optical SubAssembly
Tx Connection (LC)
Rx Connection (LC)
Tx Connection (LC)
Tx Connection (LC)

## Slide 4
Laser Driver
Discretes
Printed Circuit Board
TOSA
Flexible Circuit
Edge Connector Traces
Solder (SMT Connection)
Limiting Amplifier
Discretes
Printed Circuit Board
ROSA
Flexible Circuit
Edge Connector Traces
Solder (SMT Connection)
Tx Channel (side view with flexible circuit
allowed to be free)
Rx Channel (side view with flexible circuit
allowed to be free)
Strain relief for flexible circuit on each
channel?
MicroController Unit (MCU)
Latching design
may be
needed
Latching design
may be
needed

## Slide 5
Leave Cross Point Adjust and Automatic Laser Shutdown unconnected (50% cross point, laser enabled)
Simple Evaluation Board for Analog Devices ADN2526 Laser Diode Driver
Electrical Tests
Vibias_adj
Vimod_adj
SMA pair
SMA pair
All components will be
tested in LN2.
Power, configuration,
electrical excitation, and
electrical diagnostics
will be outside the dewar

## Slide 6
Leave Cross Point Adjust and Automatic Laser Shutdown unconnected (50% cross point, laser enabled)
Simple Evaluation Board for Analog Devices ADN2526 Laser Diode Driver
Optical Tests
Vibias_adj
Vimod_adj
SMA pair
TOSA Coupled to
Single Mode Fiber or
MultiMode Fiber
All components will be
tested in LN2.
Power, configuration,
electrical excitation, and
optical receiver will be
outside the dewar

## Slide 7
Texas Instruments ONET1151L Laser Diode Driver

## Slide 8
Interface
To
I2C Dongle
Outside
Dewar
SMA pair
Leave DIS unconnected (laser enabled)
SMA
SMA
Texas Instruments ONET1151L PAB Test Circuit Proposal (Stage 1)
Optical Tests
TOSA Coupled to
Single Mode Fiber or
MultiMode Fiber
All components will be
tested in LN2.
Power, configuration (I2C
dongle), electrical excitation,
electrical monitoring, and
optical receiver will be
outside the dewar

## Slide 9
Interface
To
CryoFPGA
Interface
To
CryoFPGA
Texas Instruments ONET1151L PAB Test Circuit Proposal (Stage 2)
TOSA Coupled to
Single Mode Fiber or
MultiMode Fiber
All components will be
tested in LN2.
Power, electrical excitation, and
and optical receiver will be
outside the dewar. FPGA to
configure laser driver will be in
the dewar.
SMA pair

## Slide 10
Summary
FNAL and SMU will jointly investigate technologies out of which suitable CryoLink (CL)
transmitter and receiver channels may be developed.
SMU will test TOSAs and ROSAs (including VCSEL-based TOSAs).
SMU has earlier experience with LOCld (custom laser driver) and Cyclone III FPGA in
LN2.
FNAL and SMU will jointly develop custom CL Tx/Rx as necessary (if COTS modules
cannot be verified in LN2).