## Slide 1: Project X Meeting - Fall 2011
SPL Activities
E. Ciapala
On behalf of the CERN SPL team:
O. Brunner, O. Capatina, S. Calatroni, R. Garoby, F. Gerigk, W. Hofle, A. Lombardi, E. Montesinos, V. Parma, W. Weingarten
With acknowledgements & thanks to members of the collaborating institutes – see slides

## Slide 2: SPL Activities - Outline
Description of the SPL and project scope
  Cavities – design & fabrication
  Cryostat, He tank
  Tuners, couplers, HOMCs
  Power systems and pulsed modulators
  Low Level RF
  CERN SCRF infrastructure upgrade
Planning and ongoing work
Summary
Upcoming events & meetings…
  SPL documentation in EDMS [ https://edms.cern.ch/nav/SLHC-000008 ]
  SPL meetings in Indico [ http://indico.cern.ch/categoryDisplay.py?categId=1893 ]

## Slide 3: High Power SPL (HP-SPL)
    High Intensity Higher Energy SC-linac (160 MeV ® 5 GeV) with ejection at intermediate energy. 4 MW beam power.
    Compared to LP-SPL: (Which was foreseen in the injectors upgrade plan)
      5 additional b = 1 cryomodules to reach 5 GeV (p production for n Factory)
      New klystron modulators, upgraded infrastructure (cooling & electricity, etc.)
246 Cavities

## Slide 4: Present Project Scope
In 2010, program launched for study of a high intensity proton driver in the context of possible future neutrino facilities at CERN, based on the LP/HP-SPL.
Included in CERN MTP, with resources.
Comprises:
Continuation of design work on HP-SPL, excluding integration & site specifics.
Includes prototyping of critical components: cavities, RF ancillaries and cryomodule
Construction and test of four-cavity RF cryo-module
Upgrade of clean room and assembly facilities
Preparation of a power test stand
Plan to power test the cryomodule in 2014
Updated CERN yellow report on SPL to be completed by end 2011

## Slide 5: SPL Study Organization
 | Coordinator | External partners
RF hardware (low level & high power) (WG1) | E. Ciapala | ESS, Cockcroft Institute + (FNAL, SNS, JLAB, ANL)
Cavities (structures & auxiliary equipment) (WG2) | W. Weingarten | CEA-Saclay, CNRS-Orsay, Uni Rostock, Stony Brook, DESY + (JLAB, SNS)
Cryo module (cryostat & cryogenics) (WG3) | V. Parma | CEA-Saclay, CNRS-Orsay, Stony Brook + (FNAL)
Beam dynamics (beam parameters) (WG4) | A. Lombardi | CEA-Saclay, ESS + (FNAL)
Architecture (layout & geometry, extraction, transfer) | F. Gerigk | 
Surface treatment and vacuum | S. Calatroni | 
Mechanical design and construction | O. Capatina | 
Working Groups
Study leader: R. Garoby
SPL Collaboration
R.G.

## Slide 6: RF design of the b=1 cavity (Saclay)
REFERENCE PARAMETERS (CDR, 2006) | 
RF frequency | 704.4MHz
Cavity b | 1
Accelerating gradient (Eacc) | 25 MV/m
Average pulse current (Ibeam) | 40 mA
Synchronous phase (js) | -15 °
Peak RF power | 1 MW
J. Plouin, SACLAY, Joint ESS/SPL Meeting - SACLAY 2011
Design Goals
Optimization of r/Q, Epk, Bpk
Achievement of the external coupling
Resistance to Lorentz detuning (stiffeners)
  Reduction of KL with stiffening rings down to |KL|= 1 Hz/(MV/m)²
  Fast tuning system in pulsed mode (tests & operation)
RF PARAMETERS OF THE CAVITY | 
Number of gaps (Ngap) | 5
Frequency [MHz] | 704.4
Beta | 1
Bpk/Eacc [mT/(MV/m)] | 4.20
Epk/Eacc | 1.99
G [Ohm] | 270
Cell to cell coupling | 1.92 %
r/Q [Ohms] | 566
Beam diameter aperture [mm] | 129.2
Lacc = Ngap.b.l/2 [m] | 1.0647
Maximum energy gain @ Bpk = 100 mT | 25 MeV
Operating Temperature (O.T.) | 2 K
RBCS @ O.T. (theoretical) | 3.2 nW
Q0 @ O.T. for RBCS | 8.4*1010
704.4 fundamental mode (pi-mode)
6

## Slide 7: Status of b=1 cavities at CERN
Four cavities will be built
Tooling made
20 copper model half cells made, now being measured
Niobium for the four cavities (+ spare) delivered to CERN
Invitation to tender for three cavities sent out to three firms, offers being studied
CERN will manufacture the remaining cavity (TBC)
Cavity assembly at CERN, using new e-b welding machine, suitable for high quality niobium
Planned completion four cavities by end of 2012
Spinning and e-b welding

## Slide 8: Cavity tuning set-up
Development of a new tuning set-up for obtaining the field flatness after reception of the cavity.
Tuning jigs to be built both at CEA and CERN
Cell by cell tuning with plates fixed on the stiffening rings of the cavity
Drilling on rings
J. Plouin et. al. ESS/SPL Meeting July 2011.

## Slide 9: Cryostat, He Tank and Ancillaries
Schematic sectional view of the five-cell cavity inside its helium tank, with tuner magnetic shielding, power coupler and HOM coupler
Power Coupler
Magnetic Shielding
Bulk Niobium 5-cells Cavity
Helium Tank
HOM Coupler
Tuner

## Slide 10: He tank design : CEA/CERN
The ‘short SPL cryomodule’ is under-study by CERN+IPNO
CEA designing fully equipped cavity (with He tank, tuning system, coupler interfaces…) which fits on horizontal cryostat CryHolab
At CERN: integration of 4 cavities string in SPL short cryomodule
At CEA : design for tests in CRYHOLAB
(J. Plouin et al.)
Will finally use stainless steel for He tank to ease design of interfaces to other components

## Slide 11: Saclay piezo tuner for 700MHz cavities
Slow tuner with symmetric action
Excentric/lever arm proven Saclay design
Planetary gear box (3 stages)
Single NOLIAC 30mm piezo actuator
Stiffness measured on the tuner pneumatic jack = 35 kN/mm
Initially developed for the beta=0.5 5-cell cavity
G. Devanz, CEA-Saclay, SPL 3rd coll. meeting
Piezo Support
11

## Slide 12: Field flatness with & without piezo
+/- 0.7 %
field flatness
In amplitude
achieved
by using
piezos !
no piezo
piezo excited
use of piezo minimizes additional RF power needed to further improve the field flatness to the design target of +/- 0.5 %

## Slide 13: Phase flatness with & without piezo
+/- 8 degrees flatness
In phase, achieved
by only using
piezo ! Needs
RF feedback
to achieve
design goal
of +/- 0.5 degrees
no piezo
piezo excited

## Slide 14: Power Couplers
Type 1 - Air-cooled cylindrical ceramic window
Type 2 - Coaxial ceramic window.
Type 1
Type 2
Single RF window
Fixed coupling
Double walled tube on outer line
Mounted vertically, below the cavity
Double walled tube partially supporting the cavity
Due to the tight planning, and risk of difficulties with either type, the decision was taken to build 4 of each.

## Slide 15: Coupler testing and processing
Assembly at DESY using their XFEL high quality clean room facilities and procedures.
Then RF tests at CEA
RF Processing done using a “clean room line” assembly consisting of:
  A test cavity
  A pair of couplers
  Two double walled tubes
X 2
X 2

## Slide 16: Coupler assembly at DESY
All parts & components for four assemblies were prepared
All parts vacuum tested at CERN
All material sent to DESY for clean room assembly
A first test line assembled in the DESY clean room, using DESY-XFEL process cquality procedures
Vacuum tight.

## Slide 17: Couplers: Assembly & test
BUT difficulties with the Double Walled Tube (DWT) – peeling of sputtered Cu coating.
Possible explanation: machining of the DWT
Removed all copper on all DTs & clean them down to stainless steel (electro-polishing).
Four DWTs, NOT copper plated returned to allow completion of two assemblies. Completed and returned to CERN
Successful vacuum leak tested the two assemblies,
CEA tests will now be done, without Cu plating (Additional heating not an issue for warm tests – can water cool)

## Slide 18: HOM Couplers – Design studies
HOM Couplers needed if we have to cope with a variety of chopping schemes.
(Cavity has a mode at 2111.64, MHz very near 3fo)
Possibility to cool with super-fluid liquid helium retained. Therefore the HOM coupler ports are directed up.
HOM coupler port on the power coupler side extremity (right side) is directed upwards opposite the power coupler port.
A second HOM coupler port on the opposite extremity of the power coupler, rotated by 60° from vertical.
Futher design work is however needed…
Short cryomodule will have HOM ports
Preliminary design of HOM coupler for β = 1 SPL cavity.

## Slide 19: RF Power requirements along HP-SPL
Need additional power margins:
for Feedbacks (TBC)
7% Waveguide losses
Modulator droop, (?), coupling variations
1000 kW nominal (max b=1) on cavity => ~ >1.2-1.3 MW from klystron
Have a wide range of powers along the linac
Chart: High b section Power/ cavity [kW] @40 mA
Chart: Low b section power/cavity [kW] @40 mA
power, 40 mA [kW] | 150.1221 | 165.873 | 183.0505 | 185.6663 | 202.5523 | 220.3783 | 228.6063 | 246.1938 | 264.087 | 282.1433 | 299.9281 | 317.2642 | 350.974 | 368.2468 | 384.214 | 442.3474 | 457.9712 | 471.3557 | 511.508 | 521.5056 | 529.142 | 534.6375 | 538.2327 | 540.1718 | 540.691 | 540.0093 | 538.3258 | 535.8168 | 532.6361 | 528.9166 | 524.7716 | 520.2967 | 515.5724 | 510.6659 | 505.6328 | 500.5193 | 495.363 | 490.1949 | 485.04 | 479.9186 | 474.8467 | 469.8373 | 464.9003 | 460.0436 | 455.2727 | 450.5921 | 446.0046 | 441.512 | 437.1156 | 432.8154 | 428.6113 | 424.5025 | 420.4879 | 416.5662
Cavity #
Cavity #

## Slide 20: RF Power Sources
Work done on choice of power sources
Klystrons:
  One klystron per two cavities ?
  One klystron per cavity ?
IOTs:
  One IOT per cavity
  Multiple IOTs combined per cavity
Solid State Amplifiers (SSA)
  Optimal & modular config. for Low b, too big for high power sections
Magnetrons
Studied by A. Dexter CI, with JLAB
Chart: f [MHz]
| 10.0 | 352.0 | 1000.0 | 3000.0
Transistors | 1.2 | 0.33 | 0.12 | 0.02
Klystrons | 1300 | 1200 | 1000 | 500 | 250 | 2.5
Grid tubes | 6000 | 2800 | 1000 | 18
IOTs | 80 | 31 | 15
Transistors | 1.2 | 0.33 | 0.12 | 0.02
Klystrons | 1300 | 1200 | 1000 | 500 | 250 | 2.5
Grid tubes | 6000 | 2800 | 1000 | 18
IOTs | 80 | 31 | 15
Transistors | 1.2 | 0.33 | 0.12 | 0.02
Klystrons | 1300 | 1200 | 1000 | 500 | 250 | 2.5
Grid tubes | 6000 | 2800 | 1000 | 18
IOTs | 80 | 31 | 15
SPL = 704 MHz
Erk Jensen

## Slide 21: RF distribution schemes
Option 2) 1 klystron/cavity
Disadvantages:
240 power sources…
FOOTPRINT
Advantages:
Simplest RF hardware set
Full Direct RF control of each cavity. Simple non-interdependent RF loop controls
No additional power overhead or extra cooling
Good operability, best fault tolerance
Equipment | Qty | Cost/item. | Total
 |  | k Euro | kEuro
Klystron 1.2MW | 4 | 400 | 1600
1 MWp Circulator | 4 | 100 | 400
Circulator load 100kW | 4 | 20 | 80
Hybrid | 0 | 20 | 0
Hybrid load 100kW | 0 | 20 | 0
Phase shifter (mechanical) | 0 | 20 | 0
Vector Modulator 1MWp | 0 | 100 | 0
Klystron Modulator 1.5 MW | 4 | 200 | 800
Total (per 4 cavity unit) |  |  | 2880

## Slide 22: RF distribution schemes
Option 3) 1 klystron/2 cavities
Equipment | Qty | Cost/item. | Total
 |  | k Euro | kEuro
Klystron 2.4MW | 2 | 500 | 1000
1 MWp Circulator | 4 | 100 | 400
Circulator load 100kW | 4 | 20 | 80
Hybrid | 2 | 20 | 40
Hybrid load 100kW | 2 | 20 | 40
Phase shifter (mechanical) | 2 | 20 | 40
Vector Modulator 1MWp | 2 | 100 | 200
Klystron Modulator 3 MW pk | 2 | 360 | 720
Total (per 4 cavity unit) |  |  | 2520
Advantages:
120 power sources instead of 240
Disadvantages:
Still need the full hardware set, with associated cost, development effort…
Additional power overhead with its extra cooling requirement

## Slide 23: Klystron Modulators for ESS and CERN
K. Rathsmann (ESS) - Fifth SPL Collaboration Meeting - November 2010.
ESS do tender for 1-3 systems – 2 Suppliers ?
50 Hz as option for SPL
ESS tendering is finished , offers just received.
order in 2011, for delivery October 2012
ESS Modulator for SM18
Pulse repetition rate: 20 Hz
Pulse length: 2.8 ms
Modulator Peak Power: 2.88 MW
Modulator average power: 200 kW
Higher rep rate possible with shorter pulse length
Klystron:
Pulse length: 2.5 ms
Peak power: 1.5 MW

## Slide 24: Tuner control and RF feedback simulations
Matlab & Simulink modeling
Various effects studied, for dual cavity configuration:
Cavity Voltage Amplitude and Phase
Forward and Reflected Power
Additional Power for Feedback Transients and Control
Effect of Lorentz Detuning on Feedback Power
Effect of Source Current Fluctuations
Mismatched Low-Power Case
Effects of Beam Relativistic Beta Factor on Cavity Voltage with beam-loading
Mathias Hernandez-Flanez

## Slide 25: LLRF Hardware for tuner characterization
four channels analog down conversion to IF
fRF = 704.4 MHz
fLO = (39/40) fRF = 686.79 MHz
fIF = fRF -fLO = 17.61 MHz
digital IQ demodulation with
sampling at 4xfIF = 70.44 MHz
CERN modified LHC hardware used in cavity tuning tests at Saclay
rate of (I,Q) samples: 17.61 MS/s
actual bandwidth lower and
depending on desired precision
Next steps  evolution to full LLRF system with RF feedback

## Slide 26: Cavity assembly and testing at CERN
    CERN SCRF Installations date from 1990s and LEP, with minor refurbishing for LHC cavities
    Major upgrade of facilities needed to handle modern high gradient cavities, in progress:
    New preparation, rinsing equipment, UP water
    New clean room
    Improved cryo, with 2K operation
    Modern diagnostics equipment

## Slide 27: Second sound diagnostics at CERN
Second sound study
SPL test cavity
OST manufacturing at CERN, thanks to Cornell support.
4.5 ± 0.5 cm
27
CERN (LEMO) vs Cornell (SMA)
Membrane sputtering
Similar tests also at Saclay
Kitty Liao Oct 2011

## Slide 28: SPL Activities
Description of the SPL and project scope
Cavities – design & fabrication
Cryomodule , He tank
Tuners, couplers, HOMCs
Power systems and pulsed modulators
Low Level RF
CERN SCRF infrastructure upgrade
Planning and ongoing work
Summary
Upcoming events & meetings…

## Slide 29: Planning of SPL R&D
Install & test klystron End Q4 2012
Cavity fabrication end 2012 Delayed by Nb procurement.
2011
2012
2013
Modulator from industry (ESS) Q3 2012
Couplers assembled and processed by end 2013
Vertical tests by end Q1 2013
2014
Cryostat with cavities by end 2013
RF tests mid 2014

## Slide 30: Ongoing SPL work in SM18
Preparation of HP RF
1.5 MW 704 MHz klystron in final stages of being ordered
Modulator installation preparation ongoing, including 400 V distribution line
RF power distribution system layout done, waveguides ordered.
One circulator and 3 Magic Tees, loads to be ordered by EoY
(allowing simultaneous powering of up to 4 cavities)
Interlocks & controls in preparation
First vertical test of an SPL cavity
Using a low b single cell from SACLAY
Cavity cooled down
He leak discovered
Tests under way to test & commission the measurement system
Will repair leak and continue..

## Slide 31: Summary (1)
Design of all major components is complete, excluding the cryomodule
Cryomodule review upcoming, design work to complete on He tanks and magnetic shielding.
Beginning of cryomodule construction (IN2P3) planned for end 2012
Cavity fabrication on schedule, test infrastructure being commissioned
Specification & construction of He tanks – ongoing (CEA)
Tuner design (SACLAY) validated in exhaustive tests, SACLAY will provide all 4 tuners – French in-kind contribution

## Slide 32: Summary (2)
RF High power equipment & klystron procurement on schedule
Specification & order of klystron modulator from industry being managed by ESS
Power couplers: Review done March 2011. Issue with DWT to resolve but well in hand
HOM Couplers – work still needed but not needed for initial cryomodule test
Upgrade of cryogenics and overall infrastructure in SM18 expected to be ready on time.
Test of single cell sc cavity now starting…
The studies have progressed well and we are well into preparing the hardware.
The project is ambitious, but is advancing well.

## Slide 33: Some Upcoming Events
SPL / ESS Specific:
  SPL Cryomodule Review : 4th Nov. 2011 CERN.
  7th ESS-SPL Collaboration meeting : 8-9 December, 2011 CERN.
  ESS RF Workshop 12-16 December, Uppsala.
Other Meetings at CERN
  LHC Crab cavity Workshop LHC CC11: 14-15 November
  LHC Collaboration Meeting: 16-18 November.
Thank you for your attention.

## Slide 34: SPL Activities
Spare Slides

## Slide 35: Low Power SPL LP-SPL
    LP-SPL: SC-linac (160 MeV ® 4 GeV) with ejection at intermediate energy
    Part of the upgrade of the CERN injectors, with PS2
    Designed to be upgradable to High Power for future facilities such as a neutrino factory => HP-SPL
Original Injectors Upgrade Scenario using LP-SPL
206 Cavities

## Slide 36: HP-SPL basic characteristics
 | Option 1 | Option 2
Energy (GeV) | 5 | 5
Beam power (MW) | 4 MW | 4 MW
Rep. frequency (Hz) | 50 | 50
Protons/pulse (x 1014) | 1.0 | 1.0
Av. Pulse current (mA) | 20 | 40
Beam pulse duration (ms) | 0.8 | 0.4
Beam characteristics of the main options
2 ´ beam current Þ 2 ´ nb. of klystrons etc .

## Slide 37: Resume - SPL R&D until 2016
H- source R & D (part of SLHC-PP)
Continued within the Linac4 project
Study of the optimum high power RF architecture for a high power SPL (part of SLHC-PP)
Terminated
Design, construction and test of superconducting RF cavities (704 MHz – 5 cells) in a cryomodule
Continued within EuCARD (CEA and CNRS) (2 cavities) + French in-kind + CERN resources (4 cavities)
Development of high power RF coupler, HOM damper and adaptation of tuner
Continued with French in-kind contribution + CERN resources + Uni Rostock
Upgrade of the SM18 test place [2 K cooling + pulsed RF source at 704 MHz (1.5 MW @ 50 Hz )]
Continued with ESS support (modulator) + CERN resources
Pulsed high power RF tests of contiguous cavities in a common cryostat
Continued with ESS participation + CRISP support + CERN resources
(Design, construction and test a high power klystron modulator: to resume in 2014)
(Design, construction and test of a prototype cryomodule equipped with 8 b=1 cavities: delayed)
Pending definition of CERN strategy following recommendations of the “European Strategy Group for Particle Physics” at the end of 2012.

## Slide 38: Cavity Parameters b= 0.65
Type of accelerating structure | b=0.65 | 5-cell standing wave
Accelerating mode |  | TM010, π-mode
Fundamental frequency ƒRF | [MHz] | 704.0
Nominal gradient Eacc | [MV/m] | 19
Quality factor Q0 at nominal gradient |  | 1010
Active length L | [m] | 0.692
Cell-to-cell coupling kcc | [%] | 1.45
Iris diameter (inner cells) | [mm] | 96
Iris diameter (outer cells adjacent to power coupler/tuner) | [mm] | 140/130
R/Q | [Ω] | 275
Epeak/Eacc |  | 2.63
Bpeak/Eacc | [mT/MV/m] | 5.12
Geometry factor | [Ω] | 197
Δƒ/ΔL | [kHz/mm] | 164
Lorentz-force detuning constant KLor | [Hz/(MV/m)2] | -1.6
Qext of input coupler (IB = 20 mA and f =15°) |  | 1.2 × 106
Cavity bandwidth f/Qext | [Hz] FWHM | 590
Fill time | [μs] | 270

## Slide 39: B=0.65 cavities and test cryostat
PLANNING
--> end of June ’11: call for tender preparation
29th Aug’11: deadline for receiving the offers
Mid-Sept ’11: choice of the manufacturer
Beginning of Oct’11: start of the fabrication
July ’12: cavity delivery w/o helium vessel  field flatness
Sept’12: helium vessel welding
Oct’12: cavity delivery
Nov ’12: cavity preparation (BCP + HPR) & assembly in clean room
Dec ’12 (for Christmas?): test in vertical cryostat
In 2013: cavity installation & test in CRYHOLAB
J. G.Olry et al., IPN Orsay, Joint ESS/SPL Meeting - SACLAY 2011

## Slide 40: Cavity Parameters b= 1
Type of accelerating structure | b=1 | 5-cell standing wave
Accelerating mode |  | TM010, π-mode
Fundamental frequency ƒRF | [MHz] | 704.4
Nominal gradient Eacc | [MV/m] | 25
Required field flatness DV/V | [%] | < ±2.5
Quality factor Q0 at nominal gradient |  | 1010
Active length L | [m] | 1.065
Cell-to-cell coupling kcc | [%] | 1.92
Iris diameter (inner cells) | [mm] | 130
Iris diameter (outer cells adjacent to power coupler/tuner) | [mm] | 129.2/140
R/Q | [Ω] | 566
Epeak/Eacc |  | 2.0
Bpeak/Eacc | [mT/MV/m] | 4.2
Geometry factor | [Ω] | 270
Required tuning range | [kHz] | ± 300
Δƒ/ΔL | [kHz/mm] | 164
Lorentz-force detuning constant KLor | [Hz/(MV/m)2] | 1
Qext of input coupler (IB = 20 mA and f =15°) |  | 1.2 × 106
Cavity bandwidth f/Qext | [Hz] FWHM | 590
Fill time | [μs] | 270
Number of HOM couplers |  | 2, if needed

## Slide 41: Mechanical parameters of the cavity
fixed ends
 | SPL | HIPPI
Nominal wall thickness [mm] | 3 | 4
Cavity stiffness Kcav [kN/mm] | 3.84 | 2.25
Tuning sensitivity Df/Dz [kHz/mm] | 164 | 295
KL with fixed ends [Hz/(MV/m)2] | -0.55 | -2.7
KL with free ends [Hz/(MV/m)2] | -5 | -20.3
Pressure sensitivity KP [Hz/mbar] (fixed ends) | 1.2 | 
The cavity will be equipped with a Saclay 4 tuner. The stiffness of the HIPPI - Saclay 4 tuner has been measured : Kext 35 kN/mm
The SPL cavity equipped with this tuner would present a detuning coefficient
|KL| = 1 Hz/(MV/m)2 ≈ |KL| estimated for Tesla
free ends
with tank and tuner
G. Devanz/J. Plouin 3rd SPL Meeting CERN 2009.
41

## Slide 42: Mechanical properties of cavities
Further design studies completed at CERN:
Maximum external pressure of 2 bars – fix-fix boundary condition (1)
Sensitivity to pressure fluctuation => one order of magnitude lower than the frequency bandwidth
Deformation for tuning
Natural vibration - First longit. mode at ~140 Hz (2)
Buckling (3)
=> Cavity thickness 3mm.
(1)
(2)
(3)

## Slide 43: Transfer function measurements
G. Devanz, CEA-Saclay, SPL 3rd coll. meeting
43

## Slide 44: Mechanical stiffening of the cavity
Cavity aimed to work in the pulsed mode  sensitivity to Lorentz detuning is critical
Lorentz detuning coefficient :
 Insertion of stiffening rings to reduce |KL|
Optimal position for Rring = 91 mm
around the optimum
The cones are an element of flexibility in the structure  they increase |KL|
Chart: Rrings [mm]
| 88.0 | 89.0 | 90.0 | 91.0 | 92.0 | 93.0 | 94.0
without cones | 0.4347 | 0.4313 | 0.4233 | 0.4223 | 0.422 | 0.4261 | 0.428
with cones | 0.561 | 0.559 | 0.5529 | 0.5528 | 0.5534 | 0.5585 | 0.561
Mechanical model of the cavity (CASTEM)

## Slide 45: Cavity HOMs : list
#freq r/Q beta_opt Qo Rs_nOhm
692.459406 15.495341 0.55 5.87048e+10 4.58
695.691165 40.295848 0.63 5.85048e+10 4.60
699.762722 86.977902 0.71 5.82537e+10 4.62
703.121236 173.038043 0.81 5.80475e+10 4.64
704.420268 565.499512 1.00 5.8134e+10 4.65
1293.187800 3.150182 0.66 4.06538e+10 9.75
1303.568690 7.969888 0.72 4.01921e+10 9.86
1317.445320 17.344152 0.79 3.95608e+10 10.02
1329.742220 59.154893 1.00 3.9004e+10 10.16
1335.734260 107.744313 0.98 3.8525e+10 10.23
1450.724780 0.831396 0.92 5.06898e+10 11.62
1460.366080 1.999197 0.89 5.03429e+10 11.74
1474.206000 2.839266 0.85 5.03023e+10 11.92
1488.535980 2.701775 0.80 5.09436e+10 12.10
1499.066360 2.342662 0.73 5.20134e+10 12.24
1843.272060 0.209069 0.95 3.35164e+10 17.22
1858.324840 0.596186 0.91 3.26306e+10 17.47
1881.326440 1.603429 0.98 3.28434e+10 17.84
1911.484360 1.329645 0.94 3.31308e+10 18.33
1948.248770 1.819111 1.00 3.35394e+10 18.95
2000.236410 2.451434 0.98 3.13642e+10 19.84
2039.865120 1.377179 0.78 3.70143e+10 20.53
2072.798390 3.019703 0.83 3.349e+10 21.12
2086.249930 5.689452 0.88 3.00335e+10 21.36
2089.642160 19.164504 1.00 2.90251e+10 21.42
2111.640680 10.636820 1.00 2.94648e+10 21.82
2119.767790 8.476595 1.00 2.65214e+10 21.97
2138.944200 1.075819 0.95 2.94674e+10 22.33
2175.157760 1.744804 0.91 3.24669e+10 23.00
2219.889020 4.482180 0.97 3.46431e+10 23.86
2262.192880 7.529522 1.00 3.6688e+10 24.68
2290.061390 0.330347 0.85 4.00758e+10 25.23
2464.607050 0.764947 0.95 2.5928e+10 28.82
2485.980300 1.514541 1.00 2.63647e+10 29.28
2512.576190 1.303253 0.96 2.84428e+10 29.86
2538.171130 8.505168 1.00 3.13472e+10 30.42
2559.022710 6.760250 0.99 3.40374e+10 30.88
2565.011240 2.855068 0.95 3.43392e+10 31.01
2639.339900 0.070686 0.90 2.41594e+10 32.69
2645.191100 0.071469 1.00 2.48068e+10 32.82
2650.937090 0.150348 1.00 2.47399e+10 32.96
2657.099030 0.275372 1.00 2.44513e+10 33.10
2721.471070 1.230228 0.96 2.23449e+10 34.60
2765.009700 0.249521 0.83 2.99369e+10 35.63
2781.989510 0.411752 0.87 2.61634e+10 36.04
2799.460470 0.229298 0.90 2.30615e+10 36.46
2809.660150 6.941103 1.00 2.09609e+10 36.71
List of monopole HOM calculated with Superfish between 0 and 3000 kHz
Axisymetric calculations
Operating frequency mode (p) : f0 = 704.4 MHz
No monopole HOM at 2f0
Mode at 2111.64 MHz very near 3f0
Cut-off frequencies for the mode TM010
Ø 80 mm : 2865 MHz
Ø 130 mm : 1763 MHz
Ø 140 mm : 1637 MHz
J. Plouin et al., 3rd SPL Meeting CERN 2009
45

## Slide 46: HOM Coupler design issues
A larger coupling port increases the transmission in the low frequency regime, but has little effect on a parasitic notch near 2.1 GHz.
This notch only appears on the HOM coupler opposite the power coupler, indicating that it depends on the geometry of the beam tube.
The parasitic notch frequency is close to three times the fundamental mode frequency and could therefore be harmful.
From the determination of the Qext values one concludes that around 2.1 GHz the damping is insufficient by far
However, power coupler may contribute to HOM damping
Futher design work needed…
Will not fit HOMCs to first cryomodule
Simulated transmission for the SPL cavity
Simulated Qext vs frequency for two HOMCs and power coupler port shorted

## Slide 47: SPL Power Coupler – Design
Technical Choices
Single RF window
Fixed coupling
Double Walled Tube on outer line
Clean room mounted together with the double walled tube horizontal in one operation
Mounted vertically below the cavity, with double walled tube partially supporting the cavity
With HV DC bias
Air cooled
RF Specs | 
f0 | 704.4 MHz
High Power SPL | 1000 kW pulsed Max. foreseen RF pulse length: 2.0 ms 50 Hz (20 ms) 100 kW average
Cavity design gradient | 19-25 MV/m
Qext of input coupler | 1.2 x 106 - HPSPL setting
Input line Ø | 100 / 43.5 mm = 50 Ω (from the cavity design)
Waveguides | WR 1150

## Slide 48: RF Power Sources - Comparisons
Magnetrons
Efficiency high, but can we get the power we need?
Phase locking needed, in development by CI
Response in a feedback loop? Bandwidth, group delay..
Cost, HV requirements, size ? Studied by A. Dexter CI, with JLAB
Parameter | Remark
Power | IOTs reaching klystrons - 600kW feasible..(TBC)
Efficiency | IOT 75% Klystron 55-60% (70% limit)
HV | IOTs lower ~ 40kV (oil-free ?)
Size | IOTs shorter
Cost | IOTs 30% lower
Lifetme | IOT Not known for high power, low power as klystrons
Drive | Klystron gain 35db, IOT 20dB – needs more drive
Characteristic | Klystron gain reduces at high drive, IOT saturates
Comparison of Klystrons & IOTs

## Slide 49: RF distribution schemes
Option 1) 1 klystron/4 cavities
Initially Preferred Layout for LP SPL – klystron economy
  Linear distribution, using less space consuming “planar” hybrids with individually adjusted coupling.
  Vector modulators for fast phase/amplitude field control
  Mech. phase shifters for cavity phasing or isolation
D. Valuch

## Slide 50: Layout with two cavities per klystron
Vector
modulator
Vector
modulator
Vector
SUM
Klystron
Feedback
Simulation program developed for LLRF simulations, user interface for 1, 2 and 4 cavities per klystron, M. Hernandez Flano
piezo tuner indispensible to avoid vector modulator.
X
X

## Slide 51: Amplitude and Phase variation for Dual Cavity Case (Without Piezo Feed-Forward)
K=-0.5
K=-1

## Slide 52: Phase variation for Dual Cavity Case (With Piezo Feed-Forward)
Cavity 1 (K=-1 )
Cavity 2 (K=-0.5 )

## Slide 53: Transit Time Factor variation
b=1 cavities, open loop simulation
Beamloading
Beamloading
Values obtained from SUPERFISH simulations by Marcel Schuh (CERN)
Weaker beam loading will result in a higher flat-top equilibrium and less phase detuning of the cavity for the same generator power.
Beta value taken from beam energy at beginning of SPL β=1 section.

## Slide 54: CERN SM18 SCRF test stand activities
    Ongoing work:
        LHC spare cavities, cryomodules & power couplers
        HIE Isolde cavities, cryomodules (later)
        CTF3 pets structures
        SPL cavities and cryomodules
        Nb studies λ/4 resonator (To cryo Lab)
        Linac 4 structure tests (short-term)
      Future
        Crab Cavity assembly & test
        Prototypes LHeC, LHC 800 MHz??

## Slide 55: Upgrade of SM18 Facilities
    Assembly area & clean rooms (J. Chambrillon)
      Upgrade of clean rooms, installation of access rooms (personal + material)
      Installation of high pressure rinsing equipment & ultra pure water supply
      Improved cleanliness, more working space..
      Preliminary design shown, still being studied
Outer working place
Class 10
Control room
Air supplier
Baldaquin 1
Class 100
Personnel access, with air shower Class 1 000
Class 100
Ionized air shower
Cleaning & rinsing room Class 100
HPWR system
UPW production
Baldaquin 2
Storage area Class 100