## Slide 1: Main Injector Single Bunch Tune Measurements
Duncan Scott
Main Injector Department

## Slide 2: Introduction
How will the Main Injector respond to higher intensity beams?
Currently slip stacking gives ~ 1011 particles per bunch
Project X has 3 1011 particles per bunch
What experiments can we do now to compare with simulations?
Can we generate beams with > 1011 particles?

## Slide 3: Space Charge Tune Shift
As intensity increases There are coherent and incoherent space charge tune shifts to consider
  Incoherent shifts difficult to measure,
These tune shifts induce blow-up and shorten lifetimes
Therefore we can measure lifetime vs bunch charge for 1, or a few, (5) bunches

## Slide 4: Exp. 1: Using beam from booster
Studied beam for 2.5 seconds @ 8 GeV in the MI
  Nominal tune Qh=26.47 Qv=25.43
  Chrom, -7
Fix Qh(v) change Qv(h)
Measure:
  Transmission (beam in / beam out )
  Tune (using bpms)
  Beamsize / Emittance (wirescanner)
  Injection dp/p

## Slide 5: Example Experiment 1 Data
As well as using existing console programmes we can analyse Wall Current Monitor data

## Slide 6: WCM Data
WCM data shows loss of intensity in bunches
  Each bunch loses similar intensity
Signal can be integrated to give bunch intensity loss with time
Can also measure bunch length

## Slide 7: Relate WCM signal to beam intensity
Integrate WCM signal and compare to IBEAM to get bunch intensities

## Slide 8: Transmission vs Tune

## Slide 9: Higher Intensity Bunches: Coalescing
Coalescing Can give higher intensity bunches
  Initial bunches in 53 MHz RF
  Rotate bunches in 2.5 MHz RF
  Recapture in 53 MHz RF

## Slide 10: Energy Spread at Rotation Determines Coalescing Efficiency

## Slide 11: Increase Coalescing Efficiency
Adiabatically Reduce 53 MHz RF voltage to damp the beam energy spread
With current RF can get to 25 kV
  ~70% efficient for 5 initial bunches
Simulation
Experiment

## Slide 12: Coalescing With Existing RF
With current RF, there must be 0.75 turns in 2.5 MHz bucket
Minimum time between RF commands too long for 0.25 rotations
Reduce
53 MHz RF
53 MHz off
2.5 MHz On
2.5 MHz Off
53 MHz On

## Slide 13: Coalescing With Existing RF
Example WCM data for 0.75 rotations of 5 bunches then recapture
Position in ring
Time
(turns)

## Slide 14: Bunch Length Increase
After coalescing the bucket is almost full
Therefore bunch length has increased
Example WCM signals
No Coalescing
With Coalescing

## Slide 15: Tune Measurement
When 53 MHz RF is snapped on change tune, Ping beam and take TBT BPM Reading
  TBT BPM data for approx. 100 vertical and 100 horizontal BPMS
  Small signal but by combining FFT of all BPMs tune can be measured
  No horizontal pinger so small skew quad time bump used to increase coupling for measurement
Then measure transmission from WCM data

## Slide 16: Transmission vs Tune

## Slide 17: Example Comparison
Similar transmission with factor of 3.2 increase in intensity
However Bunch length increased by factor 3.4
172 109 Coalesced
54 109 Uncoalesced

## Slide 18: Increasing Beam Intensity
Reducing the 53 MHz voltage below 25 kV should increase efficiency and bunch intensity
Could try coalescing 7 bunches?
53 MHz voltage and initial bunch intensity required to give 3 1010 particles
5 bunch coalescing
7 bunch coalescing
11 Booster Turns

## Slide 19: Increasing Beam Intensity
Bunch Stretching at unstable fixed point
Requires shorter time between RF commands

## Slide 20: Summary & Further Work
One way for the MI to prepare for Project X is to look at space charge tune shifts for single (few) bunches
Initial Experiments have been carried out
  Measure transmission vs tune for different bunch intensities and bunch lengths
  Coalescing currently gives ~1.7 1011 particles
  Clear differences seen -> Space charge tune shifts
Further Study
  Compare with simulations
  By improving RF coalescing may be able to get 3 1011 particles
  What is for Project X and can we recreate it?
Other ideas…