## Slide 1: PXIE Facility and Layout
Rich Stanek
Session 5 / WG1
October 26th, 2011

## Slide 2: Background
Project X will form the backbone of Fermilab operation in the future
Risks for Project X include generating beam parameters in the front end, chopping, and controlling halo, emittance growth, beam losses…
  Mitigate these risks by building first 30 MeV of the Project X design
Idea for PXIE is just a few months old
Decided on a really good acronym
  Project X Injector Experiment
Designs are in progress but still have many details to work out
  Need to start looking at integration issues
  Want to form some level of consistency across the various components

## Slide 3: PXIE Location
Decision to site PXIE at the CryoModule Test Facility (CMTF) building driven by
  Availability of space and cryogenics (new superfluid cryogenic plant)
  Looked at several options, this was the best choice
NML, CMTF and PXIE form an integrated complex of facilities targeting future accelerator R&D
  NML  ~1 GeV pulsed e- linac for ILC RF Unit tests and AARD activities
  CMTF  two CM test stands (multi-frequency) serviced by 200w @1.8K superfluid cryogenic system and ~220 L/hr. helium liquefier, RF power test area, clean room, tech area…
  PXIE  ~30 MeV CW H- linac for Project X R&D

## Slide 4: Schedule/Cost Estimate
Have some very high level goals (proposed by Project Scientists)
  First beam through PXIE October 2015
    This has generated a series of additional intermediate milestones for component design and construction
  Need to validate all of these dates
Working on a “bottoms up” schedule
  Take into account: scope of work, personnel availability, commitments to other projects, other priorities, and funding
  Must have a credible schedule to set proper expectations
Cost estimate starting point is the current Project X estimate
  Modify by
    Changes in the assumptions
    Current technical design, facilities and resources
  Need to have this cost estimate in order to accurately plan

## Slide 5: Engineering Processes
Fermilab has recently established a more defined engineering process guided by our Engineering Manual
  Graded approach based on engineering judgment and risk assessment
Documentation of requirements, risks, analysis, approvals…
  Functional Requirements Specification (FRS)
  Technical Requirements Specification (TRS)
  Formal Design Reviews
  Quantification of Risk
  Procedures
  More complete engineering and QC documentation
  Central repository for engineering information (including 3D CAD models)
    EDMS (Teamcenter)
Collaborators on PXIE will have access to Teamcenter data base
  Unfortunately not available until March/April 2012 timeframe
    Forces us to look at interim solutions
    Currently using Doc DB, website links, file servers…

## Slide 6: PXIE Facility Planning
What we are building is a general purpose Accelerator Test Area
  First tenant will be PXIE
Working on the details of overall facility construction
  Size of concrete pad
  Layout of tunnel walls and support equipment area
  Building exterior
  Requirement for crane coverage
  Power requirements
  Cryogenic loads and performance specifications
  Required radiation shielding
    How to deal with penetrations, labyrinths…
  Dump requirements

## Slide 7: Accelerator Test Area Initial Concepts
Looked at variety of options for connecting Test Area to CMTF building
  Minimize cost (use existing shield blocks) but provide reasonable space in order to test components
  Factor in initial cost and ease of modification/maintenance

## Slide 8: NML, CMTF and PXIE
High bay area:
NML ~ 15,000 sq. ft.
CMTF ~ 14,000 sq. ft.
PXIE ~ 8,900 sq. ft.

## Slide 9: Accelerator Test Area (PXIE)

## Slide 10: SRF Accelerator Test Area Complex Layout
Jerry Leibfritz working with FESS on building layout

## Slide 11: SRF Accelerator Test Area Complex Layout (2)

## Slide 12: Component Layout
Jim Kerby working on detailed component layout using latest optics
  Will be an iterative process
  Gathering information on size of components and interface dimensions
  Question of how close PXIE design should be to Project X
    Should it be one for one to test critical components?
    Do we need to test installation procedures and alignment schemes?

## Slide 13: Key Parameters/Issues
Physical Layout
  Concrete pad 178’ (L) x 50’ (W)  close to maximum size for that area
  Tunnel internal cross section 15’ (W) x 16’ (H)  compatible to Project X
  Beam height = 4.265’ (1.3 m)
Cryogenics (A. Klebaner)
  Capacity vs. load at operating temperature needs to be examined
  Need to understand stability requirements vs. operation modes
    Turn on off test stands and PXIE is staged so real data will be available
AC Power
  Should have enough wall plug power but if not, option to add transformer
RF Power (R. Pasquinelli)
  Substantial space required for power sources, racks, waveguides, coax…
Controls
  Global controls will utilize standard FNAL control system (ACNET)
  LLRF control is an area that needs additional communication
Instrumentation (V. Scarpine, M. Wendt)
  One of the key R&D features that will be explored is validating instrumentation
    Including chopper extinction measurements

## Slide 14: PXIE and SRF Program
PXIE’s SRF components (HWR and SSR1) are fully consistent with and integrated into FNAL’s overall SRF Program
  SSR1 has been ongoing (Roark/Niowave)
  Recent switch from SSR0 to HWR means ANL has a larger role
  SRF organizations and responsibilities are already well established
  FRS drafts exist and TRS documents are being written
  Infrastructure will be modified to accommodate new frequency
  Priorities will be adjusted to reflect relative critical nature of work
Non-SRF work for the rest of PXIE will be integrated with Project X RD&D Program
  Clearly PXIE is a high priority in that it demonstrates several key beam components/parameters and reduces risk for Project X

## Slide 15: Summary
Just beginning the process of facility planning
Beamline layout  in progress
Civil construction planning  in progress
Component specifications  being developed
  Design work  in progress
    Source & RFQ  LBNL
    HWR  ANL
    SSR1  FNAL/India
    Magnets  FNAL
    RF Sources  FNAL/SLAC/India
    Cryogenics  FNAL
    Instrumentation  FNAL/SLAC/SNS/India
Working on “bottoms up” schedule and cost estimate
PXIE will serve as a valuable R&D tool for Project X