## Slide 1
A.Valishev, A.Romanov, J.Jarvis, B.Cathey, J.Santucci, V.Lebedev, N.Eddy, K.Carlson
IOTA/FAST Meeting
19 March 2021
IOTA OSC Beam Commissioning - Update

## Slide 2: Tasks / Notes
Beam lifetime up to 10 min
Orbit correction / centering
  Presently corrected to within 1 mm of quadrupole centers
  L/R asymmetry of main dipole correctors not well understood
Aperture study
  In progress, vertical is 70-80% of design, possibly restricted in horizontal
  RF frequency scans show low range +300 Hz
Optics correction (LOCO)
  Few iterations, some focusing errors identified
Coupling correction
  Down to 0.02 tune split, limited by tune measurement
  Some skew correctors run at 1A already
Chromaticity correction
  Not started, limited by tune measurement

## Slide 3: Problems
Fast decoherence of kicked-beam dipole oscillations
  Limits tune measurement capabilities
  Origin not understood
Longitudinal beam instability
  High-harmonic RF helped, new amplifier will extend range
Tune measurement
  Sweeping SA + amp
Chromatic correction
  Difficult in the OSC lattice
  +300 Hz RF corresponds to p/p=2.4E-3
  At U=50V, the bucket is 4.3E-3
  If energy acceptance is limited, will impact lifetime

## Slide 4: OSC Lattice

## Slide 5: OSC Lattice Chromaticity

## Slide 6: Tune Chromaticity – OptiM Computation (for nomnal OSC lattice)