## Slide 1
DUNE Cryogenic Optical Links
Dave Christian (FNAL)
Greg Deuerling (FNAL)
Jason Greskoviak (FNAL)
Jason Keyzer (SMU)
Andy Liu (SMU)
Alan Prosser (FNAL)
Jingbo Ye (SMU)
March 31, 2021

## Slide 2
Introduction
Tx Channels:
We have ordered some laser drivers for LN2 testing (AD, TI, MAXIM).
TOSAs have been found and some received with fiber pigtails.
Rx Channels:
Some limiting amplifiers are also part of vendor portfolios so we will see about ordering
some of these for Rx channels.
Have yet to search and order ROSAs (one supplier, Vitex, has been queried).
Other:
We have obtained guidance on discrete component part selection from BNL. No word
similar information from JPL so we are going ahead with designs with our best information.
Awaiting NDA from one supplier (Semtech) of multiple components. FNAL and Semtech
legal teams are in communication.
Greg Deuerling is developing the first test PCB for the ADN2526 laser driver.

## Slide 3
Power Supply
Laser Diode
62 Ohms
62 Ohms
SMF
Pigtail
Handheld Power
Meter
Newport 1310 nm Fabry-Perot Laser Diode (pigtailed)
CW Test Configuration
FC terminated SMF
Laser Diode
+
-

## Slide 4
Newport 1310 nm Fabry-Perot Laser Diode (pigtailed)
CW Test Configuration

## Slide 5
Chart: 
| 5 | 7 | 9 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 25
Pdiode(uW) | 0.79433 | 1.2589 | 5.0119 | 100 | 208.9296 | 354.8134 | 489.7788 | 660.6934 | 794.3282 | 944.0609 | 1073.9894 | 1183.0416
Ith ~= 10 mA
Slope Efficiency ~= 72 microwatts/milliamp
Newport 1310 nm Fabry-Perot Laser Diode (pigtailed)
Room Temperature
Next…
Repeat this measurement
at PAB in LN2
Diode Current (mA)
Optical Diode Power
(mW)

## Slide 6
Input
Electrical
Pair
Power Header
Configuration/
Monitoring Header
50 Ohm differential
100
Ohm
differential
DSA8200
Ch7
Ch8
Dewar (bottom)
Dewar (top)
50 Ohm coax
50 Ohm coax
35 ohms
35 ohms
75
ohms
DC Block
Laser Driver Electrical Eval Board/LN2 Test Setup
Data+
Data-
Laser
Driver
BSA286CL
50
Ohm
coax

## Slide 7
Laser Driver Electrical Eval Board/LN2 Test Setup
Engineer: Greg Deuerling
Concept
Layout

## Slide 8
Laser Driver Electrical Eval Board/LN2 Test Setup – Dual Footprint
50 Ohm differential
35 ohms
35 ohms
75
ohms
Laser
Driver
Through holes for laser
diode anode, cathode

## Slide 9
Laser Driver Electrical Eval Board/LN2 Test Setup – electrical configuration
50 Ohm differential
35 ohms
35 ohms
75
ohms
Laser
Driver

## Slide 10
Laser Driver Electrical Eval Board/LN2 Test Setup – optical configuration
50 Ohm differential
Laser
Driver
Through holes for laser
diode anode, cathode

## Slide 11
Extra Slides

## Slide 12
Will Route Cross Point Adjust and Automatic Laser Shutdown to header.
Simple Evaluation Board for Analog Devices ADN2526 Laser Diode Driver
Electrical Tests
Vibias_adj
Vimod_adj
SMA pair
SMA pair
All components will be
tested in LN2.
Power, configuration,
electrical excitation, and
electrical diagnostics
will be outside the dewar
SMA
pair
Coax
cable
DC
Block

## Slide 13
Will Route Cross Point Adjust and Automatic Laser Shutdown to header.
Simple Evaluation Board for Analog Devices ADN2526 Laser Diode Driver
Optical Tests
Vibias_adj
Vimod_adj
SMA pair
SMA pair
SMA
Pair (disconnected from circuit)
Optical signal
(to eye, jitter
measurements)*
*After L-I tests of pigtailed laser diode
have demonstrated suitability in the cold.
All components will be
tested in LN2.
Power, configuration,
electrical excitation, and
optical diagnostics
will be outside the dewar